| Pseudo CHANGE REQUEST |
| --- |
| 124 008 | Version | 11.8.0 | CR | P-CR | rev | - |
| CR Title: | eCall over IMS (PS based services (UTRAN)) |
| Source: | STF 456 |
| Work Item Ref: | Migration of eCall transport | Date: | 06/01/2014 |
| Category: | B | Release: | Rel-11 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature) C (functional modification of feature) D (editorial modification) |
| Reason for change: | ETSI STF456, partly funded by the European Commission, is investigating migration of eCall transport over PS domain/EPS. The Release-8 eCall covers CS only, and therefore excludes PS/IMS emergency services. ETSI MSG TC agreed the TR103140 that studies the Migration of eCall transport. Proposed and recommended solutions are included in this TR. The solution considered for eCall over IMS is in line with the IMS emergency call/services. |
| Summary of change: | eCall over IMS is applicable to UTRAN Iu mode only (and E-UTRAN). The IMS eCall only MS (as determined by information configured in the USIM), while camping on a suitable cell that preferably supports “IMS eCall” indicated by the broadcasted system Information (that still need to be defined in RAN2), shall not register to the PLMN, and shall enter the newly defined state GMM-DEREGISTERED.eCALL INACTIVE. In this substate the eCall only MS does not perform GMM mobility management procedures apart from registration to the PLMN, by performing the GMM attach for emergency bearer services procedure upon triggering IMS eCall (eCall-manual or eCall-automatic). Also in the substae DEREGISTERED.eCALL INACTIVE, an IMS eCall only MS may register to the PLMN upon triggering non-emergency service (IMS eCall test and eCall reconfiguration), by performing the normal GMM attach procedure. After the termination of an IMS eCall emergency service or IMS eCall non emergency service, the timer Txx or timer Txy is triggered respectively for IMS eCall service (emergency or non-emergency). The value for each of these timers is set by the operator and has the max of 12 hours, where during this time the eCall only MS is in PMM-Idle state. Upon expiration of these timers the eCall only MS performs the GPRS eCall inactivity procedure and enters the substate DEREGISTERED.eCALL INACTIVE. Upon eCall only MS reconfiguration, the MS can receive normal services. Changes are summarised as: - Adding definition for “IMS eCall”. - Adding GPRS eCall inactivity procedure to GMM specific procedures in the MS. - Adding a new MS state; GMM-DEREGISTERED.eCALL INACTIVE, and describing how this new substate interworks with other MS subsates. Also describing eCall only MS behaviour in GMM-DEREGISTRED substates. - Providing a new GPRS update status for eCall in UTRAN-PS (GU4) - Adding clarification in 4.2.4.1.1 that on power on, the IMS eCall only MS has its timers (T33XX and T33XY) expired. This makes the eCall only MS move to the GMM-DEREGISTERED.eCALL INACTIVE substate as clarified in the CR. - indicating eCall conditions for the GPRS detach procedure and GPRS Routing area updating procedure. For the attach procedure, the eCall only MS shall perform GPRS attach for emergency bearer services in case of eCall emergency services and a normal GPRS attach for the non-emergency services. - Describing in a new subcaluse, the GPRS eCall inactivity procedure. - Introducing 2 new timers (T33XX and T33XY) that are triggered when the MS leaves the PMM-Connected mode (after an emergency session or a test/reconfiguration session) and enters PMM-IDLE mode. On expiration of these timers the MS enters GPRS eCall Inactive state. |
| Clauses affected: | 2.1.2, 4.1.1.1, 4.1.3.1.2.x (new), 4.1.3.2, 4.2.4, 4.2.4.1.1, 4.2.4.2.1, 4.2.4.2.2, 4.2.4.2.3, 4.2.4.2.6, 4.2.4.2.7, 4.2.4.2.8, 4.2.4.2.x (new), 4.2.4.3, 4.2.5.1.6, 4.2.5.1.8, 4.7.3, 4.7.4.0, 4.7.5, 4.7.x (new),11.2.2 |
| Other deliverables affected: |  |
| Other comments: |  |

### 2.1.2	Vocabulary

For the purposes of the present document, the following terms and definitions apply:

-	A GSM security context is established and stored in the MS and the network as a result of a successful execution of a GSM authentication challenge. The GSM security context for the CS domain consists of the GSM ciphering key and the ciphering key sequence number. The GSM security context for the PS domain consists of the GPRS GSM ciphering key and the GPRS ciphering key sequence number.

-	A UMTS security context is established and stored in the MS and the network as a result of a successful execution of a UMTS authentication challenge. The UMTS security context for the CS domain consists of the UMTS ciphering key, the UMTS integrity key, the GSM ciphering key, the ciphering key sequence number and the GSM Kc128 (if an A5 ciphering algorithm that requires a 128-bit ciphering key is in use). The UMTS security context for the PS domain consists of the GPRS UMTS ciphering key, the GPRS UMTS integrity key, the GPRS GSM ciphering key, the GPRS ciphering key sequence number and the GPRS GSM Kc128 (if a GEA ciphering algorithm that requires a 128-bit ciphering key is in use).

-	An MS is attached for emergency bearer services if it has successfully completed an attach for emergency bearer services or if it has only a PDN connection for emergency bearer services established.

-	idle mode: In this mode, the mobile station is not allocated any dedicated channel; it listens to the CCCH and the BCCH;

-	group receive mode: (only applicable for mobile stations supporting VGCS listening or VBS listening) In this mode, the mobile station is not allocated a dedicated channel with the network; it listens to the downlink of a voice broadcast channel or voice group call channel allocated to the cell. Occasionally, the mobile station has to listen to the BCCH of the serving cell as defined in 3GPP TS 43.022 [82] and 3GPP TS 45.008 [34];

-	dedicated mode: In this mode, the mobile station is allocated at least two dedicated channels, only one of them being a SACCH;

-	EAB: Extended Access Barring, see 3GPP TS 22.011 [138].

-	group transmit mode: (only applicable for mobile stations supporting VGCS talking) In this mode, one mobile station of a voice group call is allocated two dedicated channels, one of them being a SACCH. These channels can be allocated to one mobile station at a time but to different mobile stations during the voice group call;

-	packet idle mode: (only applicable for mobile stations supporting GPRS) In this mode, mobile station is not allocated any radio resource on a packet data physical channel; it listens to the BCCH and the CCCH, see 3GPP TS 44.060 [76].

-	packet transfer mode: (only applicable for mobile stations supporting GPRS) In this mode, the mobile station is allocated radio resource on one or more packet data physical channels for the transfer of LLC PDUs.

-	main DCCH: In Dedicated mode and group transmit mode, only two channels are used as DCCH, one being a SACCH, the other being a SDCCH or a FACCH; the SDCCH or FACCH is called here "the main DCCH";

-	A channel is activated if it can be used for transmission, in particular for signalling, at least with UI frames. On the SACCH, whenever activated, it must be ensured that a contiguous stream of layer 2 frames is sent;

-	A TCH is connected if circuit mode user data can be transferred. A TCH cannot be connected if it is not activated. A TCH which is activated but not connected is used only for signalling, i.e. as a DCCH;

-	The data link of SAPI 0 on the main DCCH is called the main signalling link. Any message specified to be sent on the main signalling link is sent in acknowledged mode except when otherwise specified;

-	The term "to establish" a link is a short form for "to establish the multiframe mode" on that data link. It is possible to send UI frames on a data link even if it is not established as soon as the corresponding channel is activated. Except when otherwise indicated, a data link layer establishment is done without an information field.

-	"channel set" is used to identify TCHs that carry related user information flows, e.g., in a multislot configuration used to support circuit switched connection(s), which therefore need to be handled together.

-	A temporary block flow (TBF) is a physical connection used by the two RR peer entities to support the uni-directional transfer of LLC PDUs on packet data physical channels, see 3GPP TS 44.060 [76].

-	RLC/MAC block: A RLC/MAC block is the protocol data unit exchanged between RLC/MAC entities, see 3GPP TS 44.060 [76].

-	A GMM context is established when a GPRS attach procedure is successfully completed.

-	Network operation mode

The network operation modes I and II are defined in 3GPP TS 23.060 [74].

The network operation mode shall be indicated as system information. For proper operation, the network operation mode should be the same in each cell of one routing area.

-	GAN mode: See 3GPP TS 43.318 [75a].

-	GPRS MS operation mode

The three different GPRS MS operation modes A, B, and C are defined in 3GPP TS 23.060 [74].

-	RR connection: A RR connection is a dedicated physical circuit switched domain connection used by the two RR or RRC peer entities to support the upper layers' exchange of information flows.

-	PS signalling connection is a peer to peer Iu mode connection between MS and CN packet domain node.

-	Inter-System change is a change of an MS from A/Gb mode to Iu mode of operation or vice versa. or from S1 mode to A/Gb mode or Iu mode of operation.

-	GPRS: Packet Services for systems which operate the Gb or Iu-PS interfaces.

-	GSM ciphering key: A 64-bit CS GSM ciphering key

-	GSM Kc128: A 128-bit CS GSM ciphering key

-	GPRS GSM ciphering key: A 64-bit PS GSM ciphering key

-	GPRS GSM Kc128: A 128-bit PS GSM ciphering key

-	The label (A/Gb mode only) indicates this section or paragraph applies only to a system which operates in A/Gb mode, i.e. with a functional division that is in accordance with the use of an A or a Gb interface between the radio access network and the core network. For multi system case this is determined by the current serving radio access network.

-	The label (Iu mode only) indicates this section or paragraph applies only to a system which operates in Iu mode. The Iu mode includes UTRAN and GERAN Iu modes, i.e. with a functional division that is in accordance with the use of an Iu-CS or Iu-PS interface between the radio access network and the core network. For multi system case this is determined by the current serving radio access network.

-	In A/Gb mode,... Indicates this paragraph applies only to a system which operates in A/Gb mode. For multi system case this is determined by the current serving radio access network.

-	In Iu mode,... Indicates this paragraph applies only to a system which operates in Iu mode. The Iu mode includes both UTRAN Iu mode and GERAN Iu mode. For multi system case this is determined by the current serving radio access network.

-	In A/Gb mode and GERAN Iu mode,... Indicates this paragraph applies only to a system which operates in A/Gb mode or GERAN Iu mode. For multi system case this is determined by the current serving radio access network.

-	In UTRAN Iu mode,... Indicates this paragraph applies only to a system which operates in UTRAN Iu mode. For multi system case this is determined by the current serving radio access network.

-	In a shared network,... Indicates this paragraph applies only to a shared network. For the definition of shared network see 3GPP TS 23.122 [14].

NOTE:	A shared network is applicable to GERAN and UTRAN, however, according to this definition, a multi-operator core network (MOCN) with common GERAN is not considered a shared network in 3GPP TS 23.122 [14] and in the present specification.

-	Multi-Operator Core Network (MOCN) with common GERAN: a network in which different core network operators are connected to a shared GERAN broadcasting only a single, common PLMN identity.

-	Chosen PLMN: The same as selected PLMN as specified in 3GPP TS 23.122 [14].

-	A default PDP context is a PDP context activated by the PDP context activation procedure that establishes a PDN connection. The default PDP context remains active during the lifetime of the PDN connection.

-	A PDP context for emergency bearer services is a default PDP context which was activated with request type "emergency", or any secondary PDP contexts associated to this default PDP context.

-	Non-emergency PDP context: any PDP context which is not a PDP context for emergency bearer services.

-	SIM, Subscriber Identity Module (see 3GPP TS 42.017 [7]).

-	USIM, Universal Subscriber Identity Module (see 3GPP TS 21.111 [101]).

-	MS, Mobile Station. The present document makes no distinction between MS and UE.

-	MS configured for dual priority: An MS which provides dual priority support is configured for NAS signalling low priority and also configured to override the NAS signalling low priority indicator (see 3GPP TS 24.368 [135], 3GPP TS 31.102 [112]).

-	Cell Notification is an (optimised) variant of the Cell Update Procedure which uses the LLC NULL frame for cell change notification which does not trigger the restart of the READY timer

-	DTM: dual transfer mode, see 3GPP TS 44.018 [84] and 3GPP TS 43.055 [87]

-	The term "eCall only" applies to a mobile station which is in the eCall only mode, as described in 3GPP TS 22.101 [8].

-	"removal of eCall only restriction" means that all the limitations as described in 3GPP TS 22.101 [8] for the eCall only mode do not apply any more.

-	The term "IMS eCall" applies to a mobile station which is operates in eCall over IMS, as described in 3GPP TS 22.101 [8].

NOTE:	for eCall over packet switched; there can be other packet based solutions than IMS eCall.

-	"SMS-only service": A subset of services which includes only Short Message Service. The MS can request "SMS-only service" in order to obtain SMS.

-	Access domain selection: The process to select whether the CS domain or the IMS/IP-CAN is used to transmit the call control signalling between MS and core network. Definition derived from 3GPP TS 23.221 [131].

-	APN based congestion control: Congestion control in session management where the network can reject session management requests from MSs or deactivate PDP contexts when the associated APN is congested.

-	NAS level mobility management congestion control: Congestion control mechanism in the network  in mobility management. "NAS level mobility management congestion control" consists of "subscribed APN based congestion control" and "general NAS level mobility management congestion control".

-	General NAS level mobility management congestion control: The type of congestion control that is applied at a general overload or congestion situation in the network, e.g. lack of processing resources.

-	Subscribed APN based congestion control: Congestion control in mobility management where the network can reject attach requests from MSs with a certain APN in the subscription.

-	Mapped P-TMSI: a P-TMSI which is mapped from a GUTI previously allocated to the MS by an MME. Mapping rules are defined in 3GPP TS 23.003 [10]. Definition derived from 3GPP TS 23.401 [122].

-	Native P-TMSI: a P-TMSI previously allocated by an SGSN. Definition derived from 3GPP TS 23.401 [122].

-	Valid LAI: a LAI that is not deleted LAI.

-	EMM Combined UE Waiting Flag: See 3GPP TS 29.018 [149].

For the purposes of the present document, the following terms and definitions given in 3GPP TS 23.401 [122], subclause 3.2, apply:

Globally Unique MME Identifier (GUMMEI)

Globally Unique Temporary Identity (GUTI)

Idle Mode Signalling Reduction (ISR)

M-Temporary Mobile Subscriber Identity (M-TMSI)

PDN connection

Tracking Area Identity (TAI)

Temporary Identity used in Next update (TIN)

For the purposes of the present document, the following terms and definitions given in 3GPP TS 24.301 [120] apply:

CSG cell

CSG ID

CSG selection

LIPA PDN connection

PDN connection for emergency bearer services

S1 mode

For the purposes of the present document, the following terms and definitions given in 3GPP TS 23.272 [133] apply:

CS fallback

SMS over SGs

For the purposes of the present document, the following terms and definitions given in 3GPP TS 33.401 [123] apply:

Current EPS security context

Mapped security context

eKSI

CK' and IK'

NAS downlink COUNT

NAS uplink COUNT

For the purposes of the present document, the following terms and definitions given in 3GPP TS 23.251 [109] apply:

Multi-Operator Core Network (MOCN)

Network Sharing non-supporting MS: see non-supporting UE.

Network Sharing supporting MS: see supporting UE.

For the purposes of the present document, the following terms and definitions given in 3GPP TS 23.122 [14] apply:

Country

Suitable Cell

For the purposes of the present document, the following terms and definitions given in 3GPP TS 23.216 [8] apply:

SRVCC

vSRVCC

CS to PS SRVCC

For the purposes of the present document, the following terms and definitions given in 3GPP TS 23.251 [109] and 3GPP TS 44.018 [84] apply:

Common PLMN

For the purposes of the present document, the following terms and definitions given in 3GPP TS 44.018 [84] apply:

Additional PLMN

Network sharing

**************** ****************Next Change**********************

### 4.1.1	MM and GMM procedures

#### 4.1.1.1	Types of MM and GMM procedures

Depending on how they can be initiated, three types of MM procedures can be distinguished:

1)	MM common procedures:

A MM common procedure can always be initiated whilst a RR connection exists. The procedures belonging to this type are:

Initiated by the network:

-	TMSI reallocation procedure;

-	authentication procedure;

-	identification procedure;

-	MM information procedure;

-	abort procedure.

However, abort procedure is used only if an MM connection is being established or has already been established i.e. not during MM specific procedures or during IMSI detach procedure, see subclause 4.3.5.

Initiated by the mobile station:

-	IMSI detach procedure (with the exceptions specified in subclause 4.3.4).

2)	MM specific procedures:

A MM specific procedure can only be initiated if no other MM specific procedure is running or no MM connection exists. The procedures belonging to this type are:

-	normal location updating procedure;

-	periodic updating procedure;

-	IMSI attach procedure; and

-	eCall inactivity procedure.

3)	MM connection management procedures:

These procedures are used to establish, maintain and release a MM connection between the mobile station and the network, over which an entity of the upper CM layer can exchange information with its peer. A MM connection establishment can only be performed if no MM specific procedure is running. More than one MM connection may be active at the same time.

Depending on how they can be initiated, three types of GMM procedures can be distinguished:

1)	GMM common procedures:

In Iu mode, a GMM common procedure can always be initiated whilst a PS signalling connection exists.

The procedures belonging to this type are:

Initiated by the network when a GMM context has been established:

-	P-TMSI (re-) allocation;

-	GPRS authentication and ciphering;

-	GPRS identification;

-	GPRS information.

2)	GMM specific procedures:

Initiated by the network and used to detach the IMSI in the network for GPRS services and/or non-GPRS services and to release a GMM context:

-	GPRS detach.

Initiated by the MS and used to attach or detach the IMSI in the network for GPRS services and/or non-GPRS services and to establish or release a GMM context:

-	GPRS attach and combined GPRS attach;

-	GPRS detach and combined GPRS detach.

Initiated by the MS when a GMM context has been established:

-	normal routing area updating and combined routing area updating;

-	periodic routing area updating.

In UMTS Iu mode only, initiated by the MS if no other GMM specific procedure is ongoing or no RR connection exists:

-	GPRS eCall inactivity procedure.

3)	GMM connection management procedures (Iu mode only):

Initiated by the MS and used to establish a secure connection to the network and/or to request the resource reservation for sending data:

Service Request.

The Service Request procedure can only be initiated if no MS initiated GMM specific procedure is ongoing.

**************** ****************Next Change**********************

###### 4.1.3.1.2.x	GMM-DEREGISTERED.eCALL INACTIVE (UTRAN Iu mode only)

Valid subscriber data is available, GPRS update status is GU4, and a suitable cell is selected (that should support "IMS eCall"). Only emergency bearer services and test/reconfiguration sessions can be initiated by the mobile station. This state is applicable only to an eCall only mobile station (as determined by information configured in USIM). This state is entered by the mobile station in order to avoid GMM activity and GMM signalling in the absence of an emergency bearer service or test/reconfiguration session. This state is ended when an emergency bearer services or test/reconfiguration sessions is initiated by the mobile station and the MS enters the new state PMM-CONNECTED, see 3GPP TS 22.101[8] and 3GPP TS 23.060 [74].

**************** ****************Next Change**********************

#### 4.1.3.2	GPRS update status

In addition to the GMM sublayer states described so far, a GPRS update status exists.

The GPRS update status pertains to a specific subscriber embodied by a SIM/USIM. This status is defined even when the subscriber is not activated (SIM/USIM removed or connected to a switched off ME). It is stored in a non volatile memory in the SIM/USIM. The GPRS update status is changed only after execution of a GPRS attach, combined GPRS attach, network initiated GPRS detach, authentication, service request, paging for GPRS services using IMSI,  routing area updating or combined routing area updating procedure.

GU1: UPDATED

The last GPRS attach or routing area updating attempt was successful (correct procedure outcome, and the answer was accepted by the network). The SIM/USIM contains the RAI of the routing area (RA) to which the subscriber was attached, and possibly a valid P-TMSI, GPRS GSM ciphering key, GPRS UMTS ciphering key, GPRS UMTS integrity key and GPRS ciphering key sequence number. Furthermore, if the ME supports any GEA ciphering algorithm that requires a 128-bit ciphering key and a USIM is in use, then the ME may contain a valid GPRS GSM Kc128.

GU2: NOT UPDATED

The last GPRS attach or routing area updating attempt failed procedurally, i.e. no response was received from the network. This includes the cases of failures or congestion inside the network.

In this case, the SIM/USIM can contain the RAI of the routing area (RA) to which the subscriber was attached, and possibly also a valid P-TMSI, GPRS GSM ciphering key, GPRS UMTS ciphering key, GPRS UMTS integrity key and GPRS ciphering key sequence number. For compatibility reasons, all these fields shall be set to the "deleted" value if the RAI is deleted. However, the presence of other values shall not be considered an error by the MS. Furthermore, if the ME supports any GEA ciphering algorithm that requires a 128-bit ciphering key and a USIM is in use, then the ME shall delete the GPRS GSM Kc128 stored if the RAI is deleted.

GU3: ROAMING NOT ALLOWED

The last GPRS attach or routing area updating attempt was correctly performed, but the answer from the network was negative (because of roaming or subscription restrictions).

In this case, the SIM/USIM can contain the RAI of the routing area (RA) to which the subscriber was attached, and possibly also a valid P-TMSI, GPRS GSM ciphering key, GPRS UMTS ciphering key, GPRS UMTS integrity key or GPRS ciphering key sequence number. For compatibility reasons, all these fields shall be set to the value "deleted" if the RAI is deleted. However, the presence of other values shall not be considered an error by the MS. Furthermore, if the ME supports any GEA ciphering algorithm that requires a 128-bit ciphering key and a USIM is in use, then the ME shall delete the GPRS GSM Kc128 stored if the RAI is deleted.

GU4: UPDATING DISABLED (UTRAN Iu mode only)

Routing area updating has been disabled.

For this status, the SIM/USIM does not contain any valid RAI, P-TMSI, UMTS integrity key, UMTS ciphering key or ciphering key sequence number. For compatibility reasons, all these fields shall be set to the "deleted" value at the moment the status is set to GMM-DEREGISTERED.eCALL INACTIVE. However the presence of other values shall not be considered an error by the mobile station. The "GPRS update status" stored on the SIM/USIM shall be "not updated".

If the MS is attached for emergency bearer services, the MS shall not store the GMM parameters described in this subclause on the SIM/USIM or in non-volatile memory. Instead the MS shall temporarily store these parameters locally in the ME and the MS shall delete these parameters when the MS is detached.

**************** ****************Next Change**********************

### 4.2.4	Behaviour in state GMM-DEREGISTERED

The state GMM-DEREGISTERED is entered when:

-	the MS is switched on;

-	the GPRS capability has been enabled in the MS;

-	a GPRS detach or combined GPRS detach procedure has been performed;

-	a GMM procedure has failed (except routing area updating, see subclause 4.7.5);

-	the MS attached for emergency bearer services is in PMM-IDLE mode and its periodic routing area update timer expires (see subclause 4.7.2.2); or

-	an eCall only mobile station (as determined by information configured in the USIM) is switched on, or Timers T33XX and T33XY expire.

The selection of the appropriate substate of GMM-DEREGISTERED after switching on is described in subclause 4.2.4.1. The specific behaviour of the MS in state GMM-DEREGISTERED is described in subclause 4.2.4.2. The substate chosen when the GMM-DEREGISTERED state is returned to from another state except state GMM-NULL is described in subclause 4.2.4.3.

It should be noted that transitions between the various substates of GMM-DEREGISTERED are caused by (e.g.):

-	insertion or removal of the SIM/USIM;

-	cell selection/reselection (see also 3GPP TS 43.022 [82] and 3GPP TS 25.304 [98]);

-	PLMN search;

-	loss/regain of coverage; or

-	change of RA.

How various GMM procedures affect the GMM-DEREGISTERED substates and the GPRS update status is described in the detailed description of the GMM procedures in subclause 4.7.

#### 4.2.4.1	Primary substate selection

##### 4.2.4.1.1	Selection of the substate after power on or enabling the MS's GPRS capability

For an eCall only mobile station (as determined by information configured in the USIM), Timers T33XX and T33XY are considered to have expired at power-on. When mobility management is activated after power-on, , the substate shall be PLMN-SEARCH in case the SIM/USIM is inserted and valid. See 3GPP TS 23.122 [14] and 3GPP TS 45.008 [34] for further details.

When the GPRS capability in an activated MS has been enabled, the selection of the GMM-DEREGISTERED substate depends on the MM state and the GPRS update status.

The substate chosen after PLMN-SEARCH, in case of power on or after enabling of the GPRS capability is:

-	if the cell is not supporting GPRS, the substate shall be NO-CELL-AVAILABLE;

-	if no SIM/USIM is present the substate shall be NO-IMSI;

-	for an eCall only mobile station (as determined by information configured in USIM), the state is eCALL INACTIVE;

-	if a suitable cell supporting GPRS has been found and the PLMN or LA is not in the forbidden list, then the substate shall be NORMAL-SERVICE;

-	if the selected cell supporting GPRS is in a forbidden PLMN, is in a forbidden LA, or is a CSG cell with a CSG ID and associated PLMN identity that are not in Allowed CSG list or in the Operator CSG list stored in the MS , then the MS shall enter the substate LIMITED-SERVICE;

-	if the MS is in manual network selection mode and no cell supporting GPRS of the selected PLMN has been found, the MS shall enter the substate NO-CELL-AVAILABLE.

**************** ****************Next Change**********************

#### 4.2.4.1	Primary substate selection

#### 4.2.4.2	Detailed description of the MS behaviour in state GMM-DEREGISTERED

In state GMM-DEREGISTERED, the MS shall behave according to the substate. In the following subclauses, the behaviour is described for the non transient substates.

##### 4.2.4.2.1	Substate, NORMAL-SERVICE

-	The MS shall initiate GPRS attach

-	An eCall only mobile station (as determined by information configured in USIM) shall perform the GPRS eCall inactivity procedure at expiration of timer T33XX or timer T33XY (UTRAN Iu mode only).

##### 4.2.4.2.2	Substate, ATTEMPTING-TO-ATTACH

The MS:

-	shall initiate GPRS attach on the expiry of timers T3311, T3302, or T3346;

-	shall initiate GPRS attach when entering a new PLMN not in the list of equivalent PLMNs, if the PLMN identity of the new cell is not in one of the forbidden PLMN lists and the location area this cell is belonging to is not in one of the lists of forbidden LAs;

-	may initiate GPRS attach for emergency bearer services (UTRAN Iu mode only) even if timer T3346 is running;

-	shall initiate GPRS attach when the routing area of the serving cell in the current PLMN or equivalent PLMN has changed, if timer T3346 is not running and the location area this cell is belonging to is not in one of the lists of forbidden LAs;

-	shall if entry into this state was caused by b) or d) with cause "Retry upon entry into a new cell" of subclause 4.7.3.1.5, perform GPRS attach when a new cell is entered;

-	shall if entry into this state was caused by c) or d) with cause different from "Retry upon entry into a new cell" of subclause 4.7.3.1.5, not perform GPRS attach when a new cell is entered;

-	shall use requests from CM layers to trigger the combined GPRS attach procedure, if timer T3346 is not running and the network operates in network operation mode I. Depending on which of the timers T3311 or T3302 is running the MS shall stop the relevant timer and act as if the stopped timer has expired;

-	initiate GPRS attach upon request of the upper layers to establish a PDN connection for emergency bearer services (UTRAN Iu mode only); and

-	is an eCall only mobile station (as determined by information configured in USIM), it shall perform the GPRS eCall inactivity procedure at expiration of timer T33XX or timer T33XY (UTRAN Iu mode only).

##### 4.2.4.2.3	Substate, LIMITED-SERVICE

The MS:

-	shall initiate GPRS attach when a cell is entered which may provide normal service (e.g. location area is not in one of the forbidden lists);

-	may initiate GPRS attach for emergency bearer services (UTRAN Iu mode only); and

-	is an eCall only mobile station (as determined by information configured in USIM), it shall perform the GPRS eCall inactivity procedure at expiration of timer T33XX or timer T33XY (UTRAN Iu mode only).

##### 4.2.4.2.4	Substate, NO-IMSI

The MS:

-	shall perform default cell selection; and

-	may initiate GPRS attach for emergency bearer services (UTRAN Iu mode only).

##### 4.2.4.2.5	Substate, NO-CELL

The MS shall:

-	perform cell selection according to 3GPP TS 43.022 [82] and 3GPP TS 25.304 [98] and shall choose an appropriate substate.

##### 4.2.4.2.6	Substate, PLMN-SEARCH

The MS shall perform PLMN selection. If a new PLMN is selected, the MS shall reset the GPRS attach attempt counter and initiate the GPRS attach procedure (see subclause 4.7.3.1).

If the selected cell is known not to be able to provide normal service, the MS may initiate GPRS attach for emergency bearer services (UTRAN Iu mode only).

For an eCall only mobile station (as determined by information configured in USIM), if a PLMN is selected an eCall only mobile station perform the GPRS eCall inactivity procedure at expiry of timer T33XX or timer T33XY (UTRAN Iu mode only).

##### 4.2.4.2.7	Substate, ATTACH-NEEDED

The MS shall start a GPRS attach procedure if still needed as soon as the access class control allows network contact in the selected cell.

The MS may initiate GPRS attach for emergency bearer services (UTRAN Iu mode only).

An eCall only mobile station (as determined by information configured in USIM), it shall perform the GPRS eCall inactivity procedure at expiration of timer T33XX or timer T33XY (UTRAN Iu mode only).

##### 4.2.4.2.8	Substate, SUSPENDED (A/Gb mode only)

The MS:

-	shall not send any user data; and

-	shall not send any signalling information.

##### 4.2.4.2.x	Substate, eCALL INACTIVE  (UTRAN Iu mode only)

When in state GMM-DEREGISTERED and substate eCALL INACTIVE, the mobile station shall:

-	not perform periodic routing area updating;

-	not perform detach;

-	reject any requests from CM entities for SM connections except for emergency bearer services and to a non-emergency service (for test and terminal reconfiguration services);

-	not perform normal Routing area updating; and

-	not respond to paging.

**************** ****************Next Change**********************

#### 4.2.4.3	Substate when back to state GMM-DEREGISTERED from another GMM state or PMM state

When returning to state GMM-DEREGISTERED, the MS shall select a cell as specified in 3GPP TS 43.022 [82] and 3GPP TS 25.304 [98].

The substate depends on the result of the cell selection procedure, the outcome of the previously performed GMM specific procedures, on the GPRS update status of the MS, on the location area data stored in the MS and on the presence of the SIM/USIM:

-	if no cell has been found, the substate is NO-CELL-AVAILABLE, until a cell is found;

-	if no SIM/USIM is present or if the inserted SIM/USIM is considered invalid by the MS, the substate shall be NO-IMSI;

-	for an eCall only mobile station (as determined by information configured in USIM), if timer T33XX has expired (if the return to GMM-DEREGISTERED state is the result of an emergency bearer services) or timer T33XY has expired (if the return to GMM-DEREGISTERED state is the result of a non-emergency service for test and terminal reconfiguration services) and the MS does not enter the substate PLMN SEARCH, then the substate shall be eCALL INACTIVE and the GPRS eCall inactivity procedure shall be performed as described in subclause 4.7.x;

-	if a suitable cell supporting GPRS has been found and the PLMN or LA is not in the forbidden list, the substate shall be NORMAL-SERVICE;

-	if a GPRS attach shall be performed (e.g. network requested reattach), the substate shall be ATTEMPTING-TO-ATTACH;

-	if a PLMN reselection (according to 3GPP TS 23.122 [14]) is needed, the substate shall be PLMN SEARCH;

-	if the selected cell is known not to be able to provide normal service, the substate shall be LIMITED-SERVICE.

**************** ****************Next Change**********************

##### 4.2.5.1.6	Substate, LIMITED-SERVICE

The MS:

-	shall perform cell selection/reselection according to 3GPP TS 43.022 [82] and 3GPP TS 25.304 [98];

-	may initiate GPRS attach for emergency bearer services (UTRAN Iu mode only); and

-	is an eCall only mobile station (as determined by information configured in USIM), it shall perform the GPRS eCall inactivity procedure at expiration of timer T33XX or timer T33XY (UTRAN Iu mode only).

**************** ****************Next Change**********************

##### 4.2.5.1.8	Substate, PLMN-SEARCH

When the MM state is IDLE, the GMM substate PLMN-SEARCH may be entered if the MS is in automatic network selection mode and the maximum allowed number of subsequently unsuccessful routing area update attempts controlled by the GPRS routing area updating attempt counter (subclause 4.7.5) have been performed. If a new PLMN is selected, the MS shall reset the routing area updating attempt counter and perform the routing area updating procedure.

If the selected cell is known not to be able to provide normal service, the MS may initiate GPRS attach for emergency bearer services (UTRAN Iu mode only).

For an eCall only mobile station (as determined by information configured in USIM), if a PLMN is selected an eCall only mobile station perform the GPRS eCall inactivity procedure at expiry of timer T33XX or timer T33XY (UTRAN Iu mode only).

**************** ****************Next Change**********************

### 4.7.4	GPRS detach procedure

#### 4.7.4.0	General

The GPRS detach procedure is used:

-	to detach the IMSI for GPRS services only. Independent of the network operation mode, this procedure is used by all kind of GPRS MSs;

-	as a combined GPRS detach procedure used by GPRS MSs operating in MS operation mode A or B to detach the IMSI for GPRS and non-GPRS services or for non-GPRS services only, if the network operates in network operation mode I and no circuit-switched transaction is ongoing;

-	in the case of a network failure condition to indicate to the MS that a re-attach with successive activation of previously active PDP contexts shall be performed. In this case, the MS may also perform the procedures needed in order to activate any previously active multicast service(s);

-	to detach the IMSI or IMEI for emergency bearer services; or

-	as part of the GPRS eCall inactivity procedure defined in subclause 4.7.x.

After completion of a GPRS detach procedure or combined GPRS detach procedure for GPRS and non-GPRS services the GMM context is released.

The GPRS detach procedure shall be invoked by the MS if the MS is switched off, the SIM/USIM card is removed from the MS or if the GPRS or non-GPRS capability of the MS is disabled. The procedure may be invoked by the network to detach the IMSI for GPRS services. The GPRS detach procedure causes the MS to be marked as inactive in the network for GPRS services, non-GPRS services or both services.

If a detach is requested by the HLR for an MS that has a PDP context for emergency services, the SGSN shall not send a DETACH REQUEST message to the MS, and shall follow the procedure described in subclause 6.1.3.4.2 for an MS that has PDP contexts for emergency bearer services.

When upper layers indicates that emergency bearer services are no longer required, the MS if still attached for emergency bearer services, may perform a detach followed by a re-attach to regain normal services, if the MS is in or moves to a suitable cell.

In A/Gb mode, if the GPRS detach procedure is performed, the PDP contexts and the MBMS contexts, if any, are deactivated locally without peer to peer signalling between the SM and LLC entities in the MS and the network.

In Iu mode, if the GPRS detach procedure is performed, the PDP contexts and the MBMS contexts, if any, are deactivated locally without peer to peer signalling between the SM entities in the MS and the network.

If the MS supports S1 mode, the MS shall store the TIN in the non-volatile memory in the ME, as described in 3GPP TS 24.301 [120], annex C, for a subsequent attach procedure.

The MS is allowed to initiate the GPRS detach procedure even if the timer T3346 is running.

The network proceeds with the GPRS detach procedure even if NAS level mobility management congestion control is active.

**************** ****************Next Change**********************

### 4.7.5	Routing area updating procedure

This procedure is used for:

-	normal routing area updating to update the registration of the actual routing area of an MS in the network. This procedure is used by GPRS MSs in MS operation mode C and by GPRS MSs in MS operation modes A or B that are IMSI attached for GPRS and non-GPRS services if the network operates in network operation mode II;

-	combined routing area updating to update the registration of the actual routing and location area of an MS in the network. This procedure is used by GPRS MSs in MS operation modes A or B that are IMSI attached for GPRS and non-GPRS services provided that the network operates in network operation mode I;

-	periodic routing area updating. This procedure is used by GPRS MSs in MS operation mode C and by GPRS MSs in MS operation modes A or B that are IMSI attached for GPRS or for GPRS and non-GPRS services independent of the network operation mode;

-	IMSI attach for non-GPRS services when the MS is IMSI attached for GPRS services. This procedure is used by GPRS MSs in MS operation modes A or B, if the network operates in network operation mode I;

-	in A/Gb mode, resuming GPRS services when the RR sublayer indicated a resumption failure after dedicated mode was left, see 3GPP TS 44.018 [84];

-	in A/Gb mode, updating the network with the new MS Radio Access Capability IE when the content of the IE has changed;

-	updating the network with the new DRX parameter IE when the content of the IE has changed;

NOTE 1:	Such changes can be used e.g. when the MS activates a PDP context with service requirements that cannot be met with the current DRX parameter. As PDP context(s) are activated and deactivated, the GMM context will be updated with an appropriate DRX parameter;

-	re-negotiation of the READY timer value;

-	Iu mode to A/Gb mode and for A/Gb mode to Iu mode intersystem change, see subclause 4.7.1.7;

-	in Iu mode, re-synchronizing the PMM mode of MS and network after RRC connection release with cause "Directed signalling connection re-establishment", see subclause 4.7.2.5;

-	in Iu mode and A/Gb mode after intersystem change from S1 mode, and the GMM receives an indication of "RRC connection failure" from lower layers due to lower layer failure while in S1 mode;

-	S1 mode to Iu mode or S1 mode to A/Gb mode intersystem change and ISR is not activated;

-	S1 mode to Iu mode or S1 mode to A/Gb mode intersystem change and ISR is activated, but the MS changes to a routeing area it has not previously registered with the network;

-	indicating to the network that due to a manual CSG selection the MS has selected a CSG cell whose CSG identity and associated PLMN identity are not included in the MS's Allowed CSG list or in the MS's Operator CSG list;

-	indicating to the network that the mobile station classmark 2, mobile station classmark 3 or the supported codecs have changed for a MS supporting SRVCC; or

-	indicating the current radio access technology to the network for the support of terminating access domain selection for voice calls or voice sessions (for details see subclause 4.7.5.1 and subclause 4.7.5.2.1).

While an MS has a PDN connection for emergency bearer services, the MS shall not perform manual CSG selection.

The routing area updating procedure shall also be used by a MS which is attached for GPRS services if a new PLMN is entered (see 3GPP TS 23.122 [14]), unless the MS is configured for "AttachWithIMSI" as specified in 3GPP TS 24.368 [135] or 3GPP TS 31.102 [112] and the new PLMN is neither the registered PLMN nor in the list of equivalent PLMNs.

An eCall only mobile station (as determined by information configured in USIM) shall not perform a normal or combined routing area updating procedure while in GMM-DEREGISTERED.eCALL INACTIVE state.

Subclause 4.7.5.1 describes the routing area updating procedures for updating the routing area only. The combined routing area updating procedure used to update both the routing and location area is described in subclause 4.7.5.2.

The routing area updating procedure is always initiated by the MS. It is only invoked in state GMM-REGISTERED.

To limit the number of subsequently rejected routing area update attempts, a routing area updating attempt counter is introduced. The routing area updating attempt counter shall be incremented as specified in subclause 4.7.5.1.5. Depending on the value of the routing area updating attempt counter, specific actions shall be performed. The routing area updating attempt counter shall be reset when:

-	a GPRS attach procedure is successfully completed;

-	a routing area updating procedure is successfully completed; or

-	a combined routing area updating procedure is completed for GPRS services only with cause #2 or #28;

-	a routing area updating procedure is rejected with cause #11, #12, #13, #14, #15 or #25;

and additionally when the MS is in substate ATTEMPTING-TO-UPDATE:

-	a new routing area is entered;

-	expiry of timer T3302;

-	at request from registration function; or

-	timer T3346 is started.

The mobile equipment shall contain a list of "forbidden location areas for roaming", as well as a list of "forbidden location areas for regional provision of service". The handling of these lists is described in subclause 4.4.1.

The Mobile Equipment shall contain a list of "equivalent PLMNs". The handling of this list is described in subclause 4.4.1.

In a shared network, the MS shall choose one of the PLMN identities as specified in 3GPP TS 23.122 [14]. The MS shall construct the Routing Area Identification of the cell from this chosen PLMN identity, and the LAC and the RAC received on the BCCH. If the constructed RAI is different from the stored RAI, the MS shall initiate the routing area updating procedure. For:

-	a shared GERAN, in A/Gb mode, the chosen PLMN identity is indicated to the GERAN in the first RLC data block of an upper layer PDU (see 3GPP TS 44.060 [76]) when a foreign TLLI is used by the network sharing supporting MS for the transmission.

-	a shared UTRAN, the chosen PLMN identity shall be indicated to the UTRAN in the RRC INITIAL DIRECT TRANSFER message (see 3GPP TS 25.331 [23c]).

For GERAN Iu mode, network sharing is not supported.

Whenever a ROUTING AREA UPDATING REJECT message with the cause "PLMN not allowed" is received by the MS, the chosen PLMN identity shall be stored in the "forbidden PLMN list". Whenever a ROUTING AREA UPDATING REJECT message is received by the MS with the cause "Roaming not allowed in this location area", "Location Area not allowed", or "No suitable cells in Location Area", the LAI that is part of the constructed RAI which triggered the routing area updating procedure shall be stored in the suitable list.

In A/Gb mode, user data transmission in the MS shall be suspended during the routing area updating procedure, except if the routing area updating procedure is triggered by a PS handover procedure as described in 3GPP TS 43.129 [113]; user data reception shall be possible. User data transmission in the network may be suspended during the routing area updating procedure.

In Iu mode, user data transmission and reception in the MS shall not be suspended during the routing area updating procedure. User data transmission in the network shall not be suspended during the routing area updating procedure.

In Iu mode, when a ROUTING AREA UPDATE REQUEST is received by the SGSN over a new PS signalling connection while there is an ongoing PS signalling connection (network is already in mode PMM-CONNECTED) for this MS, the network shall progress the routing area update procedure as normal and release the previous PS signalling connection when the routing area update procedure has been accepted by the network.

NOTE 2:	The re-establishment of the radio bearers of active PDP contexts is done as described in subclause "Service Request procedure".

The network informs the MS about the support of specific features, such as LCS-MOLR, MBMS, IMS voice over PS session, emergency bearer services in Iu mode in the Network feature support information element. The information is either explicitly given by sending the Network feature support IE or implicitly by not sending it. The handling in the network is described in subclause 9.4.15.11The network can also use the Additional network feature support IE in order to inform the MS about the support of specific features such as the delivery of SMS via GPRS (GPRS-SMS) or implicitly by not sending it. . The MS may use the support indications for LCS-MO,LR MBMS and GPRS-SMS to inform the user about the availability of the appropriate services. The MS shall not request the LCS-MOLR or MBMSservices, if the service has not been indicated as available. The indication for MBMS is defined in subclause "MBMS feature support indication" in 3GPP TS 23.246 [106]. In an MS with IMS voice over PS capability, the IMS voice over PS session indicator and the emergency bearer services indicator shall be provided to the upper layers. The upper layers take the IMS voice over PS session indicator into account as specified in 3GPP TS 23.221 [131], subclause 7.2a and subclause 7.2b, when selecting the access domain for voice sessions or calls in Iu mode. When initiating an emergency call in Iu mode, the upper layers also take the emergency bearer services indicator into account for the access domain selection. The MS may use the GPRS-SMS indication in order to obtain SMS.

**************** ****************Next Change**********************

### 4.7.x	GPRS eCall inactivity procedure

The eCall inactivity procedure is applicable only to an eCall only mobile station (as determined by information configured in USIM) for UTRAN in Iu mode only. The procedure shall be initiated when timer T33XX or timer T33XY expires or is found to have already expired in any GMM-DEREGISTERED state except NO IMSI, NO CELL AVAILABLE or PLMN SEARCH. The mobile station shall then stop other running timers (e.g. T3311, T3312) and shall perform detach procedure if required by the serving network and if the update state is GU1, or shall perform local detach procedure. The mobile station then enters GMM-DEREGISTERED.eCALL INACTIVE state and the mobile station shall delete any RAI, P-TMSI, ciphering key sequence number stored in the SIM/USIM and set the update state to GU4 Updating Disabled.

NOTE:	If timers T33XX and T33XY are larger in value than T3312 or T3312 extended, then the MS shall set the timers T33XX and T33XY to the value of T3312 or T3312 extended.

While in GMM-DEREGISTERED.eCALL INACTIVE state, the mobile station shall maintain awareness of a potential serving cell in a potential serving network but shall not initiate GMM signalling with the network and shall ignore any paging request.

The mobile station shall leave GMM-DEREGISTERED.eCALL INACTIVE state only when one of the following events occurs:

-	if the SIM or USIM is removed, the mobile station enters the NO IMSI state;

-	if coverage is lost, the mobile station enters PLMN SEARCH state;

-	if the mobile station is deactivated (e.g. powered off) by the user, the mobile station enters the NULL state;

-	if there is a CM request for an emergency bearer services, the mobile station should follow the procedure in subclause 4.2.4.3 and enter the GMM-DEREGISTERED state,  and initiate the GMM and CM procedures to establish the emergency bearer services; or

-	if there is a CM request for a non-emergency service (for the purpose of accessing test and terminal reconfiguration services), the mobile station should follow the procedure in subclause 4.2.4.3 and enter the GMM-DEREGISTERED state, and initiate the GMM and CM procedures to establish the non-emergency service.

**************** ****************Next Change**********************

### 11.2.2	Timers of GPRS mobility management

Table 11.3/3GPP TS 24.008: GPRS Mobility management timers - MS side

| TIMER NUM. | TIMER VALUE | STATE | CAUSE OF START | NORMAL STOP | ON THE 1st, 2nd, 3rd, 4th EXPIRY Note 3 |
| --- | --- | --- | --- | --- | --- |
| T3310 | 15s | GMM- REG-INIT | ATTACH REQUEST sent | ATTACH ACCEPT received ATTACH REJECT received | Retransmission of ATTACH REQUEST |
| T3311 | 15s | GMM-DEREG ATTEMPTING TO ATTACH or GMM-REG ATTEMPTING TO UPDATE GMM-REG NORMAL SERVICE | ATTACH REJECT with other cause values as described in chapter 'GPRS Attach' ROUTING AREA UPDATE REJECT with other cause values as described in chapter 'Routing Area Update' Low layer failure | Change of the routing area GPRS attach procedure initiated RAU procedure initiated Iu mode - PMM CONNECTED mode entered (Note 1) A/Gb mode - READY timer is started (Note 1) | Restart of the Attach or the RAU procedure with updating of the relevant attempt counter |
| T3316 | 30s | GMM- REG-INIT GMM-REG GMM-DEREG-INIT GMM-RA-UPDATING-INT GMM-SERV-REQ-INIT (Iu mode only) | RAND and RES stored as a result of a UMTS authentication challenge RAND and SRES stored as a result of a GSM authentication challenge | Security mode setting (Iu mode only) SERVICE ACCEPT received. (Iu mode only) SERVICE REJECT received (Iu mode only) ROUTING AREA UPDATE ACCEPT received AUTHENTICATION AND CIPHERING REJECT received AUTHENTICATION AND CIPHERING FAILURE sent Enter GMM-DEREGISTERED, GMM-NULL or PMM-IDLE mode (Iu mode only) | Delete the stored RAND, and either RES (if it was a UMTS authentication challenge) or SRES (if it was a GSM authentication challenge) |
| T3318 | 20s | GMM- REG-INIT GMM-REG GMM-DEREG-INIT GMM-RA-UPDATING-INT GMM-SERV-REQ-INIT (Iu mode only) | AUTHENTICATION AND CIPHERING FAILURE (cause=’MAC failure’ or ‘GSM authentication unacceptable’) sent | AUTHENTICATION AND CIPHERING REQUEST received or AUTHENTICATION AND CIPHERING REJECT received | On first expiry, the MS should consider the network as false and will follow subclause 4.7.7.6.1, if the MS is not attached for emergency bearer services. On the first expiry, the MS will follow subclause 4.7.7.6, under "for items f and g", if the MS is attached for emergency bearer services. |
| T3320 | 15s | GMM- REG-INIT GMM-REG GMM-DEREG-INIT GMM-RA-UPDATING-INT GMM-SERV-REQ-INIT (Iu mode only) | AUTHENTICATION AND CIPHERING FAILURE (cause=synch failure) sent | AUTHENTICATION AND CIPHERING REQUEST received or AUTHENTICATION AND CIPHERING REJECT received | On first expiry, the MS should consider the network as false and will follow the subclause 4.7.7.6.1, if the MS is not attached for emergency bearer services. On the first expiry, the MS will follow subclause 4.7.7.6, under "for items f and g", if the MS is attached for emergency bearer services. |
| T3321 | 15s | GMM- DEREG-INIT | DETACH REQUEST sent | DETACH ACCEPT received | Retransmission of the DETACH REQUEST |
| T3330 | 15s | GMM-ROUTING-UPDATING-INITIATED | ROUTING AREA UPDATE REQUEST sent | ROUTING AREA UPDATE ACCEPT received ROUTING AREA UPDATE REJECT received | Retransmission of the ROUTING AREA UPDATE REQUEST message |
| T3340 (Iu mode only) | 10s | GMM- REG-INIT GMM-DEREG-INIT GMM-RA-UPDATING-INT GMM-SERV-REQ-INIT (Iu mode only) GMM-ATTEMPTING-TO-UPDATE-MM GMM-REG-NORMAL-SERVICE | ATTACH REJECT, DETACH REQUEST, ROUTING AREA UPDATE REJECT or SERVICE REJECT with any of the causes #11, #12, #13, #15, or #25. ATTACH ACCEPT or ROUTING AREA UPDATE ACCEPT is received with “no follow-on proceed“ indication. DETACH ACCEPT received after the MS sent DETACH REQUEST with detach type to "IMSI detach" | PS signalling connection released | Release the PS signalling connection and proceed as described in subclause 4.7.1.9 |
| NOTE 1: The conditions for which this applies are described in subclause 4.7.5.1.5. |

Table 11.3a/3GPP TS 24.008: GPRS Mobility management timers – MS side

| TIMER NUM. | TIMER VALUE | STATE | CAUSE OF START | NORMAL STOP | ON EXPIRY |
| --- | --- | --- | --- | --- | --- |
| T3302 | Default 12 min Note 5 | GMM-DEREG or GMM-REG | At attach failure and the attempt counter is greater than or equal to 5. At routing area updating failure and the attempt counter is greater than or equal to 5. | GPRS attach procedure initiated RAU procedure initiated | On every expiry, initiation of the GPRS attach procedure or RAU procedure |
| T3312 | Default 54 min Note 8 | GMM-REG | In A/Gb mode, when READY state is left. In Iu mode, when PMM-CONNECTED mode is left. | When entering state GMM-DEREG | Initiation of the Periodic RAU procedure if the MS is not attached for emergency bearer services. Implicit detach from network if the MS is attached for emergency bearer services. |
| T3314 READY (A/Gb mode only) | Default 44 sec Note 2 | All except GMM-DEREG | Transmission of a PTP PDU | Forced to Standby | No cell-updates are performed |
| T3317 (Iu mode only) | 15s | GMM-SERVICE-REQUEST-INITIATED | SERVICE REQUEST sent | Security mode control procedure is completed, SERVICE ACCEPT received, or SERVICE REJECT received | Abort the procedure |
| T3319 (Iu mode only) | Default 30s Note 1 Note 4 | GMM-REG | Completion of the Security Mode Control procedure after sending a SERVICE REQUEST with service type "data". Reception of a SERVICE ACCEPT message. | When entering PMM-IDLE mode. When the radio access bearer is released for any active PDP context. When entering state GMM-DEREG | SERVICE REQUEST with service type “data” may be invoked again, if required. |
| T3323 | NOTE 6 | GMM-REGISTERED | T3312 expires while ISR is activated and the MS is in one of the following states: -GMM-REGISTERED.NO-CELL-AVAILABLE ; -GMM-REGISTERED.PLMN-SEARCH; -GMM-REGISTERED.UPDATE-NEEDED;or -GMM-REGISTERED.LIMITED-SERVICE. | When entering state GMM-DEREGISTERED or when entering GMM-CONNECTED mode. | Deactivation of ISR by setting TIN to "GUTI" |
| T3346 | NOTE 7 | GMM-DEREGISTERED. ATTEMPTING-TO-ATTACH GMM-REGISTERED. ATTEMPTING-TO-UPDATE GMM-REGISTERED EMM-DEREGISTERED. ATTEMPTING-TO-ATTACH EMM-REGISTERED. ATTEMPTING-TO-UPDATE EMM-REGISTERED (defined in 3GPP TS 24.301 [120]) | ATTACH REJECT, ROUTING AREA UPDATE REJECT or SERVICE REJECT received with a timer value for T3346; "Extended wait time" for PS domain from the lower layers (defined in 3GPP TS 25.331 [23c]). ATTACH REJECT, TRACKING AREA UPDATE REJECT or SERVICE REJECT (defined in 3GPP TS 24.301 [120]) received with a timer value for T3346; "Extended wait time" from the lower layers. (defined in 3GPP TS 36.331 [22]) | Paging received | Initiation of attach procedure, routing area updating procedure or service request procedure, dependent on GMM state and GPRS update status. Initiation of attach procedure, tracking area updating procedure or service request procedure, dependent on EMM state and EPS update status. (defined in 3GPP TS 24.301 [120]) |
| T33XX (UTRAN Iu mode only) | All except NULL (NOTE 9) | 12 hours | eCall only MS enters PMM-IDLE state after an emergency call | Removal of eCall only restriction | Perform eCall Inactivity procedure in subclause 4.7.x |
| T33XY (UTRAN Iu mode only) | All except NULL (NOTE 9) | 12 hours | eCall only MS enters PMM-IDLE state after a test/reconfiguration call | Removal of eCall only restriction | Perform eCall Inactivity procedure in subclause 4.7.x |

NOTE 1:	The default value of this timer is used if the network does not indicate another value in a GMM signalling procedure.

NOTE 2:	The default value of this timer is used if neither the MS nor the Network send another value, or if the Network sends this value, in a signalling procedure.

NOTE 3:	Typically, the procedures are aborted on the fifth expiry of the relevant timer. Exceptions are described in the corresponding procedure description.

NOTE 4: 	The purpose of this timer is to prevent the MS from repeating the SERVICE REQUEST message with service type "data" too early in case the request to setup the radio access bearer is queued by the radio access network.

NOTE 5:	The cases in which the default value of this timer is used are described in subclause 4.7.2.7.

NOTE 6:	The value of this timer may be provided by the network to the MS in the ATTACH ACCEPT message and ROUTING AREA UPDATE ACCEPT message. The default value of this timer is identical to the value of timer T3312.

NOTE 7:	The timer value is provided by the network in an ATTACH REJECT, ROUTING AREA UPDATE REJECT, TRACKING AREA UPDATE REJECT or SERVICE REJECT message or as a "Extended wait time" value by the lower layers, or chosen randomly from a default value range of 15 – 30 minutes.

NOTE 8:	The cases in which the default value of this timer is used are described in subclause 4.7.2.2.

NOTE 9:	If the value of T33XX or T33XY is larger than T3312, then the value of this timer is set equal to T3312.

Table 11.4/3GPP TS 24.008: GPRS Mobility management timers - network side

| TIMER NUM. | TIMER VALUE | STATE | CAUSE OF START | NORMAL STOP | ON THE 1st, 2nd, 3rd, 4th EXPIRY Note 3 |
| --- | --- | --- | --- | --- | --- |
| T3322 | 6s | GMM- DEREG-INIT | DETACH REQUEST sent | DETACH ACCEPT received | Retransmission of DETACH REQUEST |
| T3350 | 6s | GMM-COMMON-PROC-INIT | ATTACH ACCEPT sent with P-TMSI and/or TMSI RAU ACCEPT sent with P-TMSI and/or TMSI P-TMSI REALLOCATION COMMAND sent | ATTACH COMPLETE received RAU COMPLETE received P-TMSI REALLOCATION COMPLETE received | Retransmission of the same message type, i.e. ATTACH ACCEPT, RAU ACCEPT or REALLOCATION COMMAND |
| T3360 | 6s | GMM- COMMON-PROC-INIT | AUTHENTICATION AND CIPHERING REQUEST sent | AUTHENTICATION AND CIPHERING RESPONSE received AUTHENTICATION-AND CIPHERING-FAILURE received | Retransmission of AUTHENTICATION AND CIPHERING REQUEST |
| T3370 | 6s | GMM-COMMON-PROC-INIT | IDENTITY REQUEST sent | IDENTITY RESPONSE received | Retransmission of IDENTITY REQUEST |

Table 11.4a/3GPP TS 24.008: GPRS Mobility management timers - network side

| TIMER NUM. | TIMER VALUE | STATE | CAUSE OF START | NORMAL STOP | ON EXPIRY |
| --- | --- | --- | --- | --- | --- |
| T3313 | Note 1 | GMM_REG | Paging procedure initiated | Paging procedure completed | Network dependent |
| T3314 READY (A/Gb mode only) | Default 44 sec Note 2 | All except GMM-DEREG | Receipt of a PTP PDU | Forced to Standby | The network shall page the MS if a PTP PDU has to be sent to the MS |
| Mobile Reachable | Note 4 | All except GMM-DEREG | In A/Gb mode, change from READY to STANDBY state In Iu mode, change from PMM-CONNECTED mode to PMM-IDLE mode. | PTP PDU received | Network dependent but typically paging is halted on 1st expiry if the MS is not attached for emergency bearer services. Implicitly detach the MS which is attached for the emergency bearer services. |
| Implicit Detach timer | Note 5 | All except GMM-DEREG | The Mobile Reachable timer expires while the network is in PMM-IDLE mode or STANDBY state. | PTP PDU received | Implicitly detach the MS on 1st expiry |

NOTE 1:	The value of this timer is network dependent.

NOTE 2:	The default value of this timer is used if neither the MS nor the Network send another value, or if the Network sends this value, in a signalling procedure. The value of this timer should be slightly shorter in the network than in the MS, this is a network implementation issue.

NOTE 3:	Typically, the procedures are aborted on the fifth expiry of the relevant timer. Exceptions are described in the corresponding procedure description.

NOTE 4:	The default value of this timer is 4 minutes greater than T3312. If T3346 is larger than T3312 and the SGSN includes timer T3346 in the ROUTING AREA UPDATE REJECT message or the SERVICE REJECT message, the value of the Mobile Reachable timer is 4 minutes greater than T3346. If the MS is attached for emergency bearer services, the value of this timer is set equal to T3312.

NOTE 5:	The value of this timer is network dependent. If ISR is activated, the default value of this timer is 4 minutes greater than T3323.

# Comments

Enter the ETSI deliverable number in this box. For example, "180 002". Do not prefix the number. i.e. do not use "TR TS EN DTR etc",

Enter the version of the deliverable here. This number is the version of the deliverable to which the CR will be applied if it is approved. Make sure that the latest version of the deliverable (of the relevant release) is used when creating the CR.

Enter the CR number here. This number is allocated by the ETSI Support Team.  It consists of at least three digits, padded with leading zeros as necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter a concise description of the subject matter of the CR. It should be no longer than one line.  Do not use redundant information such as "Change Request number xxx to TR  xx.xxx".

One or more organizations (ETSI Members) which drafted the CR and are presenting it.

Enter the Work Item Reference in this box. For example, "00005". Do not prefix the number.

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter the number of each clause which contains changes.

Enter the Work Item Reference of  any other specifications are affected by this change.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.