Updated Terms of Reference for STF 85V 
TBR for TETRA Emergency Services
[TA23(95)55], [B11(98)17]

1.	Reasons for proposing the STF:

To produce a TBR for TETRA Emergency services in accordance with Directive 91/263/EEC under mandate BC-T-314.

2.	Consequences if not agreed:

To allow the market entrance of TETRA terminal equipment, intended for Police and Emergency services operating within European harmonised frequency bands in the range 380-383 MHz and 390-393 MHz, a base for certification is required which allows interconnection to other networks.

A non-agreement would limit the ability of free movement of these TETRA terminals and limit the right of TETRA networks to connect to any other network.

3.	Detailed description:

3.1.	Subject title:

TBR for TETRA Emergency Services.

3.2.	Reference TC:

EP/TETRA

3.3.	Other interested TCs (if any):

3.4.	Duration:

Until 1998.

3.5.	Target date for the start of work:

Start: Beginning January 1996.

3.6.	Necessary manpower (expertise, mix of skills and amount):

14 man-months.

3.7.	Context of the study:

Based on the Conformance Test ETS 300 394, parts 1, 2, and 3, the STF shall produce the TBR for TETRA Emergency Services.

3.8.	Related activity in other bodies and necessary coordination of schedules:

N/A

3.9.	Scope of the terms of reference and relevant Work Items:

TETRA terminal equipment consists of several elements. The TBR shall be structured to allow testing and approval of the individual elements as separate items. Because of the need for effective use of the radio frequency spectrum, the essential air interface characteristics shall be tested. For each essential requirement, a test should be given including measurement methods.

Requirements shall be applicable to the public network interface and the RF air interface of the equipment. Both interfaces may be stimulated to perform the tests by additional equipment.

In collaboration with TRAC correspondent, consideration shall be given to which of the article 4 paragraphs are appropriate for Emergency access.

The TBR shall be based on the radio and protocol provisions of ETS 300 394. There shall be no EMC requirements in terms of the Terminal Directive 91/263/EEC article 4c.

3.10.	Reference specification(s) and existing documents, including ETSI member contributions:

ETS 300 392, parts 1 and 2;

ETS 300 393, parts 1 and 2;

ETS 300 394, parts 1, 2, and 3.

3.11.	Work Item(s) from the ETSI Work Programme (EWP) for which the STF is required:

DTBR/RES-06016

3.12.	Expected output(s):

TBR for TETRA Emergency Services.