# Terms of Reference for a Specialist Task Force 191 (ex IT) (EP/BRAN) on
Maintenance and Validation of Conformance Test Specifications for HIPERLAN type 2 systems

# 1	Reasons for proposing a Specialist Task Force

HIPERLAN type 2 (H/2 in the following) is a wireless LAN designed to transport data between a wireless access point and a terminal at speeds up to 25 Mbit/s. One of the major goals of H/2 standards is interoperability. This can only be achieved by quick, careful and broad conformance test specification.

EP/BRAN has developed and published technical specifications for H/2 between December 1999 and the middle of 2000. In the next two years several revisions of these specifications are expected.

The initial steps for conformance test specifications have been completed. They comprise of the complete set of conformance test specifications for H/2 Physical Layer, Data Link Control Layer and the common part of the packet based Convergence Sub-layer. The work is in progress to develop additional documents and features such as profile of the DLC for Business and Home Environments and convergence layers for ATM and IEEE 1394 networks and adding more test cases to the RLC test specifications.

The Specialist Task Force is proposed to upgrade existing H/2 conformance test specifications based on:

-	revisions of the base standards expected during the next two years;

-	comments on existing test specifications provided by Members;

-	comments made by companies implementing test tools.

The following should also be noted:

-	the need for conformance test specifications in assuring interoperability of H/2 devices as one of it’s key competitive advantages;

-	the need for high-scaled experts having practice in writing advanced TTCN programs;

- the need for specialised equipment and programs which are not available to voluntary experts in the normal course of their work;

- the possibility of relying on H/2 expertise already established in previous phases of the work.

Experience with the development of other standards has shown that involvement of experts on conformance testing requires highly specialised knowledge, notably of TTCN. In addition, the generation of this kind of specifications requires significant effort and it cannot be expected that this effort can be provided on a voluntary basis. Hence, the involvement of testing experts is needed, in order to assure timely completion and high quality of the Test Specifications. These testing experts are not available on EP/BRAN level and need to be recruited on a funded basis.

# 2	Consequences if not agreed

Comments derived during implementation of existing ETSI test specifications cannot be handled appropriately and validated test suites can only be provided at a much later date. Absence of the unique solution of conformance test bugs will force test suite implementers to develop their own solutions. This results in different test suite implementations (all claiming be conformant to the ETSI standard) and different equipment implementations possibly suffering from interworking problems. Finding own solution is diverting resource from completing implementations, and delaying presence of implementations of the standard in the field.

Conformance test specifications can only be provided at a much later date, requiring implementations to be developed in the absence of a harmonised conformance testing specification. This will result in a higher probability of inconsistent implementations within Europe.

Absence of conformance testing specifications will force implementers and service providers to develop their own interim solutions, diverting resource from completing implementations, implementing and verifying test standards produced up to now and delaying presence of implementations of the standard in the field.

- Producing own interim solutions by each implementation and service provider would result in a more expensive solution than using centralised resources on a European level. A delay of the conformance test specifications would jeopardise the leading position ETSI has with its work on H/2. The result will be that products according to other standards, e.g. IEEE 802.11, would have enough time to completely penetrate the market, which will make it very difficult if not impossible to re-gain a significant share for H/2.

- A lack of interoperability. As explained above, interoperability is vital for the market success.

These two issues are of significant importance for the success of the standardisation of H/2 systems. The failure of the standard would result in a major waste of time and money spent by a huge number of European companies in the course of the project.

It can be expected that IEEE 802.11 will fill the gap completely if interoperability and time-to-market are not achieved, even if the technology may be inferior to HIPERLAN type 2. Currently, mostly US companies are building IEEE 802.11 wireless LAN products. The failure of H/2 would result in another area in communications technology that is occupied by US companies and lost for European manufacturers.

Hence, an STF is urgently needed in order to produce new revisions of the Conformance Testing standards in the scheduled time frame, using the tools and formal methods that have proven their value in ETSI.

# 3	Detailed description

## 3.1	Subject title

Maintenance and validation of Conformance Test Specifications for the interoperability of HIPERLAN type 2 systems.

## 3.2	Reference Technical Body

ETSI Project Broadband Radio Access Networks (EP BRAN).

## 3.3	Other interested TBs

EP UMTS, TC-ERM

## Duration

The STF should complete the deliverables for approval in 12 month from the start date. STF resources should be available for the resolution of the remaining comments.

## Target dates for the start of the work

July 2001.

## 3.6.	Necessary manpower (expertise, mix of skills and amount):

### 3.6.1	Necessary manpower

The total resources required for this STF are 6 man month, split as follows:

| for drafting deliverables (test specifications): | 5,8 MM |
| --- | --- |
| for general technical support of the Technical Body and its WGs: | 0,2 MM |

### 3.6.2	Estimated costs, additional to the manpower:

No travels are planned for the experts. The travel for the PEX member (see 3.6.3 bullet 4) will be covered from the PTCC budget.

### 3.6.3	Qualification required, mix of skills

The documents that shall be produced will consist of PICS (Protocol Implementation Conformance Statement), Test Suite Structure and Test Purposes (TSS&TP), and Abstract Test Suite (ATS) and PIXIT. Hence, persons with the following skills are required:

- One expert with expertise in the production of PICS, available part time. It is expected that this task will require approximately 15% of the STF funding.

- One expert for the maintenance of the Test Suite Structure and Test Purposes (TSS&TP) documents, available part time. It is expected that this task will require approximately 20% of the STF funding

- At least one expert with experience in production of TTCN is needed.. It is expected that this task will require approximately 55% of the STF funding.

- General technical support and project leadership should be carried out by a member of the ETSI PEX. It is expected that a PEX member will be the STF leader and will participate at the project and WG meetings.

## 3.7	Related activity in other bodies and necessary co-ordination of schedules

Possible co-ordination with activities of HIPERLAN Global Forum.

## 3.8	Scope of the Terms of Reference

- The tasks of the STF are based on the specifications produced and expected to be revised by EP/BRAN. The related work items are described in section 3.9. The areas to be covered by the STF will be the maintenance of test specifications for functions of H/2 that are relevant for interoperability.

What is not in the scope of these ToR:

- The STF will not develop the RLC or any other protocol. This work is being performed completely on a voluntary basis on EP/BRAN level with some PEX support.

- The test specifications will not explicitly cover the data transport functions. These will be tested implicitly by the ability of the system under test to communicate with the test system for example during error control tests.

## 3.9	Reference specifications and existing documents, including member contributions

The following work items are relevant references for the work on Conformance Test Specifications:

| Name of the work item | Stable version expected availability |
| --- | --- |
| TR 101 031: Broadband Radio Access Networks (BRAN); HIgh PErformance Radio Local Area Network (HIPERLAN) Type 2; Requirements and architectures for wireless broadband access. | Available |
| DTS/BRAN-0024003-1: Broadband Radio Access Networks (BRAN); Cell based convergence layer for HIPERLAN Type 2; Part 1: Common part | Available |
| DTS/BRAN-0024003-2: Broadband Radio Access Networks (BRAN); Cell based convergence layer for HIPERLAN Type 2; Part 2: ATM-UNI service specific part | Available |
| DTS/BRAN-0024004-1: Broadband Radio Access Networks (BRAN); Packet Based Convergence Layer for HIPERLAN Type 2; Part 1: Common Part | Available |
| DTS/BRAN-0024004-2: Broadband Radio Access Networks (BRAN); Packet Based Convergence Layer for HIPERLAN Type 2; Part 2: Ethernet Service Specific Convergence Sublayer | Available |
| DTS/BRAN-0024004-3: Broadband Radio Access Networks (BRAN); Packet Based Convergence Layer for HIPERLAN Type 2; Part 3: IEEE 1394 Service Specific Convergence Sublayer | Available |
| DTS/BRAN-0024004-4: Broadband Radio Access Networks (BRAN); Packet Based Convergence Layer for HIPERLAN Type 2; Part 4: IEEE 1394 Bridge Layer | February 2001 |
| DTS/BRAN-0020004-1: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2 Data Link Control (DLC) Layer; Part 1: Basic Data Transport Functions | Available |
| DTS/BRAN-0020004-2: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2 Data Link control (DLC) Layer; Part 2: Radio Link Control Sublayer Basic Functions | Available |
| DTS/BRAN-0020004-3: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Data Link Control (DLC) Layer; Part 3: Profile for Business Environment | Available |
| DTS/BRAN-0020004-4: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2 Data Link Control (DLC) Layer; Part 4: Extension for Home Environment. | Available |
| ETR 212: PICS pro-forma style guide | Available |
| ETR 266: Test purpose style guide | Available |
| ETS 300 406: Protocol and profile conformance testing specifications; standardisation methodology | Available |
| DTS/BRAN-002T004-2-2: Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for Radio Link Control Sublayer (RLC) Basic Functions; Part 2: Test Suite Structure and Test Purposes (TSS & TP) | Available |
| RTS/BRAN-002T0A4-2-3: Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for Radio Link Control Sublayer (RLC) Basic Functions; Part 3: Abstract Test Suite (ATS) (Major Revision) | 15/04/ 2001 |
| RTS/BRAN-002T004-2-1: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Data Link Control (DLC) Layer; Part 2: Radio Link Control (RLC) sublayer; Sub-part 1: PICS | 15/04/ 2001 |
| RTS/BRAN-002T004-2-2: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Data Link Control (DLC) Layer; Part 2: Radio Link Control (RLC) sublayer; Sub-part 2: TSS & TP | 15/04/ 2001 |
| RTS/BRAN-002T004-2-3: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Data Link Control (DLC) Layer; Part 2: Radio Link Control (RLC) sublayer; Sub-part 3: ATS (Major Revision) | 15/04/ 2001 |
| DTS/BRAN-002T004-3-1: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Data Link Control (DLC) Layer; Part 3: Profile for Business Environment; Sub-part 1: PICS proforma | 15/04/ 2001 |
| DTS/BRAN-002T004-3-2: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Data Link Control (DLC) Layer; Part 3: Profile for Business Environment; Sub-part 2: TSS & TP | 15/04/ 2001 |
| DTS/BRAN-002T004-3-3: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Data Link Control (DLC) Layer; Part 3: Profile for Business Environment; Sub-part 3: ATS | 15/04/ 2001 |
| DTS/BRAN-002T004-4-1: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Data Link Control (DLC) Layer; Part 4: Extension for Home Environment; Sub-part 1: PICS proforma | 15/04/ 2001 |
| DTS/BRAN-002T004-4-2: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Data Link Control (DLC) Layer; Part 4: Extension for Home Environment; Sub-part 2: TSS & TP | 15/04/ 2001 |
| DTS/BRAN-002T004-4-3: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Data Link Control (DLC) Layer; Part 4: Extension for Home Environment; Sub-part 3: ATS | 15/04/ 2001 |
| DTS/BRAN-0024T03-1-1: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Cell based Convergence Layer; Part 1: Common part; Sub-part 1: PICS proforma | 15/04/ 2001 |
| DTS/BRAN-0024T03-1-2: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Cell based Convergence Layer; Part 1: Common part; Sub-part 2: TSS & TP specification | 15/04/ 2001 |
| DTS/BRAN-0024T03-1-3: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Cell based Convergence Layer; Part 1: Common part; Sub-part 3: ATS | 15/04/ 2001 |
| DTS/BRAN-0024T03-2-1: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Cell based Convergence Layer; Part 2: UNI Service SpecificConvergence Sublayer (SSCS); Sub-part 1: PICS proforma | 15/04/ 2001 |
| DTS/BRAN-0024T03-2-2: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Cell based Convergence Layer; Part 2: UNI Service Specific Convergence Sublayer (SSCS); Sub-part 2: TSS & TP | 15/04/ 2001 |
| DTS/BRAN-0024T03-2-3: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Cell based Convergence Layer; Part 2: UNI Service Specific Convergence Sublayer (SSCS); Sub-part 3: ATS | 15/04/ 2001 |
| DTS/BRAN-0024T04-1-1: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Packet Based Convergence Layer; Part 1: Common part; Sub-part 1: PICS proforma | available |
| DTS/BRAN-0024T04-1-2: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Packet Based Convergence Layer; Part 1: Common part; Sub-part 2: TSS & TP | available |
| DTS/BRAN-0024T04-1-3: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Packet Based Convergence Layer; Part 1: Common part; Sub-part 3: ATS | available |
| DTS/BRAN-0024T04-2-1: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Packet Based Convergence Layer Part 2: Ethernet Service Specific Convergence Sublayer (SSCS); Sub-part 1: PICS proforma | 15/04/ 2001 |
| DTS/BRAN-0024T04-2-2: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Packet Based Convergence Layer; Part 2 : Ethernet Service Specific Convergence Sublayer (SSCS); Sub-part 2: TSS & TP | 15/04/ 2001 |
| DTS/BRAN-0024T04-2-3: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Packet Based Convergence Layer; Part 2: Ethernet Service Specific Convergence Sublayer (SSCS); Sub-part 3: ATS | 15/04/ 2001 |
| DTS/BRAN-0024T04-3-1: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Packet Based Convergence Layer; Part 3: IEEE 1394 Service Specific Convergence Sublayer (SSCS); Sub-part 1: PICS proforma. | 15/04/ 2001 |
| DTS/BRAN-0024T04-3-2: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Packet Based Convergence Layer; Part 3: IEEE 1394 Service Specific Convergence Sublayer (SSCS); Sub-part 2: TSS & TP | 15/04/ 2001 |
| DTS/BRAN-0024T04-3-3: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Packet Based Convergence Layer; Part 3: IEEE 1394 Service Specific Convergence Sublayer (SSCS); Sub-part 3: ATS | 15/04/ 2001 |
| DTS/BRAN-0024T04-4-1: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Packet Based Convergence Layer; Part 4: IEEE 1394 Bridge Layer; Sub-part 1: PICS proforma. | 15/04/ 2001 |
| DTS/BRAN-0024T04-4-2: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Packet Based Convergence Layer; Part 4: IEEE 1394 Bridge Layer; Sub-part 2: TSS & TP | 15/04/ 2001 |
| DTS/BRAN-0024T04-4-3: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Packet Based Convergence Layer; Part 4: IEEE 1394 Bridge Layer; Sub-part 3: ATS | 15/04/ 2001 |
| RTS/BRAN-002T104-2-1: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Data Link Control (DLC) Layer; Part 1: Basic Functions; Sub-part 1: PICS proforma. | 15/04/ 2001 |
| RTS/BRAN-002T104-2-2: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Data Link Control (DLC) Layer; Part 1: Basic Functions; Sub-part 2: TSS & TP | 15/04/ 2001 |
| RTS/BRAN-002T104-2-3: Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Data Link Control (DLC) Layer; Part 1: Basic Functions; Sub-part 3: ATS | 15/04/ 2001 |

## 3.10	Part of the ETSI Work Programme (EWP) for which the STF is required

The BRAN Project has a number of work items in hand for Interoperability Specifications of H/2. STF support is required for the maintenance and validation of the corresponding Conformance Test Specifications.

The relevant work items to be produced are:

| WI number | Work item title |
| --- | --- |
| RTS/BRAN-002T0B4-2-1 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for Data Link Control (DLC) Layer; Part 2: Radio Link Control (RLC) sublayer; Sub-part 1: Protocol Implementation Conformance Statement (PICS) |
| RTS/BRAN-002T0B4-2-2 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing Data Link Control (DLC) Layer; Part 2: Radio Link Control (RLC) sublayer; Sub-part 2: Test Suite Structure and Test Purposes (TSS & TP) |
| RTS/BRAN-002T0B4-2-3 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for Data Link Control (DLC) Layer; Part 2: Radio Link Control (RLC) sublayer; Sub-part 3: Abstract Test Suite (ATS) (Major Revision) |
| RTS/BRAN-002T0A4-3-1 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Data Link Control Layer (DLC); Part 3: Profile for Business Environment; Sub-part 1: Procotol Conformance Implementation Statement (PICS) proforma |
| RTS/BRAN-002T0A4-3-2 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Data Link Control Layer (DLC); Part 3: Profile for Business Environment; Sub-part 2: Test Suite Structure and Test Purposes (TSS & TP) |
| RTS/BRAN-002T0A4-3-3 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Data Link Control Layer (DLC); Part 3: Profile for Business Environment; Sub-part 3: Abstract Test Suite (ATS) |
| RTS/BRAN-002T0A4-5-1 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Data Link Control Layer (DLC; Part 5: Profile for Home Environment; Sub-part 1: Procotol Conformance Implementation Statement (PICS) proforma |
| RTS/BRAN-002T0A4-5-2 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Data Link Control Layer (DLC); Part 5: Profile for Home Environment; Sub-part 2: Test Suite Structure and Test Purposes (TSS & TP) |
| RTS/BRAN-002T0A4-5-3 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Data Link Control Layer (DLC); Part 5: Profile for Home Environment; Sub-part 3: Abstract Test Suite (ATS) |
| RTS/BRAN-0024TA3-1-1 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Cell based Convergence Layer; Part 1: Common part; Sub-part 1: Procotol Conformance Implementation Statement (PICS) proforma |
| RTS/BRAN-0024TA3-1-2 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Cell based Convergence Layer; Part 1: Common part; Sub-part 2: Test Suite Structure and Test Purposes (TSS & TP) specification |
| RTS/BRAN-0024TA3-1-3 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Cell based convergence Layer; Common part; Sub-part 3: Abstract Test Suite (ATS) |
| RTS/BRAN-0024TA3-2-1 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Cell based Convergence Layer; Part 2: UNI Service Specific Convergence Sublayer (SSCS); Sub-part 1: Procotol Conformance Implementation Statement (PICS) proforma |
| RTS/BRAN-0024TA3-2-2 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Cell based Convergence Layer; Part 2: UNI Service Specific Convergence Sublayer (SSCS); ; Sub-part 2: Test Suite Structure and Test Purposes (TSS & TP) |
| RTS/BRAN-0024TA3-2-3 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Cell based Convergence Layer; Part 2: UNI Service Specific Convergence Sublayer (SSCS); Sub-part 3: Abstract Test Suite (ATS) |
| RTS/BRAN-0024TA4-3-1 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Packet based Convergence Layer; Part 3: IEEE 1394 Service Specific Convergence Sublayer (SSCS); Sub-part 1: Procotol Conformance Implementation Statement (PICS) proforma |
| RTS/BRAN-0024TA4-3-2 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Packet based Convergence Layer; Part 3: IEEE 1394 Service Specific Convergence Sublayer (SSCS); Sub-part 2: Test Suite Structure and Test Purposes (TSS & TP) |
| RTS/BRAN-0024TA4-3-3 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Packet based Convergence Layer; Part 3: IEEE 1394 Service Specific Convergence Sublayer (SSCS); Sub-part 3: Abstract Test Suite (ATS) |
| RTS/BRAN-0024TA4-4-1 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Packet based Convergence Layer; Part 4: IEEE 1394 Bridge Layer; Sub-part 1: Procotol Conformance Implementation Statement (PICS) proforma |
| RTS/BRAN-0024TA4-4-2 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Packet based Convergence Layer; Part 4: IEEE 1394 Bridge Layer; Sub-part 2: Test Suite Structure and Test Purposes (TSS & TP) |
| RTS/BRAN-0024TA4-4-3 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Packet based Convergence Layer; Part 4: IEEE 1394 Bridge Layer; Sub-part 3: Abstract Test Suite (ATS) |
| RTS/BRAN-002T0B4-1-1 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Data Link Control (DLC) Layer; Part 1: Basic Functions; Sub-part 1: Procotol Conformance Implementation Statement (PICS) proforma |
| RTS/BRAN-002T0B4-1-2 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Data Link Control (DLC) Layer; Part 1: Basic Functions; Sub-part 2: Test Suite Structure and Test Purposes (TSS & TP) |
| RTS/BRAN-002T0B4-1-3 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Data Link Control (DLC) Layer; Part 1: Basic Functions; Sub-part 3: Abstract Test Suite (ATS) |
| RTS/BRAN-0024TA4-2-1 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Packet based Convergence Layer; Part 2: Ethernet Service Specific Convergence Sublayer (SSCS); Sub-part 1: Procotol Conformance Implementation Statement (PICS) proforma |
| RTS/BRAN-0024TA4-2-2 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Packet based Convergence Layer; Part 2: Ethernet Service Specific Convergence Sublayer (SSCS); Sub-part 2: Test Suite Structure and Test Purposes (TSS & TP) |
| RTS/BRAN-0024TA4-2-3 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Packet based Convergence Layer; Part 2: Ethernet Service Specific Convergence Sublayer (SSCS); Sub-part 3: Abstract Test Suite (ATS) |
| RTS/BRAN-0024TA4-1-1 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Packet based Convergence Layer; Part 1: Common part; Sub-part 1: Procotol Conformance Implementation Statement (PICS) proforma |
| RTS/BRAN-0024TA4-1-2 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Packet based Convergence Layer; Part 1: Common part; Sub-part 2: Test Suite Structure and Test Purposes (TSS & TP) |
| RTS/BRAN-0024TA4-1-3 | Broadband Radio Access Networks (BRAN); HIPERLAN type 2; Conformance Testing for the Packet based Convergence Layer; Part 1: Common part; Sub-part 3: Abstract Test Suite (ATS) |
| RTS/BRAN-002T0A4-4-1 | Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Data Link Control (DLC) Layer; Part 4: Extension for Home Environment; Sub-part 1: PICS proforma |
| RTS/BRAN-002T0A4-4-2 | Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Data Link Control (DLC) Layer; Part 4: Extension for Home Environment; Sub-part 2: TSS & TP |
| RTS/BRAN-002T0A4-4-3 | Broadband Radio Access Networks (BRAN); High Performance Radio Local Area Networks (HIPERLAN) Type 2; Conformance Testing for the Data Link Control (DLC) Layer; Part 4: Extension for Home Environment; Sub-part 3: Abstract Test Suite (ATS) |

## 3.11	Expected output

The expected output is as follows:

- The revision of PICS, TSS&TP and ATS specifications for all H/2 conformance test specification. The output will be revised editions of the related documents.

|  | PICS | TSS & TP | ATS |
| --- | --- | --- | --- |
| RLC | X | X | X |
| DLC basic | X | X | X |
| DLC home extension | X | X | X |
| DLC business profile | X | X | X |
| DLC home profile | X | X | X |
| Cell based CL common part | X | X | X |
| Cell based CL ATM-UNI service specific part | X | X | X |
| Packet based CL IEEE 1394 SSCS | X | X | X |
| Packet based CL IEEE 1394 Bridge Layer | X | X | X |
| Packet based CL common part | X | X | X |
| Packet based CL (Ethernet SSCS) | X | X | X |

B30(00)07.