|  | ToR STF 418 (TB DECT /WG DECT-NG) |
| --- | --- |
|  | Version: 0.2 |
|  | Author: Dr. Günter Kleindl – Date: 19 October 2010 |
|  | Last updated by: Dr. Günter Kleindl |
|  | page 1 of 7 |

Terms of Reference for Specialist Task Force STF 418 
(TB DECT / WG DECT-NG) on 
”DECT maintenance and NG-DECT development 2011”

Document status

| Status of these ToR | DECT(10)0373 Version 0.1 approved by TC DECT and Board#80 |
| --- | --- |
| Work Items approved | Yes, one new WI: RTS/DECT-NG (TS 102 527-5), the others are carried over from 2010 (extension of STF388) |

# Reasons for proposing the Specialist Task Force (STF)

## Overview of the proposal

### Purpose of the work

The scope of this STF is the maintenance of the basic DECT standard, the maintenance of the NG_DECT specifications developed during the last years and the development of a new NG-DECT specification corresponding to what DECT Forum calls CAT-iq 2.1

The continuous maintenance of the standard is needed due to wide usage of the DECT standard by the industry (installed base > 800 M), the feedback from industry partners and test certification program, and the handling of the many change requests received from the members.

The requirements for the new CAT-iq specification have been provided by DECT Forum, and have been coordinated with HGI (Home Gateway Initiative), since it is believed that it will be implemented embedded in home gateways/ADSL routers in a similar way to WIFI radios today.

The STF outcome will be materialized in the short term on real products that will be sold in large scale, and that will provide tangible practical benefits to the end users.

The documents should be ready for TB approval in December 2011 or before.

### Relation with the ETSI strategic objectives

DECT is one of the most important ETSI standards in terms of public acceptance. The standard provides a convenient solution to the needs of cordless telecommunications in the business, residential and WLL scenarios. DECT dominates the voice cordless market with an installed base of 800 M of devices.

DECT is, by far, the most successful European Standard in the field of unlicensed radio communications.

The work on DECT New Generation has attracted new ETSI members. It is also related to the ETSI Green Agenda.

### Market impact, benefits to be gained

The DECT specification from ETSI is the world-wide leading standard for digital cordless telecommunications. There are more than 800 million devices in the market and every year more than 100 million devices are sold. In the last 2 years DECT has also become the number one in the US. Recently the introduction of DECT in Japan has been approved.

Despite this great success, there is continuing threat from other systems, to take over market shares from DECT and without continuous development and permanent improvements, DECT would quickly disappear.

### Interest of ETSI Members and other stakeholders

The DECT manufacturers including the chip manufacturers have come to the conclusion, that the market requires a new generation of DECT products. The DECT Forum has approached TC DECT to develop the specification for new generation DECT products, based on the market requirements as provided by DECT Forum. They also stressed the urgency of the work and therefore we agreed to develop the specification in phases. For the integration of NG-DECT products into home-gateways a higher level of interoperable features is required by the operators. The new generation DECT provides not only an increase of the quantity of products, but also of the value of the DECT products. DECT Forum is also launching a certification programme. Due to new requirements from the DECT Forum an additional part of the NG-DECT specifications is necessary.

ETSI members who support the STF work are AVM, DSPG, FEEI, France Telecom, Gigaset Communications, Lantiq, Panasonic, RTX and Sitel Semiconductor.

### Relation with other activities within ETSI and/or related organizations

We have a close cooperation with some of the other ETSI groups like SAGE, who support us to improve the DECT security features and TC STQ, who support us in regard of the speech transmission aspects including testing. We also cooperate with ITU in the area of IMT, where we regularly provide the updated DECT specifications for inclusion in the relevant ITU Recommendations.

There is a complementary activity within the DECT Forum, who has established a marketing group for NG DECT to provide market requirements to TC DECT. DECT Forum is also promoting the NG DECT technology in cooperation with the ETSI secretariat.

### Priority within the TB

Highest priority

### Motivation why the work cannot be performed within the TB

The DECT Forum has expressed an urgent need for the completion of the specifications and with the support of an STF expert a high quality standard can be produced much more rapidly.

The support of an STF is essential for the timely production of the standards and the seamless continuation of the DECT success story.

### Support from ETSI Members

The following ETSI Members support the creation of an STF to produce the deliverables listed in this document:

- AVM	Mathias Frey, Sven Trevisany

- BMWi	Bernd Wolf

- DSPG	Jochen Kilian, Ziv Galmor, Heinz Thürauf

- FEEI	Günter Kleindl

- France Telecom	Laurent Clarimon, Aymeric de Solages

- Gigaset Communications	Dieter Kehren, Andreas Müller

- Lantiq	Stefan Kluwe

- Panasonic	Hans-Peter Steinbrück

- RTX Telecom	Arne Henriksen

- Sitel Semiconductor	Oliver Maiwald

- Wireless Partners SLL	Angel Boveda

Motivation for the support is the increase of the DECT business by enhancing the system and adding new features to the products.

## Organization of the work

### Identification of tasks, phases, priorities, technical risk

- Update of the DECT Common Interface standard EN 300 175 parts 1 to 8 (basic DECT library):  Because of change requests received from the industry, feedback from the product testing activities and from the market, enhancement of security features, addition of new features and because of the cross interaction with other specifications an update of such specifications is necessary.

- Update of the DECT New Generation part 1 (TS 102 527-1) specification: Because of feedback from the product testing activities and from the market, addition of new features and because of the cross interaction with other specifications an update of such specifications is necessary.

- Update of the DECT New Generation part 3 (TS 102 527-3) specification: Because of feedback from the product testing activities and from the market, addition of new features and because of the cross interaction with other specifications an update of such specifications is necessary.

- Update of the DECT Generic Access Profile (GAP) EN 300 444 specification: Because of feedback from the product testing activities and from the market, enhancement of security features, addition of new features and because of the cross interaction with other specifications an update of such specifications is necessary.

- Creation of a new Technical Specification NG-DECT Part 5, defining additional features for DECT New Generation including energy saving: The new features are described in a requirements document from the DECT Forum.

### Outcome of the STF

The work consists of the following major activities:

- Creation of a new revision of the DECT Common Interface standard EN 300 175 parts 1 to 8

- Creation of a new revision of the DECT New Generation part 1 (TS 102 527-1) specification

- Creation of a new revision of the DECT New Generation part 3 (TS 102 527-3) specification

- Creation of a new revision of the DECT Generic Access Profile (GAP) EN 300 444 specification

- Creation of the new specification for NG-DECT (CAT-iq 2.1) release (TS 102 527-5)

# Consequences if not agreed:

The DECT Forum has asked ETSI to produce the specifications for ‘New Generation DECT’ as fast as possible in order to be able to quickly develop a standardized solution and to ensure that the DECT technology continues to hold the top market position in the cordless domain. There is strong competition from other technologies, e.g. WLAN and PHS, and any delay of the introduction of ‘New Generation DECT’ products will hurt the DECT industry. The support of an STF is essential for the timely production of the standards and the seamless continuation of the DECT success story.

The update of all specifications is also essential for the NG-DECT certification program and for timely introduction of NG-DECT certified products.

# Detailed description:

## Subject title:

DECT-update and NG-DECT development 2011

## Reference Technical Body:

TB DECT and WG DECT New Generation

## Other interested TBs:

ETSI SAGE regarding the security enhancements, ETSI TC STQ regarding the speech quality aspects, ITU-R WP5D regarding the contributions for the IMT Recommendations, DECT Forum regarding the feature definition for release 2011; DECT Forum regarding the test specification and the NG-DECT certification program.

## Steering Committee

The steering is done by TC DECT, during the meetings and phone conferences and in between via the e-mail list. The Steering Group is led by the TC DECT chairman.

## Target date for the start of work:

January 2011

## Duration and target date for the conclusion of the work (TB approval):

TB approval is planned December 2011 or before according to detailed plan.

## Resources required

### Experts manpower

Total manpower required: 150 working days

### Travel cost:

2 000 €, expected, to attend the reference TB/WG, Steering Group meetings (3 travels)

Note: The travel cost is for travels to meetings other than the normal STF sessions, for which the travel cost is already included in the contractual compensation of the manpower.

## Experts qualification required, mix of skills

The following experts are required to perform the work.  The actual number of experts and mix of skills may depend on the actual applications received and will be decided when setting up the STF.

- Relevant expertise required: authority expert in DECT technology, with in-depth knowledge of all layers. The background of the candidates should include proven experience in the field in the DECT industry or research institutes,

- Familiar with protocol specification, ETSI methodology and working procedures.

- Period over which the experts are required and duration of the secondment: 1 year.

## Scope of Terms of Reference:

The work consists of 5 major activities:

- Creation of a new revision of the DECT Common Interface standard EN 300 175 parts 1 to 8

- Creation of a new revision of the DECT New Generation part 1 (TS 102 527-1) specification

- Creation of a new revision of the DECT New Generation part 3 (TS 102 527-3) specification

- Creation of a new revision of the DECT Generic Access Profile (GAP) EN 300 444 specification

- Creation of the new NG-DECT specification for CAT-iq 2.1 release

## Organization of the work in tasks and/or phases:

The work on all tasks will be done in parallel.

## Validation

No protocol test specifications are directly developed as part of the tasks of this STF. However  all specifications are linked to DECT testing standards that are implemented by test companies and used by the DECT Forum certification program. Therefore all specifications will be indirectly validated.

## Related activity in other bodies and co-ordination schedule

We have already received the relevant information from SAGE, TC STQ and DECT Forum to start the work.

## Base documents and their availability

The STF work will be based upon the following documents:

| Work Item | Title | Current Status | Date TB approval |
| --- | --- | --- | --- |
| REN/DECT-000254-1 to 8 | Base standard parts 1 to 8 | published |  |
| REN/DECT-000255 | Generic Access Profile | published |  |
| RTS/DECT-NG0254 | New Gen DECT; part 1 | published |  |
| RTS/DECT-NG0257-3 | New Gen DECT; part 3 | stable draft | Nov 2010 |

## Work Items to be produced by the STF

The STF will produce the following deliverables, for TB approval:

- RTS/DECT-00257 … 264 (EN 300 175 parts 1 to 8)	
Title: DECT: Common Interface, parts 1 to 8

Scope: Maintenance due to change requests received from the industry, feedback from the product testing activities and from the market, enhancement of security features, addition of new features and because of the cross interaction with other specifications Work Item approved by TB DECT (Oct 2009)

- RTS/DECT-00256 (EN 300 444)	
Title: DECT Generic Access Profile (GAP)

Scope: Maintenance due to test specification and feedback received from DECT Forum certification program.	
Work Item approved by TB DECT (Oct 2009)

- DTS/DECT-NG00259-5 (TS 102 527-5)	
Title: DECT New Generation Part 5: Additional feature set

Scope: To create a new NG-DECt specification for CAT-iq 2.1 defining additional features for NG DECT such as: Phone book handling, Answering machine control, Handset Capability Enquiry, Security Enhancements, ECO mode.	
Work Item approved by TB DECT (Sept 2009)

- RTS/DECT-NG0260 (TS 102 527-1)	
Title: DECT New Generation Part 1: NG DECT Wideband speech

Scope: Maintenance of the wideband speech specification for New Generation DECT. Enhancement of security.	
Work Item approved by TB DECT (2009-10-07)

- RTS/DECT-NG0265 (TS 102 527-3)
Title: DECT New Generation Part 3: NG DECT extended

Scope: Maintenance due to test specification and feedback received from implementation.	
Work Item approved by TB DECT (2010-10-07)

## Planned output schedule:

The STF will produce the deliverables according to the following time scale:

EN 300 175 parts 1 to 8

Work Item(s): REN/DECT-0257 to 264

- Start of the work 	Feb/2010

- First stable draft for WG review	Apr/2011

- Draft for WG approval	Jun/2011

- WG approval	Jun/2011

- Draft for TB approval	Jun/2011

- TB approval	Jun/2011

- Publication	Dec/2011

EN 300 444

Work Item(s): REN/DECT-0256

- Start of the work 	Oct/2009

- First stable draft for WG review	Jun/2011

- Draft for WG approval	Sep/2011

- WG approval	Sep/2011

- Draft for TB approval	Sep/2011

- TB approval	Sep/2011

- Publication	Mar/2012

TS 102 527-1

Work Item(s): RTS/DECT-NG0260

- Start of the work 	Oct/2009

- First stable draft for WG review	Jun/2011

- Draft for WG approval	Sep/2011

- WG approval	Sep/2011

- Draft for TB approval	Sep/2011

- TB approval	Sep/2011

- Publication	Nov/2011

TS 102 527-3

Work Item(s): RTS/DECT-NG0265

- Start of the work 	Jan/2011

- First stable draft for WG review	Oct/2011

- Draft for WG approval	Dec/2011

- WG approval	Dec/2011

- Draft for TB approval	Dec/2011

- TB approval	Dec/2011

- Publication	Feb/2012

TS 102 527-5

Work Item(s): DTS/DECT-NG0259

- Start of the work 	April/2010

- First stable draft for WG review	Mar/2011

- Draft for WG approval	Jun/2011

- WG approval	Jun/2011

- Draft for TB approval	Jun/2011

- TB approval	Jun/2011

- Publication	Aug/2011

In addition, the STF will produce the following reports:

- Progress Report#1	Feb/2011	TB DECT#45

- Progress Report#2	Apr/2011	TB DECT#46

- Progress Report#3	Jul/2011 	TB DECT#47

- Progress Report#4	Oct/2011	TB DECT#48

- Final Report 	Dec/2011

# Performance indicators

TC DECT proposes as performance indicator of the STF the real usage of the produced standard by the industry and end-users.

After the conclusion of the STF, the TB shall report to the OCG/Board on the actual achievement of the objectives set in the proposal.  This information will be used to assess further requests from the same reference TB.

Other performance indicators:

- Interest from stakeholders other than ETSI Members

  - Stakeholder representation in the project (e.g. category, business area)

  - Potential interest of new members to join ETSI

  - Contribution to other standardization bodies

  - Liaison with industry to identify requirements and raise awareness on the project deliverables

  - Comments received on drafts (e.g. on the WEB site, on mailing lists, etc.)

  - Liaison activities performed by the STF (e.g. workshops/Plugtests/conferences/events)

- Quality of deliverables

  - Approval of deliverables from the Reference TB according to schedule

  - Respect of time scale, with reference to start/end dates in the approved ToR

  - Application of the ETSI drafting rules

  - Interim and Final Report approved by the EC/EFTA (if applicable)

# Document history

| Version | Date | Author | Status | Comments |
| --- | --- | --- | --- | --- |
| 0.0 | 6 Oct 10 | Kleindl | Draft for review | Created by TC DECT at DECT#43 meeting |
| 0.1 | 7 Oct 10 | Kleindl | approved | TC DECT approved |
| 0.2 | 19 Oct 10 | Kleindl | Approved Board#80 | Member support updated, WI editorial check |