|  | ToR STF 452 (TC ITS WG5) |
| --- | --- |
|  | Version: 0.5 |
|  | Author: ITS WG5 / ETSI CTI – Date: 24 April 2012 |
|  | Last updated by Alberto Berrini – Date: 17 October 2012 |
|  | page 1 of 7 |

Terms of Reference for Specialist Task Force STF 452 
(ITS WG5)
”Extension of ITS Conformance Validation Framework with Security Test Specifications of TS 102 867 and TS 102 941”

Summary information

| Status of these ToR | WP1, WP2 approved by ITS#10 [ITS(12)000088] Funding for WP1 approved by Board#88 Funding for WP2 approved by Board#90 (15-Nov) |
| --- | --- |
| Work Items | DTS/ITS-0050019, DTS/ITS-0050020, DTS/ITS-0050021 and DTR/ITS-0050022 approved at ITS#10, 26 – 27 April 2012 |
| Funding required | WP1 – testing (in course) 94 800 € Budget 2012 WP2 - Validation (current proposal) 70 000 € Budget 2013 Total project cost 168 000 € Voluntary contribution proposed ≈ 27% of total. |
| Funding criteria B(12)88_030 | 4. Standards enablers/facilitators (e.g. conformance test/interoperability) 5) horizontal activities (quality) |
| Notes from Secretariat | WP1 started end-Sep. Strong participation from industry, under CTI leadership. Actual resources required will be reviewed in Feb-2013. Possible budget adjustment may be requested to Board#91. |

# Reasons for proposing the Specialist Task Force (STF)

ITS protocols have been specified and designed to operate correctly across a wide variety of infrastructures worldwide. The risk profile for ITS systems indicates a high impact of these protocols if their design includes a widespread error or fault. This issue provides evidence that successful testing and interoperability are key factors that enable the deployment of these technologies and their successful global introduction.

The provisioning of security testing and compliance scenarios for ITS applications is essential and allows ETSI to maintain its leadership in present and future ITS technology

The proposed STF improves the quality of the base specifications for ITS Security profiles. A change request mechanism will be put in place to allow the timely feedback on revealed bugs and inconsistencies of base specifications into the TC ITS standardization process, and thus achieve optimized base specifications.

## Overview of the proposal

### Purpose of the work

The purpose of the work is to assure interoperability of devices produced in compliance with the TS 102 867 and TS 102 941 standards. This particular work is to produce the Protocol Implementation Conformance Statement (PICS), the Test Suite Structure and Test Purposes (TSS&TP), the Abstract Test Suite (ATS) and Protocol Implementation eXtra Information for Testing (PIXIT), and to provide an executable test suite (ETS) integrated with the existing ITS Conformance Validation Framework.

### Relation with the ETSI strategic objectives

This STF will address the interoperability issues related to security.

### Market impact, benefits to be gained

The ITS Conformance Validation Framework is a reference test implementation available to all players in the ITS market. It allows to assess the level of compliance of implementations and to validate the understanding of the ITS base specifications. The availability of the security extension is essential for market as it allows to cover tests which make sure that safety-critical ITS implementations perform in ad-hoc networks in a secure and reliable manner.

### Interest of ETSI Members and other stakeholders

The work is supported by TC ITS member companies.

### Relation with other activities within ETSI and/or related organizations

The STF will be interacting with the responsible TB, i.e. TC ITS WG5 and the related TBs such as WG1 and WG3.

It is planned to demonstrate and make live tests of the ITS Conformance Validation Framework during an ITS Plugtests event in 2013. The goal is to show to the participants the importance of the conformance testing to enable interoperable implementations as well as the benefits of the conformance testing for enhancing the quality of their products.

### Priority within the TB

High.

### Motivation why the work cannot be performed within the TB

Experience with the development of other standards has shown that involvement of experts on conformance and interoperability testing of protocols requires highly specialised knowledge in testing methodology. The generation of this kind of specifications requires significant concentrated effort that can be done in this case by experts provided on a funded basis. Hence the involvement of testing experts is needed in order to assure timely completion and high quality of the Test Specifications. The experts will use dedicated software tools available at ETSI.

To complement the effort, security experts are required to ensure that all implementation requirements are fully covered by the test specifications.

### Support from ETSI Members

The following ETSI Members support the creation of an STF to produce the deliverables listed in §3.14:

Cadzow Communications	Scott Cadzow /ITS WG 5 chair/monitor

PQM Consultants	Steve Randall

Lecit Consulting s.r.l.	Fausto Caneschi

CCSR	Haitham Cruickshank

RENAULT 	Brigitte LONC

Robert Bosch 	Benjamin Glas

NXP semiconductors 	Timo van Roermund

The ETSI Members supporting the creation of the STF are prepared to provide the following voluntary contribution:

Members are prepared to review the produced deliverables

Members are prepared to monitor questions on base standards (questions on base standards are recorded in Mantis)

## Organization of the work

### Identification of tasks, phases, priorities, technical risk

The work shall be split in 2 phases, a development phase and a validation phase. In the validation phase PICS, TSS&TP and ATS&PIXIT shall be developed. In the validation phase the ETS shall be developed and validated against some implementations.

In order to harmonize efforts between Europe, US and Japan and the different stakeholders in the field, it is proposed, as part of phase 1, to review existing test programmes and test plans in order to determine the correct test coverage. Furthermore it is proposed to liaise with the existing test programmes so as to achieve mutual feedback on test strategy and test methodology.

### Outcome of the STF

To produce for TS 102 867 and TS 102 941: PICS, TSS&TP, ATS&PIXIT test specifications, and to provide an ETS integrated with the existing ITS Conformance Validation Framework.

# Consequences if not agreed:

The production of test specifications as described in the present document is key to the testing and certification activities that should assure the interoperability of ITS equipment. Such devices are required to have high levels of interoperability if the safety is to be kept at the highest level. Without the availability of such standards the deployment of Cooperative ITS equipment according to the Roadmap to a Single European Transport Area cannot be achieved.

# Detailed description:

## Subject title:

Extension of ITS Conformance Validation Framework with Security Test Specifications of TS 102 867 and TS 102 941.

## Reference Technical Body:

TC ITS and TC ITS WG5 will be responsible for the approval of all the deliverables of this STF.

## Other interested TBs:

TC ITS WG1, TC ITS WG3

## Steering Committee

TC ITS WG5 will monitor the progress through the WG5 chairman, and no steering committee is planned. Interim results should be made public to identified ITS stakeholders.

## Target date for the start of work:

It is planned to start the STF by latest September 2012.

## Duration and target date for the conclusion of the work (TB approval):

The duration of the work is planned to be up to 10 months. The target is that the STF completes the work by end of Q2 2013.

## Resources required

### Experts manpower

Expert manpower resources required for WP1: 160 working days for drafting deliverables of which 32 working days will be voluntary contribution.

CTI resource is required for WP1: 40 working days for project management and technical work funded from the ETSI STF budget of which 25 working days will be voluntary contribution.

Expert manpower resources required for WP2: 120 working days for validation of which 20 working days will be voluntary contribution.

CTI resource is required for WP2: 25 working days for project management and technical work funded from the ETSI STF budget of which 15 working days will be voluntary contribution.

The total manpower budget is

WP1 92 800 €

128 remunerated working days experts (76 800 €)

15 remunerated working days CTI (16 000 €)

Voluntary contribution 57 working days (32 experts + 25 CTI) vs. 200 total =28,5 %

WP2 66 000 €

100 remunerated working days experts (60 000 €)

10 remunerated working days CTI (6 000 €)

Voluntary contribution 35 working days (20 experts + 15 CTI) vs. 145 total = 24%

Total manpower cost for the project: 162 000 €

Table 1: Assignment of days per task

| WP1 Development of test specifications |
| --- |
| # | Task Name | Funded Expert | CTI |
| T1 | Project Management | - | 15 |
| T2 | Kickoff meeting/Review of existing test plans | 10 | 5 |
| T3 | Identification of implementation requirements | 20 | - |
| T4 | PICS proforma | 10 | - |
| T5 | TSS&TP | 50 | 10 |
| T6 | ATS&PIXIT | 70 | 10 |
| Totals | 160 | 40 |

Table 2: Assignment of days per task

| WP2 Validation of test specifications |
| --- |
| # | Task Name | Funded Expert | CTI |
| T7 | Adaptation layers | 35 | 10 |
| T8 | Codec | 20 | - |
| T9 | Execution of tests against real implementations | 45 | 5 |
| T10 | Feedback on test specifications | 5 | 5 |
| T11 | Validation report | 15 | 5 |
| Totals | 120 | 25 |

### Travel cost:

Expected travel cost: 6 000 EUR.

Travel to at least 4 ITS TC and WG meetings

Travels to potential Plugtests®

meetings to consult with ITS stakeholders on interim results 
(e.g. Car to Car Communications Consortium)

## Experts qualification required, mix of skills

In-depth knowledge of IEEE 1609.2,

Expertise in protocol and conformance test specification, software to produce test suites,

Expertise in test strategy, test systems, conformance testing specifications,

Expertise in TTCN-3 language development and validation,

Standardisation.

The following experts are required to perform the work.  The actual number of experts and mix of skills may depend on the actual applications received and will be decided when setting up the STF.

Number of experts required: 3 – 4. In addition support from CTI is required

Period over which the experts are required: Sept 2012 – Q1/Q2 2013

It is essential to include in the STF team 1 or 2 companies which are active in the field of security testing

Type of secondment: part time, remote work is possible

For the validation task it is essential to get support from companies in form of security implementations which can be used to validate the ETS

## Scope of Terms of Reference:

To produce Security Test Specifications of TS 102 867 and TS 102 941 and to integrate and validate these test specifications with the existing ITS Conformance Validation Framework.

## Task/phases planning:

WP1 Development of test specifications

Kickoff meeting

Identification of implementation requirements/Review of existing test plans

PICS proforma

TSS&TP

ATS&PIXIT

WP2 Validation of test specifications

Codec and integration with ITS Conformance Validation Framework

Upper Tester and integration with ITS Conformance Validation Framework

Test Adapter and integration with ITS Conformance Validation Framework

Execution of tests against real implementations

## Validation

This STF will provide level 2 validation as shown in the table below. The ITS Conformance Validation Framework shall be validated against a minimum of at least 2 SUTs (= software implementation of ETSI profile of IEEE 1609.2). These SUTs need to be available and installed on computers at ETSI premises. The responsibilities shown in the table below shall be shared by the STF team. In addition and beyond the STF effort, it is expected to get documentation and support from the company providing the SUTs on any issues that may arise. This support shall be limited to reasonable effort.

Table 3: Responsibilities of validation

| Strong Validation (Level 2) |
| --- |
| Basic Validation (Level 1) |  |
| Provision of TTCN-3 analyser/compilers |  |
| Compilation of the test suite on at least 3 TTCN-3 compilers |  |
| Reporting of errors in the tools |  |
| Reporting of errors in the ATS |  |
| Updating of ATS |  |
| Compilation of validation report |  |
|  | Extending and maintaining of the ITS Conformance Validation Framework |
|  | Provision and installation of SUT(s) |
|  | Execution of the tests |
|  | Reporting of errors in the ITS Conformance Validation Framework |
|  | Validation of test verdicts |

The cost for validation is included in the overall total of section 3.7 of these ToR.

## Related activity in other bodies and co-ordination schedule

The STF will be interacting with the responsible TB, i.e., TC ITS WG5 working group and TC ITS.

## Base documents and their availability

The STF work will be based upon the following documents:

| Work Item | Title | Current Status | Date TB approval |
| --- | --- | --- | --- |
| DTS/ITS-0050013 TS 102 867 | Stage 3 mapping for IEEE 1609.2 | Available | April 2012 |
| DTS/ITS-0050015 TS 102 941 | Trust and Privacy Management | Available | April 2012 |

## Work Items to be produced by the STF

The STF will produce the following deliverables, for TB approval:

DTS/ITS-0050021

Title: Intelligent Transport System (ITS); Testing; Conformance test specification for TS 102 867 and TS 102 941; - Part 1: Test requirements and Protocol Implementation Conformance Statement (PICS) proforma

Scope: Provide the Test Suite Structure and Test Plans to be used to test the ITS use of IEEE 1609.2 messages and data structures defined in TS 102 867 and TS 102 941
Work Item to be approved by TC ITS#10 (26 – 27 April)

DTS/ITS-0050019

Title: Intelligent Transport System (ITS); Testing; Conformance test specification for TS 102 867 and TS 102 941; - Part 2: Test Suite Structure and Test Purposes (TSS&TP)

Scope: Provide the Test Suite Structure and Test Plans to be used to test the ITS use of IEEE 1609.2 messages and data structures defined in TS 102 867 and TS 102 941
Work Item to be approved by TC ITS#10 (26 – 27 April)

DTS/ITS-0050020

Title: Intelligent Transport System (ITS); Testing; Conformance test specification for TS 102 867 and TS 102 941; - Part 3: Abstract Test Suite (ATS) and Protocol Implementation eXtra Information for Testing (PIXIT)

Scope: Test cases for testing of TS 102 867 and TS 102 941

Work Item to be approved by TC ITS#10 (26 – 27 April)

DTR/ITS-0050022

Title: Intelligent Transport Systems (ITS); Security; Conformance testing validation report

This task will run the prototype test system against real equipment and will therefore validate the related test specifications and base specifications. All revealed bugs and inconsistencies of base specifications and test specifications will be reported.

Scope: Provides the validation report from the tests of ITS use of IEEE 1609.2 messages and data structures defined in TS 102 867 and TS 102 941

Work Item to be approved by TC ITS#10 (26 – 27 April)

## Planned output schedule:

The STF will produce the deliverables according to the following time scale:

Work Item(s): DTS/ITS-0050019 , DTS/ITS-0050020 ,  DTS/ITS-0050021

Start of the work 	Sept 2012

ToC and scope 	Sept 2012

First stable draft for WG review	Oct 2012	TC ITSWG5#25

Draft for WG approval	Jan 2013

WG approval	April 2013		TC ITSWG5#27

Draft for TB approval	May 2013

TB approval	June 2013		RC

Publication	Aug 2013

Validation Report DTR/ITS-0050022

Start of the work 	Dec 2012

ToC and scope 	Dec 2012

First stable draft for WG review	Jan 2013	TC ITSWG5#26

Draft for WG approval	Apr 2012

WG approval	June 2013		TC ITSWG5#28

Draft for TB approval	July 2013

TB approval	July 2013		RC

Publication	Aug 2013

In addition, the STF will produce the following reports:

Progress Report#1	Oct 2012	TC ITSWG5#25

Progress Report#2	Jan 2013	TC ITSWG5#26
(review conclusion of WP1 and planning WP2)

Progress Report#3	Apr 2013	TC ITSWG5#27

Final Report 	June 2013	TC ITSWG5#28

# Performance indicators

Contribution from the ETSI Members

  - Voluntary work of experts provided free of charge in form of review of the test specifications

Interest from stakeholders other than ETSI Members

  - Liaison activities performed by the STF (e.g. workshops/Plugtests/conferences/events)

Quality of deliverables

  - Approval of deliverables from the Reference TB according to schedule

  - Respect of time scale, with reference to start/end dates in the approved ToR

  - Application of the ETSI drafting rules

# Document history

| Version | Date | Author | Status | Comments |
| --- | --- | --- | --- | --- |
| 0.1 | 3 April | ITS WG5 | To be TB approved |  |
| 0.2 | 18 April | ETSI CTI | To be TB approved |  |
| 0.3 | 24 April | ETSI CTI | To be TB approved | Updated at the ITS WG5#23 |
| 0.4 | 21 May 12 |  |  |  |
| 0.5 | 17 Oct 12 | Berrini | For Board approval WP2 |  |