# Terms of Reference for STF 163 (SPAN13) on
Conformance test specifications for additional B-ISDN capabilities and AAL2 signalling

# 1	Reasons for proposing the STF

1) To upgrade B-ISDN basic call conformance test specifications and to prepare the B-ISDN SVP signalling conformance test specifications and 2) to prepare conformance test specifications for the B-ISDN additional capabilities 3) to prepare conformance test specifications for the B-ISDN AAL2 signalling noting the following:

-	the need for conformance test specifications in B-ISDN network infrastructure;

-	the existence of a basic call model created by STF87;

-	the existence of protocol and test specifications for modification procedures for PCR

-	the existence of STF for DSS2 basic call control and modification for PCR test specifications

-	the need for specialised equipment and programs which are not available to voluntary experts in the normal course of their work.

# 2	Consequences if not agreed

Conformance test specifications can only be provided at a much later date, requiring implementations to be developed in the absence of a harmonised conformance testing specification. This will result in a higher probability of inconsistent implementations within Europe.

Absence of conformance testing specifications will force implementers and service providers to develop their own interim solutions, diverting resource from completing implementations, implementing and verifying test standards produced up to now and delaying presence of implementations of the standard in the field.

Producing own interim solutions by each implementer and service provider would result a more expensive solution than using centralised resources on a European level.

# 3	Detailed description

## 3.1	Subject title

Conformance test specifications for additional B-ISDN capabilities and AAL2 signalling

## 3.2	Reference TB

SPAN, MTS, EASI, MCC.

## 3.3	Other interested TBs (if any)

MTS, EASI.

## 3.4	Duration

The STF should complete the deliverables for approval for public enquiry in 15 months from the start date. STF resources should be available for resolution of public enquiry comments.

## 3.5	Target date for the start of work

March 2000.

## 3.6	Necessary manpower (expertise, mix of skills and amount)

### 3.6.1	Necessary manpower

Total resources required: 11 man months, with justification, split as follows:

- for drafting deliverables: 9,75 man months (including 1 mm for 3 PICS)

- for drafting non-published documents: none

- for attending Technical Body and WG meetings: 0,5 man months

- for general technical support of the Technical Body and its WGs: none

- for technical support of the Technical Body officials: none

- for other tasks: 0,75 man months (for preparing summary on PE comments and handling resolution results)

### 3.6.2	Estimated costs, additional to the manpower:

Total additional cost 7.0 kEUROs, split as follows:

- travelling costs to the Technical Body and WG meetings: 7 000 EURO

- other costs directly related to the STF expert(s): none.

### 3.6.3	Qualification required, mix of skills

- number of experts required: 2 - 3

- relevant expertise required: Candidates ideally should be familiar with the work of existing WG SPS5 STFs active in conformance testing, especially which are producing DSS2 test specifications (STF87, STF125, STF135 etc.). Increasingly, it is necessary to take advantage of tools for automatically generating conformance testing specifications, based on a formal definition of the base specification, and a knowledge of these tools would be an advantage. In the absence of the above, consideration will be given to a mix of experts with a knowledge of developing specifications in TTCN and of the protocol as specified by ETSI SPS5.

- Experts are required part time distributed over the period of 9 months, with 5 man days left for pre- and post-resolution.

## 3.7	Context of the task(s)

The STF has to produce textual TSS & TP parts of standards in Word for Windows for the user and the network sides of the interface based on reference documents in 3.10. The STF has to produce also ATS & partial PIXIT parts of standards. An ATS & partial PIXIT consists of a textual document part and a partial PIXIT part produced in Word for Windows and a TTCN part produced in a TTCN editor. ETSI uses ITEX as the official TTCN editor. The TTCN part of an ATS has to be syntax-checked before contribution.

## 3.8	Related activities in other bodies and necessary co-ordination of schedules

1) WG SPS5 are producing conformance testing specifications using voluntary expertise and a number of STFs, and the style of the deliverables and method of testing should be consistent with this work.

The work will be liaised with the work of the ATM forum Testing group, and the work will be performed in co-operation with that group. This will ensure the maximum performance from the available world wide conformance testing experts. Results of this STF will be contributed to ITU-T SG11. The first version of the ETSI DSS2 basic call test standard, which is built on the base text and Amendment 1 of the protocol is being endorsed by ITU-T. ITU-T meantime accepted two further amendments to the protocol and prepares a third one to be approved in July 1999. Incorporating them into the ETSI version of the protocol necessitates the upgrade of existing test specifications as well.

2) WG SPS5 are producing conformance testing specifications using voluntary expertise and a number of STFs, and the style of the deliverables and method of testing should be consistent with this work.

The work will be liased with the work of the ATM forum Testing group, and the work will be performed in co-operation with that group. This will ensure the maximum performance from the available world-wide conformance testing experts.

Results of the AAL2 work will be contributed to ITU-T SG11 as no other test suite of the kind currently exists (other ETSI DSS2 test standards are being endorsed by ITU-T).

## 3.9	Scope of the terms of reference and relevant work items

1) To upgrade the existing conformance test specifications for DSS2 basic call based on Amendments and comments from members and to prepare conformance test specifications for switched virtual path capability, using the documents listed in 3.10 and to provide the documents listed in 3.11.

2) To prepare conformance test specifications for additional capabilities for B-ISDN CS2 (DSS2 modification procedures for SCR), using the documents listed in 3.10 and to provide the documents listed in 3.11.

3) To prepare conformance test specifications for DSS2 AAL2 signalling capability, using the documents listed in 3.10 and to provide the documents listed in 3.11.

## 3.10	Reference specification(s) and existing documents, including ETSI member contributions

ETR 212	ICS proforma style guide

ETR 266	Test purpose style guide

ETS 300 406	Protocol and profile conformance testing specifications; standardisation methodology

REN/SPAN-05xxx-1	DSS2 basic call, Protocol specification (ITU Q29/31)

DEN/SPS-05149-3	DSS2 basic call, TSS&TP for the user, 1st version

DEN/SPS-05149-4	DSS2 basic call, ATS for the user, 1st version

DEN/SPS-05025-5	DSS2 basic call, TSS&TP for the network, 1st version

DEN/SPS-05025-6	DSS2 basic call, ATS for the network, 1st version

DEN/SPS-05175-1	DSS2 SVP, Protocol specification

DEN/SPS-05175-2	DSS2 SVP, PICS proforma

DEN/SPS-05147-1	Modification procedures for SCR; Protocol specification

DEN/SPS-05147-2	Modification procedures for SCR; PICS proforma

DEN/SPAN-05202-1	Modification of ATD with negotiation; Protocol specification

DEN/SPS-05211-1	DSS2 AAL2 bearer signalling, Protocol specification

Other additional capabilities for B-ISDN CS2 documents may need to be referenced if the resources exist for providing other deliverables, see 3.11 below.

## 3.11	Work item(s) from the ETSI work programme (EWP) for which the STF is required

REN/SPAN-130143-2		DSS2 basic call, PICS pro-forma (ITU Q29/31)

REN/SPAN-130254-3	DSS2 basic call, TSS&TP for the user, 2nd version

REN/SPAN-130254-4	DSS2 basic call, ATS for the user, 2nd version

REN/SPAN-130254-5	DSS2 basic call, TSS&TP for the network, 2nd version

REN/SPAN-130254-6	DSS2 basic call, ATS for the network, 2nd version

DEN/SPAN-130175-3	DSS2 SVP, TSS&TP for the user

DEN/SPAN-130175-4	DSS2 SVP, ATS for the user

DEN/SPAN-130175-5	DSS2 SVP, TSS&TP for the network

DEN/SPAN-130175-6	DSS2 SVP, ATS for the network

DEN/SPAN-130239-3	Modification procedures for SCR; TSS&TP user

DEN/SPAN-130239-4	Modification procedures for SCR; ATS & PIXIT user

DEN/SPAN-130239-5	Modification procedures for SCR; TSS&TP network

DEN/SPAN-130239-6	Modification procedures for SCR; ATS & PIXIT network

DEN/SPAN-130202-2	Modification of ATD with negotiation; PICS proforma

DEN/SPAN-130202-3	Modification of ATD with negotiation; TSS&TP user

DEN/SPAN-130202-4	Modification of ATD with negotiation; ATS & PIXIT user

DEN/SPAN-130202-5	Modification of ATD with negotiation; TSS&TP network

DEN/SPAN-130202-6	Modification of ATD with negotiation; ATS & PIXIT network

DEN/SPAN-130211-2		DSS2 AAL2 bearer signalling, PICS proforma

DEN/SPAN-130211-3	DSS2 AAL2 bearer signalling,, TSS&TP for the user

DEN/SPAN-130211-4	DSS2 AAL2 bearer signalling,, ATS for the user

Other deliverables may be provided based on future work on the base specifications. These will be deliverables within the scope of this STF and based on development of ETSI protocol specification deliverables.

## 3.12	Expected outputs

Deliverables as listed in 3.11. A schedule will be proposed at the start of the STF, according to the availability of expertise, the protocol specifications, the PICS and the planing of the SPAN13 meetings.

Ref: B23(99)08, revised during Preparatory Meeting 9/3/200