|  | ToR STF AV (TC DECT) |
| --- | --- |
|  | Version: 0.4 |
|  | Author: Dr. Guenter Kleindl – Date: 01 May 2016 |
|  | Last updated by: Alberto Berrini – Date: 9 June 2016 |
|  | page 1 of 4 |

Terms of Reference STF AV (TC DECT) 
security update and evolution technical studies

Summary information

| Approval status | Approved by TC DECT#69 (18-19 May). Approved by Board#108 (8-9 June) |
| --- | --- |
| Funding | Maximum budget: 114 000 € from ETSI FWP Task A (security): 54 000 €, Task B (studies) 57 000 €, travels 3 000 €. |
| Time scale | Aug-2016 to April-2017 |
| Work Items | Deliverables to be produced: REN/DECT-00307-1 (EN 300 175-1): Part 1: Overview REN/DECT-00307-2 (EN 300 175-2): Part 2: Physical Layer (PHL) REN/DECT-00307-3 (EN 300 175-3): Part 3: Medium Access Control (MAC) layer REN/DECT-00307-4 (EN 300 175-4): Part 4: Data Link Control (DLC) layer REN/DECT-00307-5 (EN 300 175-5): Part 5: Network (NWK) layer REN/DECT-00307-6 (EN 300 175-6): Part 6: Identities and addressing REN/DECT-00307-7 (EN 300 175-7): Part 7: Security features REN/DECT-00307-8 (EN 300 175-8): Part 8: Speech and audio coding and transmission REN/DECT-00309 (EN 300 444): DECT Generic Access Profile (GAP) DTR/DECT-00311 (TR 103 445) : DECT security assessment TR (new deliverable) DTR/DECT-00308 (TR 103 422) : DECT evolution TR (new deliverable) |
| Board priority | ETSI STF funding criteria (ETSI/BOARD(12)88_030r1) Standards enablers/facilitators (Security update) Emerging domains for ETSI (Technical report) |

Part I – Reason for proposing the STF

# Rationale

DECT is one of the most important ETSI standards in terms of public acceptance. Approximately 100 M of DECT devices are sold each year. The standard provides a convenient solution to the needs of cordless telecommunications in the business, residential and WLL scenarios.

The confidentiality of communications has always been DECT technology strength from the beginning. However due to the continuous evolution in computer processing power and in technologies available to potential hackers, it is necessary to analyse new security threats and to implement security upgrades in order to continue ensuring a high standard of protection to end-user communications.

Ultra-Low Energy (ULE) is a M2M technology based on DECT and intended for Internet of Things. ULE Phases 1 and 2 provide a convenient solution for the several devices expected in the Home Automation scenario (sensors, alarms, machine-to-machine communications and various other home automation applications). An important milestone has been the definition of a universal Ipv6/6LoWPAN interface that will be specified by IETF as a RFC. This interface is required by the market in order to integrate the technology in the different architectures developed for the Internet of Things (IoT). The optimal implementation of this interface in a way practical for the end user (detection, self-configurations, pairing) requires some technical work that, for the time being, should identify the possible paths. In addition to that, other studies are required identifying the best way to address other market opportunities that require additional features or investigations.

# Objective

The objective of the proposed STF is dual and will be implemented as two tasks:

Task A: The goal of this task is analysing new security threats and implementing some security architecture enhancements in order to better protect end-user privacy and confidentiality of communications. The need of this update is a consequence of the evolution in computer hardware and hacking technologies and is required to ensure a high standard of protection to end-user communications. The security threat analysis and assessment will be implemented as a dedicated TR. Results from TC CYBER should be reused if possible. The security update will be implemented as a new release of the DECT base standard (EN 300 175 parts 1 to 8) and the Generic Access Profile (EN 300 444). The task will impact principally parts 3, parts 5 and 7 of the DECT base standard and the Generic Access Profile.. The security enhancement is also linked to the evolution of DECT and ULE as described in task B,

Task B: The goal of this task is performing some identified studies required for the short and midterm evolution of DECT and ULE technologies. These studies are required .i.e. to the properly support the new RFC for Ipv6/6LoWPAN over ULE, to address new market opportunities (in both DECT and IoT areas) and to investigate different paths for the mid-term evolution of the technology. The detailed list of studies is shown in section 7.2.  The outcome of this task will be implemented as a Technical Report (new deliverable) and will benefit not only DECT but also other initiatives in the IoT area.

It is expected that the STF outcome on security will be implemented in the short term in most DECT products impacting millions of users. The investigation on ULE evolution will allow addressing new applications and markets for ULE and DECT technologies in the mid-term, and will contribute to the ETSI effort on Internet of Things (IoT).

# Relation with ETSI strategy and priorities

DECT is the most successful European Standard in the field of cordless communications. DECT ULE is the main ETSI project providing a suitable radio technology for IoT devices requiring low operating power.

The proposed work will contribute to ETSI Long Term Strategy, addressing the trends on global level, security and privacy, and strategic objectives on being global, versatile and support EC policy objectives.

The proposed work will implement the EC policy objectives on Digital Single Market and Internet of Things (IoT).

The proposed activities will fulfil the definitions for the categories “Standards enablers/facilitators” (Security update) and “Emerging domains for ETSI” (Technical report)

# Context of the proposal

## ETSI Members support

| ETSI Member | Supporting delegate | Motivation |
| --- | --- | --- |
| AVM | Sven Trevisany | Continuous evolution of a wide established technology. Updating of possible future security threads. |
| Deutsche Telekom AG | Laura Altmüller | It is important that there will be a further development. |
| Dialog Seminconductor B.V. | Colin Foster | Dialog Semiconductor fully supports the STF work being undertaken in the investigation of security issues and the definition of procedures as part of current efforts and the continued evolution of both DECT and ULE. |
| DSPG | Steven Dickinson | DSPG supports the STF for the security assessment of DECT and ULE, and the study of evolution features for DECT and ULE. The low power of ULE is of great importance to DSPG to order to maintain our advantage over competing technologies. |
| FEEI | Günter Kleindl | Do enhance DECT with new capabilities to cover new market areas. |
| Gigaset Communications GmbH | Dieter Kehrer | To support the evolution of the DECT technology in order to open new use cases especially for devices with low power consumption. |
| Panasonic | Hans-Peter Steinbrueck | There is a need to assess the security techniques in DECT/ULE to address the security evolution issues. |
| RTX A/S | Jens Toftgaard Petersen | For ensuring evolution of DECT to address new and more demanding requirements from future applications. |
| WIRELESS PARTNERS S.L.L. | Angel Boveda | To continue the development of DECT and ULE technologies adding new features and market applications. |
| wiseSense GmbH | Andreas Wilzeck | Ensuring privacy and improved low latency and higher data-rates under known QoS constraints in current and evolved DECT communications for professional wireless applications. |

## Market impact

The DECT specification from ETSI is the worldwide leading standard for digital cordless telecommunications. There are more than 1000 million devices in the market and every year more than 100 million devices are sold. In the last 4 years, DECT has become the number one in the US. DECT products are also available in Japan.

Despite this great success, there is continuing threat from other systems to take over market shares from DECT and, in some countries, the cordless telephone market is saturated or already diminishing.

Therefore, it is essential for the DECT community to start to get its foot into new product areas and a promising one is machine-to-machine communication.

The security update will ensure continuing confidentiality of end-user communications and will benefit millions of users of DECT devices.

DECT ULE devices are suitable for long time operation with small batteries. DECT ULE also provides Ipv6 -connectivity, which is required for many new M2M applications.

There is a lot of competition between different technologies, but DECT-ULE offers a combination of several features, which makes it very suitable for M2M applications and these are internet-connectivity, ultra-low power consumption, good range, excellent quality and high capacity.

## Tasks for which the STF support is necessary

Due to the amount of work, and despite the intense activity of TC DECT delegates, the support of an STF is essential for the timely production of the specification and the seamless continuation of the DECT and ULE success story.

The security update requires specialized security expertise, not normally available in TC DECT.

The evolution study requires in depth knowledge of DECT ULE phases 1 and 2 and of general DECT capabilities and expansion possibilities.

## Related voluntary activities in the TB

Many technical contributions have been provided by the experts in TC DECT and the ULE working group. Several interoperability-testing events have been organized by the DECT Forum and performed very successfully. Further test events are planned by the ULE Alliance, the industry fora now driving for the success of this technology.

In addition to that, the DECT industry is contributing to the outgoing IETF RFC “Transmission of IPv6 Packets over DECT Ultra Low Energy” (draft-ietf-6lo-dect-ule)

TC DECT delegates will continue to identify the activities related to the STF and will further contribute to STF objectives, in parallel to the STF.

## Previous funded activities in the same domain

During last 5 years no security review has been done, (last one was done in 2010).

Regarding ULE, ULE phases 1 and 2 has been funded by ETSI as shown below:

The update of DECT repeaters to cover ULE and other new developments has also been funded by ETSI and is shown in the table below:

ETSI Resources:

| Topic | STF | Cost in EUR (ETSI funded) |
| --- | --- | --- |
| ULE Phase 1 | STF 441 | 102 000 |
| ULE Phase 2 | STF 465 | 108 000 |
| Repeaters | STF 506 | 70 000 |
| Total | Total | 280 000 |

## Consequences if not agreed

Not implementing timely security updates according to the evolution of technology may affect the security and privacy of communications.

Not addressing the required studies for immediate evolution may jeopardize the role of ULE in the IoT landscape and will reduce market opportunities for DECT and ULE products.

Part II - Execution of the work

# Technical Bodies and other stakeholders

## Reference TB

TC DECT, Chairman: Dr. Günter Kleindl

DECT ULE Working Group, Chairman: Jens T. Petersen

## Other interested ETSI Technical Bodies

TC ERM, TC smartM2M, TC CYBER

## Other stakeholders

OneM2M, AIOTI, STF 505, EC Large Scale Projects

# Base documents and deliverables

## Base documents

| Document | Title | Current Status | Expected date for stable document |
| --- | --- | --- | --- |
| ETSI EN 300 175-1 | DECT Common Interface (CI); part 1 v2.6.1 | published |  |
| ETSI EN 300 175-2 | DECT Common Interface (CI); part 2 v2.6.1 | published |  |
| ETSI EN 300 175-3 | DECT Common Interface (CI); part 3 v2.6.1 | published |  |
| ETSI EN 300 175-4 | DECT Common Interface (CI); part 4 v2.6.1 | published |  |
| ETSI EN 300 175-5 | DECT Common Interface (CI); part 5 v2.6.1 | published |  |
| ETSI EN 300 175-6 | DECT Common Interface (CI); part 6 v2.6.1 | published |  |
| ETSI EN 300 175-7 | DECT Common Interface (CI); part 7 v2.6.1 | published |  |
| ETSI EN 300 175-8 | DECT Common Interface (CI); part 8 v2.6.1 | published |  |
| ETSI EN 300 444 | DECT Generic Access Profile GAP) v2.4.1 | published |  |
| ETSI TS 102 939-1 | DECT ULE Phase 1 v1.2.1 | published |  |
| ETSI TS 102 939-1 | DECT ULE Phase 2 v.1.1.1 | published |  |
| draft-ietf-6lo-dect-ule | Transmission of IPv6 Packets over DECT Ultra Low Energy | available | Sep 2016 |

## Deliverables

| Deliv. | Work Item code Standard number | Working title Scope |
| --- | --- | --- |
| D1 | REN/DECT-00307-1 (EN 300 175-1): | DECT Common Interface Part 1 |
| D2 | REN/DECT-00307-2 (EN 300 175-2): | DECT Common Interface Part 2 |
| D3 | REN/DECT-00307-3 (EN 300 175-3): | DECT Common Interface Part 3 |
| D4 | REN/DECT-00307-4 (EN 300 175-4): | DECT Common Interface Part 4 |
| D5 | REN/DECT-00307-5 (EN 300 175-5): | DECT Common Interface Part 5 |
| D6 | REN/DECT-00307-6 (EN 300 175-6): | DECT Common Interface Part 6 |
| D7 | REN/DECT-00307-7 (EN 300 175-7): | DECT Common Interface Part 7 |
| D8 | REN/DECT-00307-8 (EN 300 175-8): | DECT Common Interface Part 8 |
| D9 | REN/DECT-00309 (EN 300 444): | DECT Generic Access Profile (GAP) |
| D10 | DTR/DECT-00311 (TR 103 445) | DECT security assessment TR (new deliverable) Scope: To analyse security threats and identifying further improvements. |
| D11 | DTR/DECT-00308 (TR 103 422) | DECT evolution TR (new deliverable) Scope: Collect requirements for the further evolution of DECT and study implementation possibilities, e.g. for low latency or higher bit rates |

## Deliverables schedule:

REN/DECT-00307-1 (EN 300 175-1):  DECT Common Interface Part 1

Start of work	15-aug-2016

ToC and scope	31-aug31-aug-2016

Early draft	1-october-2016

Stable draft	15-december-2016

TB approval	10-february-2017

Start of EN AP.	10-march-2017

Publication	10-october-2017

REN/DECT-00307-2 (EN 300 175-2):  DECT Common Interface Part 2

Start of work	15-aug-2016

ToC and scope	31-aug31-aug-2016

Early draft	1-october-2016

Stable draft	15-december-2016

TB approval	10-february-2017

Start of EN AP.	10-march-2017

Publication	10-october-2017

REN/DECT-00307-3 (EN 300 175-3):  DECT Common Interface Part 3

Start of work	15-aug-2016

ToC and scope	31-aug31-aug-2016

Early draft	1-october-2016

Stable draft	15-december-2016

TB approval	10-february-2017

Start of EN AP.	10-march-2017

Publication	10-october-2017

REN/DECT-00307-4 (EN 300 175-4):  DECT Common Interface Part 4

Start of work	15-aug-2016

ToC and scope	31-augy-2016

Early draft	1-october-2016

Stable draft	15-december-2016

TB approval	10-february-2017

Start of EN AP.	10-march-2017

Publication	10-october-2017

REN/DECT-00307-5 (EN 300 175-5):  DECT Common Interface Part 5

Start of work	15-augy-2016

ToC and scope	31-augy-2016

Early draft	1-october-2016

Stable draft	15-december-2016

TB approval	10-february-2017

Start of EN AP.	10-march-2017

Publication	10-october-2017

REN/DECT-00307-6 (EN 300 175-6):  DECT Common Interface Part 6

Start of work	15-augy-2016

ToC and scope	31-augy-2016

Early draft	1-october-2016

Stable draft	15-december-2016

TB approval	10-february-2017

Start of EN AP.	10-march-2017

Publication	10-october-2017

REN/DECT-00307-7 (EN 300 175-7):  DECT Common Interface Part 7

Start of work	15-augy-2016

ToC and scope	31-augy-2016

Early draft	1-october-2016

Stable draft	15-december-2016

TB approval	10-february-2017

Start of EN AP.	10-march-2017

Publication	10-october-2017

REN/DECT-00307-8 (EN 300 175-8):  DECT Common Interface Part 8

Start of work	15-augy-2016

ToC and scope	31-aug-2016

Early draft	1-october-2016

Stable draft	15-december-2016

TB approval	10-february-2017

Start of EN AP.	10-march-2017

Publication	10-october-2017

REN/DECT-00309 (EN 300 444):  DECT Generic Access Profile

Start of work	15-augy-2016

ToC and scope	31-aug-2016

Early draft	1-october-2016

Stable draft	15-december-2016

TB approval	10-february-2017

Start of EN AP.	10-march-2017

Publication	10-october-2017

DTR/DECT-00311 (TR 103 445):  DECT security assessment TR (new deliverable)

Start of work	15-augy-2016

ToC and scope	31-aug-2016

Early draft	1-october-2016

Stable draft	15-december-2016

TB approval	15-april-2017

Publication.	15-may-2017

DTR/DECT-00308 (TR 103 422):  DECT evolution TR (new deliverable)

Start of work	15-augy-2016

ToC and scope	31-aug-2016

Early draft	1-october-2016

Stable draft	10-february-2016

WG approval	10-april-2017

TB approval	15-april-2017

Publication.	15-may-2017

# Work plan, time scale and resources

## Organization of the work

The work will be steered by the TC DECT chairman, the ULE WG chairman and the ULE WG members. There will be about three TC DECT or WG ULE F2F meetings and 20 online meetings from July 2016 to April 2017.

## Task description

Task A – DECT core security update

Objectives

The goal of this task is implementing some security enhancements in order to better protect end-user privacy and confidentiality of communications. The need of this update is consequence of the evolution in computer hardware and hacking technologies and is required to ensure a high standard of protection to end-user communications.

Due to security considerations and due to the DECT roadmap this task should be implemented as soon as possible.

The task will consist on the following sub-tasks:

Task A1: Performing a security study (to be released as a Technical Report) analysing the following topics:

- Threat analysis of possible attacks based on the impersonation of the base (FP), attack case and corrective measures.

- Benchmarking on DECT/ULE security, including key allocation and distribution procedures.

- Threat analysis of possible security attacks during the initial registration procedures and assessment of possible improvements.

- Threat analysis of the man-in-the middle attack and proposal of corrective measures.

The above threat analysis will be implemented as a Technical Report (TR 103 445).

Task A2: Introducing a security update in DECT base standard and Generic Access Profile.

The task is to update the deliverables in order to further improve the security, implementing some previously identified areas. The goal of the design is establishing a series of contra-measures that would create a requirement of processing power to break the algorithms impossible to achieve with the means available to standard hackers. The model and the solution shall be described in EN 300 175-7 with further procedures implemented in EN 300 175-5 (including new content in NWK signalling information elements). Further rules and procedures shall be developed for EN 300 444 (Generic Access Profile).

The changes described in task A2 are considered mature enough to go directly to the implementation phase. Any early outcomes of task A1 can also be considered to be included in this update.

Input

This task will take as base document the current versions of the DECT base standard (v2.6.1) and Generic Access Profile (EN 300 444). Other DECT standards such as NG-DECT parts 1 to 5, DECT repeaters and ULE part 1 and 2 will be monitored and will inherit some of the benefits of the security updates but will not be changed as part of this STF.

Output

This enhancement will be implemented as a new Technical Report, TR 103 445 and a new release of the DECT base standard (EN 300 175 parts 1 to 8) and the Generic Access Profile (EN 300 444). The task will impact principally parts 3, 5 and 7 of the DECT base standard..

Interactions

The STF service providers are expected to interact on a regular basis with the TC and WG, and to participate in all meetings and conference calls during the STF timeframe (3 F2F meetings and 20 online meetings expected).

Resources required

Task A shall be executed by providers with the following mix of skills:

- authority expertise in DECT technology with knowledge of all layers and involved in the TC DECT developments done during last years, including NG-DECT, ULE and WRS

- strong background on DECT security architecture and algorithms

- proven knowledge of the weakness in current DECT security model, including repeaters, how to exploit them for performing an attack and how to fix them

The actual number of service providers depends on the actual mix of skills in the applications received and will be decided when setting up the STF.

Task B – DECT and ULE evolution Technical Report

Objectives

The goal of this task is performing some identified studies required for the short and midterm evolution of DECT and ULE technologies. These studies are required to the properly support the new RFC for IPv6/6LoWPAN transmission over ULE (Transmission of IPv6 Packets over DECT Ultra Low Energy, draft-ietf-6lo-dect-ule) and to further analyse some identified market (in both DECT and IoT areas) and to investigate different paths for the mid-term evolution of the technology, mostly in the area of ULE / IoT.

The study will address the following tasks:

- Implementation of the new RFC for IPv6/6LoWPAN transmission over ULE (Transmission of IPv6 Packets over DECT Ultra Low Energy, draft-ietf-6lo-dect-ule) covering aspects such as device type identification, self configuration, pairing, addressing mapping between external IPv6/6LoWPAN addresses and internal addresses and managing and allocation of paging descriptors.

- Packet based adaptive voice codecs

- DECT for critical applications with predictable QoS and latency

- Extra-ultra low power consumption in ULE (lower than now)

- Improved connection setup latency

- Operation with known QoS

- Operation with low latency (lower than now)

- Improvements in packet based service

- Improved MAC/PHY, high level modulation schemes are defined, but potential further developments to be considered

- DECT as a technology for offloading backbone wireless network

- Reliability for critical applications

- Large multi cell deployments of ULE with different levels of roaming and handover (MAC, connection, external)

- Configuration of DECT/ULE setup parameters

It is expected that the investigation on ULE evolution will allow addressing new application and markets for ULE and DECT technologies in the mid-term, and will contribute to the ETSI effort on Internet of Things (IoT).

Input

This task will take as base document the whole set of DECT specifications. The following deliverables are expected to be the most relevant:

- Current versions of the DECT base standard (EN 300 175 part 1 to 8) v2.6.1

- Generic Access Profile (EN 300 444). V2.4.1

- New Generation DECT parts 1 to 5

- DECT Ultra Low Energy parts 1 and 2 (TS 102 939 1 and 2)

- Transmission of IPv6 Packets over DECT Ultra Low Energy (draft-ietf-6lo-dect-ule)

Special attention should be paid to the two DECT ULE specifications and to the IETF draft.

The expert should be aware of the activities in other EC projects related to Internet of Things, mainly in the AIOTI WG3

Output

The outcome of this task will be implemented as a Technical Report (new deliverable)

Interactions

The STF expert is expected to interact on a regular basis with the TC and WG, and to participate in all meetings and conference calls during the STF timeframe (3 F2F meetings and 20 online meetings expected).

The expert should be ready to participate in external meetings if required by the task.

The outcome of the task will benefit other ETSI and EC projects, i.e. it may be used as contribution to the gap analysis in IoT standardization promoted by the EC.

Resources required

Task B shall be executed providers with the following mix of skills:

- authority expert in DECT technology with knowledge of all layers

- involved in the TC DECT developments done during last years, including NG-DECT, ULE and WRS

- authority expert and active participant in DECT ULE

- strong background in Internet of Things (IoT) with active participation in related projects such as AIOTI

The actual number of providers depends on the actual mix of skills in the applications received and will be decided when setting up the STF.

## Milestones

Milestone 1 – Early draft of TR 103 445, TR 103 422, EN 300 175 1 to 8, and EN 300 444 for TC review

Tasks 1, 2 and 3 completed

An early draft of EN 300 175 parts 1 to 8 and EN 300 444 will be available for TC review

An early draft of TR 103 445 will be available for TC review

An early draft of TR 103 422 will be available for TC review

Progress Report 1 approved by TC DECT

Milestone 2 – Stable draft of TR 103 445, EN 300 175 1 to 8 and EN 300 444 for TC review

Tasks 4 and 5 completed

An stable draft of EN 300 175 parts 1 to 8 and EN 300 444 will be available for TC review

The stable draft shall include an stable version of the intended security solution in EN 300 175-7 and intended NWK procedures in EN 300 175-5

An stable draft of TR 103 445 will be available for TC review

Progress Report 2 approved by TC DECT

Milestone 3 – Final draft of EN 300 175 1 to 8 and EN 300 444 approved by TC DECT and stable draft of TR 103 422 for TC review

Tasks 6 and 7 completed

Final draft of EN 300 175 parts 1 to 8 and EN 300 444 approved by TC DECT

The final draft shall include the complete security upgrade

An stable draft of TR 103 422 will be available for TC review

The stable draft of TR 103 422 shall cover at least the investigation on 8 of the topics given in section 7.2, 5 of them should be considered stable

Progress Report 3 approved by TC DECT

Milestone 4 – Final draft of TR 103 422, TR 103 445, EN 300 175 1 to 8 and EN 300 444 approved by TC DECT

Tasks 8 and 9 completed

Final draft of TR 103 422 approved by TC DECT

The final draft of TR 103 422 shall cover the investigation on 10 of the topics given in section 7.2.

Final draft of TR 103 445 approved by TC DECT

The final draft of TR 103 422 shall cover the investigation on all topics given in section 7.2.

Final Report approved by TC DECT

## STF time line summary

The following tables present the STF time line for the integration of the outcome of the tasks described in §7.2 in the deliverables.

|  | Task / Milestone / Deliverable | Target date |
| --- | --- | --- |
| M0 | Start of work | 15-aug-2016 |
| T0 | Project Management and final report | from 15-aug-2016-to 15-apr-2017 |
| T1 | Develop early draft for EN 300 175 1 to 8 and EN 300 444 | from 15-aug-2016-to 1-oct-2016 |
| T2 | Develop early draft for TR 103 445 | from 15-aug-2016-to 1-oct-2016 |
| T3 | Develop early draft for TR 103 422 | from 15-aug-2016-to 1-oct-2016 |
| M1 | Early draft of TR 103 445, TR 103 422, EN 300 175 1 to 8 and EN 300 444 for TC review | 1-oct-2016 |
| T4 | Develop stable drafts for EN 300 175 1 to 8 and EN 300 444 | from 1-oct-2016 to 15-dec-2016 |
| T5 | Develop stable draft for TR 103 445 | from 1-oct-2016 to 15-dec-2016 |
| M2 | Stable drafts of TR 103 445, EN 300 175 1 to 8 and EN 300 444 for TC review | 15-dec-2016 |
| T6 | Develop stable draft for TR 103 422 | from 1-oct-2016 to 10-feb-2016 |
| T7 | Develop final drafts for EN 300 175 1 to 8 and EN 300 444 and collecting TC comments to final drafts | from 15-dec-2016 to 10-feb-2017 |
| M3 | Final drafts of EN 300 175 1 to 8 and EN 300 444 approved by TC DECT and stable draft of TR 103 422 for TC review | 10-feb-2017 |
| T8 | Develop final drafts for TR 103 445 and collecting TC comments to final drafts | from 15-dec-2016 to 15-apr-2017 |
| T9 | Develop final drafts for TR 103 422 and collecting TC comments to final drafts | from 10-feb-2016 to 15-apr-2017 |
| M4 | Final drafts of TR 103 445 and TR 103 422, approved by TC DECT | 15-apr-2017 |

| Task Milest. | Description | J | A | S | O | N | D | J | F | M | A |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| M0 | Start of work |  | X |  |  |  |  |  |  |  |  |
| T0 | Project Management |  | X | X | X | X | X | X | X | X | X |
| T1 | Develop early draft for EN 300 175 1 to 8 and EN 300 444 |  | X | X |  |  |  |  |  |  |  |
| T2 | Develop early draft for TR 103 445 |  | X | X |  |  |  |  |  |  |  |
| T3 | Develop early draft for TR 103 422 |  | X | X |  |  |  |  |  |  |  |
| M1 | Early draft of TR 103 445, TR 103 422, EN 300 175 1 to 8 and EN 300 444 for TC review |  |  |  | X |  |  |  |  |  |  |
| T4 | Develop stable drafts for EN 300 175 1 to 8 and EN 300 444 |  |  |  | X | X | X |  |  |  |  |
| T5 | Develop stable draft for TR 103 445 |  |  |  | X | X | X |  |  |  |  |
| M2 | Stable drafts of TR 103 445, EN 300 175 1 to 8 and EN 300 444 for TC review |  |  |  |  |  | X |  |  |  |  |
| T6 | Develop stable draft for TR 103 422 |  |  |  | X | X | X | X |  |  |  |
| T7 | Develop final drafts for EN 300 175 1 to 8 and EN 300 444 and collecting TC comments to final drafts |  |  |  |  |  | X | X | X |  |  |
| M3 | Final drafts of EN 300 175 1 to 8 and EN 300 444 approved by TC DECT and stable draft of TR 103 422 for TC review |  |  |  |  |  |  |  | X |  |  |
| T8 | Develop final drafts for TR 103 445 and collecting TC comments to final drafts |  |  |  |  |  | X | X | X | X | X |
| T9 | Develop final drafts for TR 103 422 and collecting TC comments to final drafts |  |  |  |  |  |  |  | X | X | X |
| M4 | Final drafts of TR 103 445 and TR 103 422, approved by TC DECT |  |  |  |  |  |  |  |  |  | X |

## Working methods and travel cost

It is assumed that the tasks and milestones will be as shown in section 7.4. The TC may introduce changes in the timing according to the progress of the work.

The work shall be performed remotely as much as possible.

However participation in all F2F meetings of the TC and WG to present results is mandatory.

The provider(s) may be requested to participate in up to three non DECT meetings at choice of the TC (they will be funded by the STF). This participation is related to the alignment of requirements for Task B with other stakeholders such as AIOTI, or EC LSPs.

The total travel cost is estimated in 3 k E and should cover participation in 3 meetings.

# Expertise required

## Team structure

This STF is intended to be executed by service providers able to provide the following mix of skills:

authority competence in DECT technology with knowledge of all layers and involved in the TC DECT developments done during last years, including NG-DECT, ULE and WRS

strong background on DECT security architecture and algorithms

knowledge of the weakness in current DECT security model, including repeaters, how to exploit them for performing an attack and how to fix them

authority competence in DECT technology with knowledge of all layers

authority competence and active contribution to DECT ULE

strong background in Internet of Things (IoT) with active participation in related projects such as AIOTI

The actual number of providers depends on the actual mix of skills in the applications received and will be decided when setting up the STF.

Part III:	Financial conditions

# Maximum budget

| Description | Maximum estimated cost (€) |
| --- | --- |
| Service contracts | 111 000 |
| Travels |
| TC DECT#70 meeting | 1 000 |
| TC DECT#71 meeting | 1 000 |
| TC DECT#72 meeting | 1 000 |
| Travel cost | 3 000 |
| Total cost | 114 000 |

No other cost identified

Part IV:	STF performance evaluation criteria

# Key Performance Indicators

Contribution from ETSI Members to STF work

Conference calls to review STF documents/contributions

Number of delegates attending meetings attending DECT and WG DECT-ULE meetings

Number of delegates directly involved in the review of the deliverables

Contributions/comments received from the reference TBs

Contribution from the STF to ETSI work

Contributions to TC/WG meetings (number of documents / meetings / participants)

Contributions to other TBs

Presentations in workshops, conferences, stakeholder meetings

Liaison with other stakeholders

Stakeholder participation in the project (category, business area)

Cooperation with other standardization bodies

Potential interest of new members to join ETSI

Quality of deliverables

Approval of deliverables according to schedule

Respect of time scale, with reference to start/end dates in the approved ToR

Comments from Quality review by TB

Comments from Quality review by ETSI Secretariat

Time recording

For reporting purposes the STF experts shall fill in the time sheet provided by ETSI with the days spent for the performance of the services

In the course of the activity, the STF Leader shall collect the relevant information, as necessary to measure the performance indicators.  The result will be presented in the Final Report.

# Document history

|  | Date | Author | Status | Comments |
| --- | --- | --- | --- | --- |
| 0.0 | 01-May-2016 | Dr. Guenter Kleindl | Draft for TC approval |  |
| 0.1 | 18-May-2016 | Dr. Guenter Kleindl | TC approved | Approved during TC DECT #69 meeting in Vienna, 18-19.May 2016 |
| 0.2 | 20-May-2016 | Alberto Berrini | OCG/Board consultation | Start date cannot be earlier than 18 July + editorials |
| 0.3 | 31-May-2016 | Dr. Guenter Kleindl | OCG/Board consultation | Clarifications added |
| 0.4 | 09-Jun-2016 | Alberto Berrini | Board#108 | Approved with 5% maximum budget reduction |