| Pseudo CHANGE REQUEST |
| --- |
| 123 401 | Version | 11.8.0 | CR | P-CR | rev | - |
| CR Title: | eCall over IMS |
| Source: | STF 456 |
| Work Item Ref: | Migration of eCall transport | Date: | 04/02/2014 |
| Category: | B | Release: | Rel-11 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature) C (functional modification of feature) D (editorial modification) |
| Reason for change: | ETSI STF456, partly funded by the European Commission, is investigating migration of eCall transport over PS domain/EPS. The Release-8 eCall covers CS only, and therefore excludes PS/IMS emergency services. ETSI MSG TC agreed the TR103140 that studies the Migration of eCall transport. Proposed and recommended solutions are included in this TR. The solution considered for eCall over IMS is in line with the IMS emergency call/services. |
| Summary of change: | Adding a new reference – TS 22.101 Referencing the eCall related definitions. The IMS eCall over EPS follows the same procedures as IMS emergency session. eCall requires carrying a set of data called Minimum Set of Data (MSD) in addition to the voice component (VOIP). eCall exists in two modes; eCall-Automatic and eCall-Manual that are also called eCall flag. The eCall flag and the MSD are carried over IMS. The eCall only MS, determined by information configured in the USIM, performs eCall emergency services. In addition, eCall only MS performs non-Emergency services; terminal reconfiguration that follow the IMS and eCall related EPS procedures, and eCall test that follows IIMS and eCall related EPS procedures to set up eCall towards a test PSAP. Mobility management for eCall only UE has some restrictions to reduce overload on the networks as well as to respect the privacy in not following and tracing the vehicle equipped with eCall unit unless eCall is triggered. The eCall only UE camps on a network cell and only register to the network once eCall is triggered. Mobility management procedures are performed during the eCall and continue for a period of time after the call is ended, when the UE enters EMM-IDLE mode. The limited time that mobility management procedure is made possible depends on the timer value configuration that guards the eCall UE in the EMM-IDLE mode. Different timer values may be configured for the eCall emergency service and for the eCall non-emergency services. The eCall only UE, when in EMM-IDLE mode may receive call-back from the PSAP. On removal of “eCall only restriction” that results from UE reconfiguration, the UE can receive normal services. A flag in broadcast system information indicating the network support for IMS eCall is required to ensure the eCall UE receives the required service from IMS and the eCall is routed to the appropriate PSAP. RAN2 needs to introduce this flag therefore this is added here as an editor’s note. |
| Clauses affected: | 2, 3.1, 4.3.5.7, 4.3.x(new) |
| Other deliverables affected: |  |
| Other comments: |  |

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TS 23.402: "Architecture enhancements for non-3GPP accesses".

[3]	ITU-T Recommendation I.130: "Method for the characterization of telecommunication services supported by an ISDN and network capabilities of an ISDN".

[4]	ITU-T Recommendation Q.65: "The unified functional methodology for the characterization of services and network capabilities".

[5]	3GPP TS 36.300: "Evolved Universal Terrestrial Radio Access (E-UTRA) and Evolved Universal Terrestrial Radio Access Network (E-UTRAN); Overall description; Stage 2".

[6]	3GPP TS 23.203: "Policy and charging control architecture".

[7]	3GPP TS 23.060: "General Packet Radio Service (GPRS); Service description; Stage 2".

[8]	3GPP TS 43.129: "Packet-switched handover for GERAN A/Gb mode; Stage 2".

[9]	3GPP TS 23.003: "Numbering, addressing and identification".

[10]	3GPP TS 23.122: "Non-Access-Stratum (NAS) functions related to Mobile Station in idle mode".

[11]	3GPP TS 43.022: "Functions related to MS in idle mode and group receive mode".

[12]	3GPP TS 25.304: "UE procedures in idle mode and procedures for cell re-selection in connected mode".

[13]	3GPP TS 23.246: "Multimedia Broadcast/Multicast Service (MBMS); Architecture and functional description".

[14]	3GPP TS 29.060: "GPRS Tunnelling Protocol (GTP) across the Gn and Gp interface".

[15]	3GPP TS 43.051: "GERAN Overall description - Stage 2".

[16]	3GPP TS 25.401: "UTRAN overall description".

[17]	IETF RFC 1034 (1987): "Domain names – concepts and facilities" (STD 13).

[18]	IETF RFC 4862: "IPv6 Stateless Address Autoconfiguration".

[19]	IETF RFC 2131: "Dynamic Host Configuration Protocol".

[20]	IETF RFC 3736: "Stateless Dynamic Host Configuration Protocol (DHCP) Service for IPv6".

[21]	IETF RFC 3633: "IPv6 Prefix Options for Dynamic Host Configuration Protocol (DHCP) version 6".

[22]	3GPP TS 25.413: "UTRAN Iu interface Radio Access Network Application Part (RANAP) signalling".

[23]	3GPP TS 44.064: "Mobile Station - Serving GPRS Support Node (MS-SGSN); Logical Link Control (LLC) Layer Specification".

[24]	3GPP TS 23.251: "Network Sharing; Architecture and functional description".

[25]	IETF RFC 4039: "Rapid Commit Option for the Dynamic Host Configuration Protocol version 4 (DHCPv4)".

[26]	IETF RFC 768: "User Datagram Protocol".

[27]	3GPP TS 23.221: "Architectural requirements".

[28]	3GPP TS 23.008: "Organization of subscriber data".

[29]	3GPP TS 23.078: "Customized Applications for Mobile network Enhanced Logic (CAMEL) Phase X; Stage 2".

[30]	3GPP TS 23.236: "Intra-domain connection of Radio Access Network (RAN) nodes to multiple Core Network (CN) nodes".

[31]	IETF RFC 3588: "Diameter Base Protocol".

[32]	IETF RFC 4861: "Neighbor Discovery for IP Version 6 (IPv6)".

[33]	3GPP TS 25.331: "Radio Resource Control (RRC); Protocol Specification".

[34]	3GPP TS 36.304: "Evolved Universal Terrestrial Radio Access (E-UTRA); User Equipment (UE) procedures in idle mode".

[35]	IETF RFC 4960: "Stream Control Transmission Protocol".

[36]	3GPP TS 36.413: "Evolved Universal Terrestrial Access Network (E-UTRAN); S1 Application Protocol (S1AP)".

[37]	3GPP TS 36.331: "Evolved Universal Terrestrial Radio Access (E-UTRA); Radio Resource Control (RRC); Protocol specification".

[38]	3GPP TS 29.061: "Interworking between the Public Land Mobile Network (PLMN) supporting packet based services and Packet Data Networks (PDN)".

[39]	Void.

[40]	3GPP TS 33.102: "3G Security; Security architecture".

[41]	3GPP TS 33.401: "3GPP System Architecture Evolution: Security Architecture".

[42]	3GPP TS 48.018: "General Packet Radio Service (GPRS); Base Station System (BSS) - Serving GPRS Support Node (SGSN); BSS GPRS Protocol (BSSGP)".

[43]	3GPP TS 29.274: "3GPP Evolved Packet System (EPS); Evolved General Packet Radio Service (GPRS) Tunnelling Protocol for Control plane (GTPv2-C); Stage 3".

[44]	3GPP TS 32.251: "Telecommunication management; Charging management; Packet Switched (PS) domain charging".

[45]	3GPP TS 24.007: "Mobile radio interface signalling layer 3; General aspects".

[46]	3GPP TS 24.301: "Non-Access-Stratum (NAS) protocol for Evolved Packet System (EPS); Stage 3".

[47]	3GPP TS 24.008: "Mobile Radio Interface Layer 3 specification; Core Network Protocols; Stage 3".

[48]	3GPP TS 23.041: "Technical realization of Cell Broadcast Service (CBS)".

[49]	3GPP TS 22.042: "Network Identity and Time Zone (NITZ) service description; Stage 1".

[50]	Void.

[51]	3GPP TS 32.240: "Charging architecture and principles".

[52]	3GPP TS 23.228: "IP Multimedia Subsystem (IMS); Stage 2".

[53]	3GPP TS 24.285: "Allowed Closed Subscriber Group (CSG) List; Management Object (MO)".

[54]	Void.

[55]	IETF RFC 3168: "The Addition of Explicit Congestion Notification (ECN) to IP".

[56]	3GPP TS 26.114: "IP Multimedia Subsystem (IMS); Multimedia Telephony; Media handling and interaction".

[57]	3GPP TS 23.271: "Functional stage 2 description of LCS".

[58]	3GPP TS 23.272: "Circuit Switched (CS) fallback in Evolved Packet System (EPS); Stage 2".

[59]	3GPP TS 23.107: "Quality of Service (QoS) concept and architecture".

[60]	3GPP TS 23.292: "IP Multimedia Subsystem (IMS) centralized services; Stage 2".

[61]	3GPP TS 29.303: "Domain Name System Procedures; Stage 3".

[62]	IETF RFC 3376: "Internet Group Management Protocol, Version 3".

[63]	IETF RFC 3810: "Multicast Listener Discovery Version 2 (MLDv2) for IPv6".

[64]	IETF RFC 3927: "Dynamic Configuration of IPv4 Link-Local Addresses".

[65]	IETF RFC 4291: "IP Version 6 Addressing Architecture".

[66]	3GPP TS 22.368: "Service Requirements for Machine-Type Communications (MTC); Stage 1".

[67]	3GPP TS 22.011: "Service Accessibility".

[68]	3GPP TS 22.153: "Multimedia priority service".

[69]	3GPP TS 24.368: "Non-Access Stratum (NAS) configuration Management Object (MO)".

[70]	IETF Internet-Draft draft-ietf-dhc-pd-exclude-04:"Prefix Exclude Option for DHCPv6-based Prefix Delegation".

Editor's Note:	The above document cannot be formally referenced until it is published as an RFC.

[71]	3GPP TS 23.002: "Network Architecture".

[72]	3GPP TS 23.007: "Restoration procedures".

[XX]	3GPP TS 22.101: "Service aspects; Service principles".

********************* Next Change **********************************

# 3	Definitions and abbreviations

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in TR 21.905 [1] and the following apply. A term defined in the present document takes precedence over the definition of the same term, if any, in TR 21.905 [1].

MME Pool Area: An MME Pool Area is defined as an area within which a UE may be served without need to change the serving MME. An MME Pool Area is served by one or more MMEs ("pool of MMEs") in parallel. MME Pool Areas are a collection of complete Tracking Areas. MME Pool Areas may overlap each other.

Serving GW Service Area: A Serving GW Service Area is defined as an area within which a UE may be served without need to change the Serving GW. A Serving GW Service Area is served by one or more Serving GWs in parallel. Serving GW Service Areas are a collection of complete Tracking Areas. Serving GW Service Areas may overlap each other.

PDN Connection: The association between a UE represented by one IPv4 address and/or one IPv6 prefix and a PDN represented by an APN.

Default Bearer: The EPS bearer which is first established for a new PDN connection and remains established throughout the lifetime of the PDN connection.

Default APN: A Default APN is defined as the APN which is marked as default in the subscription data and used during the Attach procedure and the UE requested PDN connectivity procedure when no APN is provided by the UE.

Emergency attached UE: A UE which only has bearer(s) related to emergency bearer service.

NOTE:	The above term is equivalent to the term "attached for emergency bearer services" as specified in TS 24.301 [46].

The terms "eCall ", "eCall only" and "removal of eCall only restriction", and "MSD", are as specified in 3GPP TS 22.101 [xx].

LIPA PDN connection: a PDN Connection for local IP access for a UE connected to a HeNB.

Correlation ID: For a LIPA PDN connection, Correlation ID is a parameter that enables direct user plane path between the HeNB and L-GW.

********************* Next Change **********************************

#### 4.3.5.7	Mobility Restrictions

Mobility Restrictions comprises the functions for restrictions to mobility handling of a UE in E-UTRAN access. The Mobility Restriction functionality is provided by the UE, the radio access network and the core network.

Mobility Restriction functionality in state ECM-IDLE is executed in UE based on information received from the core network. Mobility Restriction functionality in state ECM-CONNECTED is executed in the radio network and the core network.

In state ECM-CONNECTED, the core network provides the radio network with a Handover Restriction List. The Handover Restriction List specifies roaming, area and access restrictions. If roaming restriction to GERAN or UTRAN access needs to be enforced, a MME that is connected to eNBs that may handover or invoke release with redirection to UTRAN or GERAN is configured with a list of HPLMN IDs that are permitted to access GERAN or UTRAN unless restricted by the UE individual access restriction information received from HSS.

An eCall only UE shall not perform mobility management procedures, including registration on a PLMN, except when attempting to initiate and during an eCall emergency session, or when an eCall only MS is initiating a test or reconfiguration session. Following the completion of the eCall emergency session or the test /reconfiguration session, the eCall UE shall change to EMM-IDLE mode for a limited period of time (that is preconfigured in the USIM). The timer for eCall emergency session and the timer for test/reconfiguration services may vary in value. On removal of eCall only restriction, the UE shall perform normal mobility management procedures.

********************* Next Change **********************************

### 4.3.x	IMS eCall support over EPS

eCall is an in vehicle emergency service that perform transfer of data to the appropriate PSAP during an emergency session as described in 3GPP TS 22.101[xx].  eCall UE initiating IMS eCall session via EPS is determined by information configured in the USIM that is applicable for E-UTRAN and UTRAN.

The eCall only UE over EPS supports two types of services:

- Emergency services; that are based on IMS emergency session over packet core, thus following the same procedures with the eCall restrictions.

- Non-Emergency services;

-	for the purpose of accessing terminal reconfiguration, based on normal voice IMS procedure with the eCall mobility management restrictions.

-	for the eCall test purposes, where the UE performs an IMS eCall towards a test PSAP.

On IMS level, the eCall only UE indicates at session setup if the session is triggered as eCall-manual or eCall-automatic, also the minimum set of data (MSD) shall be carried over IMS. The support of "IMS Voice over PS Sessions" is mandatory for IMS eCall.

An eCall only UE mobility management procedures restrictions is described in subclause 4.3.5.7,

On removal of eCall only restriction, the UE can receive normal services.

Editor’s Note:	 Since IMS eCall follows the same procedures as IMS emergency services, then the eCall only UEs in EMM-DEREGISTERED state determines if the cell in a PLMN supports IMS based emergency services over E-UTRAN (from a broadcast indicator in AS). However, due to the eCall additional requirements as to initiate a voice session in addition to the minimum set of data, a unique flag in the broadcast system information indicating that the network supports IMS eCall is seen necessary for a successful eCall.

# Comments

Enter the ETSI deliverable number in this box. For example, "180 002". Do not prefix the number. i.e. do not use "TR TS EN DTR etc",

Enter the version of the deliverable here. This number is the version of the deliverable to which the CR will be applied if it is approved. Make sure that the latest version of the deliverable (of the relevant release) is used when creating the CR.

Enter the CR number here. This number is allocated by the ETSI Support Team.  It consists of at least three digits, padded with leading zeros as necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter a concise description of the subject matter of the CR. It should be no longer than one line.  Do not use redundant information such as "Change Request number xxx to TR  xx.xxx".

One or more organizations (ETSI Members) which drafted the CR and are presenting it.

Enter the Work Item Reference in this box. For example, "00005". Do not prefix the number.

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter the number of each clause which contains changes.

Enter the Work Item Reference of  any other specifications are affected by this change.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.