ATAAB  ADVISORY NOTE

TRAC Analogue Type Approval Advisory Board

Proposed

ATAAB Advisory Note Number: CZ 01

Date: 	1999-06-30

Subject:	Additional requirement for attachment to the PSTN in the Czech Republic - Automatic dialling with dial tone detection

APPLICABILITY

This note is applicable for Terminal Equipment intended for connection to the Public Switched Telephone Networks in the Czech Republic, in addition to:

X	"CTR 21"

This note contains specific advice concerning the relationship between the requirements  and tests

of CTR21 and the network termination points parameters encountered in the Czech Republic.

Appendix to this Advisory Note:

A:	Additional requirements and tests for attachment to the Public Switched Telephone Network in the Czech Republic - Automatic dialling: Dialling with dial tone detection

In consideration of the following:

-	ATAAB Advisory Notes Nr. 003 and 004 contain specific advices concerning some requirements and tests. The explicitly cited parameters do not cover all parameters that may influence successful  inter-working of terminals designed to meet TBR21 with PSTN in the Czech Republic;

-	The additional parameter that may prevent regular inter-working was found as results of performed analyses of existing PSTN network termination points (NTPs) in the Czech Republic and it relates to dialling with dial tone detection;

-	The cadenced dial tone (Morse a) originally defined for the telephone exchanges operated in the Czech Republic has had different parameters than those presented in TBR21, subclause 4.8.1.2. These national dial tone parameters are presented in EN 300 001, chapter 5;

-	Due to many different dial tone generator implementations in various telephone exchanges and access equipment in the Czech Republic  successful detection of such tone cannot be assured at any TE even if it follows the above mentioned national specification in EN 300 001. This fact has also lead to  an instruction in EN 300 001 which requires the TE have possibility to disable the dial tone detection facility and enable dialling without dial tone detection;

-	TBR21 does not make preference in automatic dialling techniques (dialling with or without dial tone detection) - each of the two techniques, none or both  may be supported in terminals.  Therefore a TE may  successfully pass the tests as defined in TBR21, subclause 4.8.1.2, even if it supports only dialling with dial tone detection. Subclause 4.8.1.2, however, does not  require checking the automatic dialling if the dial tone detection facility is disabled. Consequently,  such a  TE may  not be able to dial in case of the dial tone detection failure;

For the reason of basic inter-working with the network it is necessary to require the TE supporting automatic dialling with dial tone detection to have also possibility to disable this facility and dial without necessity to detect any dial tone;

-	The conditions for TE dial tone detection in the PSTNs in the Czech Republic  may  be changed only after the future transition to new unified dial tone but this is not yet scheduled (status in July 1999);

-        TE approved to CTR 21 will need to note this additional requirement when a TE is intended   for connection to Public Switched Telephone Network in the Czech Republic;

ATAAB advises the following:

To be able to inter-work properly with the Public Switched Telephone Network in the Czech Republic, the TE shall, in addition to the requirements of CTR 21, comply with the requirements found in appendix A of this Advisory Note.

It is the responsibility of the supplier/manufacturer to provide information for users as to whether the Terminal Equipment complies with the additional requirements for the Public Switched Telephone Network in the Czech Republic specified in this Advisory Note.

Appendix A also specifies the method to assess compliance with the additional requirement, including reference to the additional test to be performed to dynamically assess compliance with the additional requirement.

ATAAB ADVISORY NOTE

TRAC Analogue Type Approval Advisory Board

Appendix  A

to

ATAAB Advisory Note Number: 00x (CZ01)

Subject:	Additional requirements and tests for attachment to the Czech Public Switched Telephone Network - Automatic dialling: Dialling with dial tone detection

A.1	INTRODUCTION

Terminal Equipment approved to CTR 21 may not inter-work properly with the NTPs of the Public Switched Telephone Network in the Czech Republic.

This Appendix specifies requirements to which a TE shall comply, in addition to the requirements of CTR 21, in order to inter-work properly with the network when the TE dials automatically.

It also specifies the method to assess compliance with these requirements, including reference to additional tests to be performed to dynamically assess compliance with the additional requirements.

A.2	NORMATIVE REFERENCES

[1]	TBR21; Terminal Equipment (TE). Attachment requirements for pan-European approval for connection to the analogue Public Switched Telephone Networks (PSTNs) of TE (excluding TE supporting the voice Telephony Service) in which network addressing, if provided, is by means of Dual Tone Multi-Frequency (DTMF) signalling. ETSI, First Edition, 1998.

[2]	EN 300 001; Attachments to Public Switched Telephone Network (PSTN); General technical requirements for equipment connected to

an analogue subscriber interface in the PSTN. ETSI, V.1.5.1, October 1998.

A.3	REQUIREMENTS and ASSOCIATED TESTS

A.3.1  Dialling with dial tone detection (TBR21 subclause 4.8.1.2)

Requirement: Additional sentence in the requirement part of subclause 4.8.1.2 of TBR21:

“The dial tone detector of the TE shall be possible to disable in accordance with the supplier’s instructions in order to allow automatic dialling without dial tone detection in compliance with subclause 4.8.1.1.”

Purpose: To check whether the dial tone detection can be disabled on a TE supporting automatic dialling with dial tone detection in accordance with the supplier’s instructions. The tests consist of disabling  the tone detector and performing the tests described in TBR21 , subclause A.4.8.1.1.

Note:

There is no need for additional testing if the TE supports both automatic dialling techniques, i.e. with and without dial tone detection, and the setting of such functions is described in the instructions to the TE. The TE normally subjects to both tests in TBR21,  subclauses A.4.8.1.1 and A.4.8.1.2, without amendments.

Measurement principle: The same as in TBR21, subclause A.4.8.1.1.

Measurement execution: The same as in TBR21, subclause A.4.8.1.1.

Formal processing: None

Verdict:    If the dialling with dial tone detection facility can be disabled in accordance with supplier’s instructions and the TE successfully passed the test in TBR21, subclause A.4.8.1.1,  then Pass; otherwise Fail.

Guidance: None

A.3.2	Requirements Table (TBR-RT)

The requirements table of TBR 21, Appendix  B is still applicable.