ATAAB  ADVISORY NOTE

TRAC Analogue Type Approval Advisory Board

Proposed

ATAAB Advisory Note Number: CZ 02

Date: 	1999-06-30

Subject:	Certain characteristics implications on the inter-working of terminals connected to certain NTP.

APPLICABILITY

This note is applicable for Terminal Equipment intended for connection to the Public Switched Telephone Networks in the Czech Republic operated by ČESKÝ TELECOM, a.s., in addition to:

X 	"CTR 21"

This note contains specific advice concerning the relationship between the requirements  and tests

of CTR21 and the range of network termination points parameters encountered in the Czech Republic.

Appendixes to this Advisory Note:

A:	Additional requirements and tests for attachment to the Public Switched Telephone Network in the Czech Republic operated by ČESKÝ TELECOM, a.s. - Ringing signal detector sensitivity

B: 	Additional requirements and tests for attachment to the Public Switched Telephone Network in the Czech Republic operated by ČESKÝ TELECOM, a.s. - Loop current characteristics

C: 	Additional requirements and tests for attachment to the Public Switched Telephone Network in the Czech Republic operated by ČESKÝ TELECOM, a.s. - DC characteristics

D: 	Additional requirements and tests for attachment to the Public Switched Telephone Network in the Czech Republic operated by ČESKÝ TELECOM, a.s. - DTMF signalling: Tone and Pause duration

In consideration of the following:

-	ATAAB Advisory Notes Nr. 003 and 004 contain specific advices concerning some requirements and tests. The explicitly cited parameters do not cover all parameters that may influence successful  interworking of terminals designed to meet TBR21 with PSTN operated by ČESKÝ TELECOM, a.s. in the Czech Republic;

-	The additional parameters that may prevent regular interworking were found as results of performed analyses of PSTN network termination points in the Czech Republic and cover the following: ringing signal detector sensitivity, certain loop current characteristics,  DC characteristics and DTMF tone and pause  duration;

-	Though the extend of objectionable NTPs is limited  to those connected to  older digital telephone exchanges called E-10 (from mid 80´s), to  many implemented PCM type access equipment and some access concentrator types (altogether 10 to 20% of all NTPs), the inter-working issue cannot be omitted as some of the mentioned network equipment are still being installed and also are implemented in major cities, where the density of non-voice terminals falling into the scope of TBR21 is higher then elsewhere. The number of NTPs connected to “E10s” decreases but they are expected to be in operation until 2005. Many of the PCM access systems should  operate even longer time, beyond  2005;

-	Simple referring to EN 300 001 Czech national parameter values as advises ATAAB AN 003 would require significant changes in design and testing of the TEs in many cases and therefore it is appropriate to define new compromised values  that should satisfy inter-working requirements of a vast majority of the objectionable NTPs.

ATAAB advises the following:

To ensure interworking with all NTPs  of Public Switched Telephone Network in the Czech Republic operated by ČESKÝ TELECOM, a.s., the TE shall, in addition to the requirements  of TBR21 (CTR21), subclauses  4.5, 4.6.2, 4.7.1, 4.8.2.4 and 4.8.2.5 comply with the requirements found in Appendixes  A, B, C and D of this Advisory Note.

The relevant requirements related to the remaining,  vast majority of NTPs are identical with requirements as stated in TBR21 (CTR21), subclauses 4.5, 4.6.2, 4.7.1, 4.8.2.4 and 4.8.2.5, if not otherwise stated in other Advisory Notes.

It is the responsibility of the supplier/manufacturer to provide information for users as to whether the Terminal Equipment complies with the additional requirements for the part of Public Switched Telephone Network operated by ČESKÝ TELECOM, a.s. as specified in this Advisory Note.

Appendixes A, B, C and D also specify the method to assess compliance with the additional requirement, including reference to the additional tests to be performed to dynamically assess compliance with the additional requirements.

ATAAB ADVISORY NOTE

TRAC Analogue Type Approval Advisory Board

Appendix  A

to

ATAAB Advisory Note Number: 00x (CZ02)

Subject:	Additional requirements and tests for attachment to the Public Switched Telephone Network in the Czech Republic operated by ČESKÝ TELECOM, a.s. - Ringing signal detector sensitivity

A.1	INTRODUCTION

Terminal Equipment approved to CTR 21 may not inter-work properly with some of the NTPs of the Public Switched Telephone Network in the Czech Republic operated by ČESKÝ TELECOM, a.s. .

This Appendix  specifies requirements to which a TE shall comply, in addition to the requirements of CTR 21 in order to inter-work properly with those NTP which connects the TE to some of the PCM type of access equipment implemented in the network, especially if the access line is longer.

It also specifies the method to assess compliance with these requirements, including reference to additional tests to be performed to dynamically assess compliance with the additional requirements.

A.2	NORMATIVE REFERENCES

[1]	TBR21; Terminal Equipment (TE). Attachment requirements for pan-European approval for connection to the analogue Public Switched Telephone Networks (PSTNs) of TE (excluding TE supporting the voice Telephony Service) in which network addressing, if provided, is by means of Dual Tone Multi-Frequency (DTMF) signalling. ETSI, First Edition, 1998.

[2]	EN 300 001; Attachments to Public Switched Telephone Network (PSTN); General technical requirements for equipment connected to

an analogue subscriber interface in the PSTN. ETSI, , V.1.5.1, October 1998.

A.3	REQUIREMENTS and ASSOCIATED TESTS

A.3.1	Ringing signal detector sensitivity (TBR 21 subclause 4.5)

Requirement: If a ring detect function is provided and enabled, the TE shall be able to respond to ringing signals of 30 Vrms at 25 Hz and 50 Hz with a cadence of 1 s ON and 5 s OFF, superimposed on a 20 VDC feeding voltage.

The response shall be as stated by the supplier.

If the TE fail in this test the manufacturer/supplier should warn to users about the TE inter-working restrictions.

Test: 	The test shall be conducted according to Clause A.3.2 below. The test is based on TBR21,  subclause A.4.5.

Purpose:	To determine the ability of the TE to respond as stated to ringing signals as specified by the supplier.

Measurement principle:

Preamble:	Set the TE in quiescent state with answering facility enabled.

Test state:	Quiescent state.

Test configuration:

Figure A.1  id:voltage.ds4

DC feeding arrangement: Feed Voltage = 20 V DC.

Measurement points:	The ringing signals shall have a sinusoidal source of  25 Hz and 50 Hz and a cadence of 1 s ON and 5 s OFF.

UTE = 30 Vrms

Safety Warning:	This test presents the potential for a shock hazard. Ensure satisfactory   safety precautions are implemented to reduce the risk of electric shock.

Measurement execution:

Using the test configuration shown in figure A.1, apply, the ringing signal described in "Measurement points" to the circuit to determine whether it is detected by the TE as stated by the supplier.

Formal processing:	None.

Verdict:	If the TE detects signals described above in "Measurement points" then Pass; if the TE detects only the ringing signal described in "Measurement points" of TBR21, subclause A.4.5 then Pass but there is a reason for manufacturer’s/supplier’s warning to the TE users; else Fail.

Guidance:	For automatic answering TE, after the stimulation to cause the seizure, the requirement stated in TBR 21, subclause 4.6.2 and its associated test case apply.

A.3.2	Requirements Table (TBR-RT)

The requirements table of TBR 21, Appendix  B is still applicable.

ATAAB ADVISORY NOTE

TRAC Analogue Type Approval Advisory Board

Appendix  B

to

ATAAB Advisory Note Number: 00x (CZ02)

Subject:	Additional requirements and tests for attachment to the Public Switched Telephone Network in the Czech Republic operated by ČESKÝ TELECOM, a.s.- Loop current characteristics

B.1	INTRODUCTION

Terminal Equipment approved to CTR 21 may not inter-work properly with some of the NTPs of the Public Switched Telephone Network of the Czech Republic (operated by ČESKÝ TELECOM, a.s.).

This Appendix  specifies requirements to which a TE shall comply, in addition to the requirements of CTR 21 in order to inter-work properly with those NTPs, which connects the TE  to older digital exchange E-10.

It also specifies the method to assess compliance with these requirements, including reference to additional tests to be performed to dynamically assess compliance with the additional requirements.

B.2	NORMATIVE REFERENCES

[1]	TBR21; Terminal Equipment (TE). Attachment requirements for pan-European approval for connection to the analogue Public Switched Telephone Networks (PSTNs) of TE (excluding TE supporting the voice Telephony Service) in which network addressing, if provided, is by means of Dual Tone Multi-Frequency (DTMF) signalling. ETSI, First Edition, 1998.

[2]	EN 300 001; Attachments to Public Switched Telephone Network (PSTN); General technical requirements for equipment connected to

an analogue subscriber interface in the PSTN. ETSI, , V.1.5.1, October 1998.

B.3	REQUIREMENTS and ASSOCIATED TESTS

B.3.1 Loop current characteristics (TBR21 subclause 4.6.2)

Requirement: Terminals intended for connection to telephone exchange ”E10” shall    perform faster transition to the loop steady state during the seizing the line as indicated by  the additional line (Rf = 1600 W) in Table B.1 below.

Other requirements related to loop current characteristics (TBR 21 subclause 4.6.2) that are not in conflict with this requirement remain as stated in TBR21.

If the TE fails in this additional requirement for Rf = 1600 W the manufacturer/supplier should warn to users about the TE inter-working restrictions.

| Condition | Requirements |
| --- | --- |
| Feeding voltage | Feeding resistance | Time (ms) | Current (mA) |
| Vf | Rf | t1-t0 | t2-t01 | t3-t01 | If1 | If2 |
| 50VDC | 3,2 k | 30 | 500 | 1200 | 13,1 | 12,8 |
| 50VDC | 1600 | 12 | 500 | 1 200 | 20 | 20 |
| 50VDC | 230 | 20 | 500 | 1200 | 49,6 | 49,6 |

Table  B.1 (modified Table 4/TBR21): TE current characteristics with feeding resistors,

which are used during the loop steady state

Test: The test shall be conducted according to TBR21,  subclause A.4.6.2, Test 2, with an additional feed resistance Rf = 1600 W and requirements as shown in Table B.1 above.

Verdict:  If the TE complies with requirements in TBR21, subclause 6.4.2, and with the additional requirement in this Appendix then Pass; if  the TE complies with requirements in TBR21, subclause 6.4.2, and fails in  the additional requirement in this Appendix then Pass but there is a reason for manufacturer’s/supplier’s warning to the TE users; else the verdict follows relevant provisions in TBR21, subclause A.4.6.2.

B.3.2	Requirements Table (TBR-RT)

The requirements table of TBR 21, Appendix  B is still applicable.

ATAAB ADVISORY NOTE

TRAC Analogue Type Approval Advisory Board

Appendix  C

to

ATAAB Advisory Note Number: 00x (CZ02)

Subject:	Additional requirements and tests for attachment to the Public Switched Telephone Network in the Czech Republic operated by ČESKÝ TELECOM, a.s. - DC characteristics

C.1	INTRODUCTION

Terminal Equipment approved to CTR 21 may not inter-work properly with some of the NTPs of the Public Switched Telephone Network of the Czech Republic (operated by ČESKÝ TELECOM, a.s.).

This Appendix  specifies requirements to which a TE shall comply, in addition to the requirements of CTR 21 in order to inter-work properly with those NTP which connects the TE  to older digital exchange designated E-10  and to PCM type of access equipment via a longer access line.

It also specifies the method to assess compliance with these requirements, including reference to additional tests to be performed to dynamically assess compliance with the additional requirements.

C.2	NORMATIVE REFERENCES

[1]	TBR21; Terminal Equipment (TE). Attachment requirements for pan-European approval for connection to the analogue Public Switched Telephone Networks (PSTNs) of TE (excluding TE supporting the voice Telephony Service) in which network addressing, if provided, is by means of Dual Tone Multi-Frequency (DTMF) signalling. ETSI, First Edition, 1998.

[2]	EN 300 001; Attachments to Public Switched Telephone Network (PSTN); General technical requirements for equipment connected to

an analogue subscriber interface in the PSTN. ETSI, , V.1.5.1, October 1998.

C.3	REQUIREMENTS and ASSOCIATED TESTS

C.3.1  DC characteristics (TBR21 subclause 4.7.1)

Requirement: Due to differences between the DC characteristics specified in Chapter 2 of EN 300 001 and in TBR21, subclause 4.7.1,  the reach of terminals with DC characteristics complying with TBR21 connected to PCM type access equipment via a longer access line is limited to about 85% (80 to 140 ohm less) of the line range.

The confrontation of both TBR21 and original Czech  DC characteristics is in figure 1. The  Czech DC characteristics is the lower line on the figure going through points (5,2 V; 0 mA),  (8,0 V; 25 mA), (13,4 V, 42 mA) and (19,2 V; 60 mA). The terminals with limited reach on the access line are those the DC characteristics of which fall into the grey area marked by points H, A, B, C, J, I and H on figure C.1 below. If the TE shows values this grey area the manufacturer/supplier should warn to users about the TE inter-working restrictions.

Test: The test shall be conducted according to TBR21, Clause A.4.7.1.

Verdict: If the DC voltage/current characteristics are within limits given by points G, H, I, J, C and D and then E,K and F on figure C.1 above then Pass; if the DC voltage/current characteristics are within limits given in table 5 and shown in figure 5 in TBR21 but are above the limits given by points H, I, J within the area marked by points H, A, B, C, J, I, and H then Pass but there is a reason for manufacturer’s/supplier’s warning to the TE users; else the verdict follows relevant provisions in TBR21, subclause A.4.7.1.

C.3.2	Requirements Table (TBR-RT)

The requirements table of TBR 21, Appendix  B is still applicable.

ATAAB ADVISORY NOTE

TRAC Analogue Type Approval Advisory Board

Appendix  D

to

ATAAB Advisory Note Number: 00x (CZ02)

Subject:	Additional requirements and tests for attachment to the Public Switched Telephone Network in the Czech Republic operated by ČESKÝ TELECOM, a.s. - DTMF signalling: Tone and Pause duration

D.1	INTRODUCTION

Terminal Equipment approved to CTR 21 may not inter-work properly with some of the NTP of the Public Switched Telephone Network of the Czech Republic (operated by ČESKÝ TELECOM, a.s.).

This Appendix specifies requirements to which a TE shall comply, in addition to the requirements of CTR 21 in order to inter-work properly with those NTPs, which connects the TE to older digital exchange designated E-10.

It also specifies the method to assess compliance with these requirements, including reference to additional tests to be performed to dynamically assess compliance with the additional requirements.

D.2	NORMATIVE REFERENCES

[1]	TBR21; Terminal Equipment (TE). Attachment requirements for pan-European approval for connection to the analogue Public Switched Telephone Networks (PSTNs) of TE (excluding TE supporting the voice Telephony Service) in which network addressing, if provided, is by means of Dual Tone Multi-Frequency (DTMF) signalling. ETSI, , V.1.5.1, October 1998.

[2]	EN 300 001; Attachments to Public Switched Telephone Network (PSTN); General technical requirements for equipment connected to

an analogue subscriber interface in the PSTN. ETSI, V.1.5.1, October 1998.

D.3	REQUIREMENTS and ASSOCIATED TESTS

D.3.1  DTMF tone duration (TBR21 subclause 4.8.2.4)

Requirement: Reliable interpretation of DTMF dialling by the receivers in the exchange requires the TE to  send any individual DTMF tone  combination not less than 90 ms. The time shall be measured from the time when the tone reaches 90 % of its steady-state value, until it has dropped to 90 % of its steady-state value.

If the tone duration is shorter the manufacturer/supplier should warn to users about the TE inter-working restrictions.

Test: The test is based on TBR21, subclause A.4.8.2.4.

Purpose: To check whether the TE sends DTMF signals of the appropriate duration. This requirement applies only to a TE with an automatic dialling function. It applies when the TE is in automatic dialling mode.

The TE shall provide a setting whereby the duration of any individual DTMF tone combination shall be at least 90 ms measured from the time when the tone level has reached 90 % of its steady-state value (without interruption), until it has dropped to 90 % of its steady-state value.

Measurement principle:

Preamble: Set the TE in loop state.

Test state: Automatic dialling. Tone signal duration according to supplier's instructions.

Test configuration:

Figure D.1

DC feeding arrangement:  Feed voltage: 50 V. Feed resistance: 850 Ohm.

AC termination of TE:  ZR.

Measurement points: Where all characters of table 9 are available, select digits A, 6, 8 and *. Else if all numerals are available, select digits 3, 5, 7 and 0, else select all available digits.

Measurement execution:

Set tone signalling duration according to supplier's instructions. The TE is set in the loop state, transmitting DTMF signals to the line. Capture the waveform of the DTMF signal.

Formal processing: In this formal processing, three waveforms derived from the measured waveform are used. These are referred to as waveforms A, B and C.

Determine waveform A such that at any time the instantaneous value of waveform A is equal to the absolute value of difference between the value of the measured waveform at that time and the mean value of the measured waveform over a period of 10 ms centred on that time.

Determine waveform B such that at any time its value is the greater of the linear

interpolation of the maxima of waveform A, and waveform A.

Determine waveform C such that at any time its value is the greater of the linear

interpolation of the maxima of waveform B, and waveform B.

Determine the reference level such that it is 90% of the highest level which

waveform C exceeds for 20 ms during the burst.

The duration of the burst is the duration of the greatest period of time for which

waveform C exceeds the reference level.

Verdict: If all bursts have a duration greater than or equal to 90 ms then Pass; if all bursts have a duration greater than or equal to 70 ms but shorter than 90 ms then Pass, but there is a reason for manufacturer’s/supplier’s warning to the TE users. If any burst has a duration of less than 60 ms then Fail;

The test shall be repeated ten times for any burst for which the duration is between 60 and 70 ms and the mean duration calculated. If the mean duration for all such bursts is greater than or equal to 65 ms then Pass, but there is a reason for manufacturer’s/supplier’s warning to the TE users; else Fail.

Guidance: The repeatability of this test is intrinsically poor because the measured duration of the burst depends on the phase relationship of the tones.Therefore averaging is needed for borderline cases. The relationship between the measured waveform and waveforms A, B and C is shown in TBR21, figure A.27 and the following figure D.2.

Figure D.2 (identical with TBR21, figure A.27)

D.3.2      DTMF Pause duration (TBR21 subclause 4.8.2.5)

Requirement: Reliable interpretation of DTMF dialling by the receivers in the exchange requires the TE to provide minimum pause duration between any individual DTMF tone combination  not less than 90 ms. The time shall be measured from the time when the tone has dropped to 10 % of its steady-state value, until it has risen to 10 % of its steady-state value.If the pause duration is shorter the manufacturer/supplier should warn to users about the TE inter-working restrictions.

Test: The test is based on TBR21, subclause A.4.8.2.5.

Purpose: To check whether the TE sends DTMF signals with the appropriate pauses. This requirement applies only to a TE with an automatic dialling function.The TE shall provide a setting whereby the duration of the pause between the DTMF tone combinations shall be at least 90 ms. Time is measured from the moment when the tone has dropped to 10 % of its steady-state value, until it has risen to 10 % of its steady-state value.

Measurement principle:

Preamble: Set the TE in loop state.

Test state: Automatic dialling.

Test configuration:

Figure D.3

DC feeding arrangement: Feed voltage: 50 V. Feed resistance: 850 Ohm.

AC termination of TE: ZR .

Measurement points: Where all characters of table 9 are available, select digits A, 6, 8 and *. Else if all numerals are available, select digits 3, 5, 7 and 0, else select all available digits.

Measurement execution:

The TE is set in the loop condition, transmitting DTMF signals to line. Set pauseduration in accordance with the supplier's instructions. Capture the waveform of the sequence of bursts.

Formal processing: In this formal processing, a number of waveforms derived from the measured waveform are used. These shall be calculated independently for each burst

These are referred to as waveforms A, B, C etc.

Determine waveform A such that at any time the instantaneous value of waveform A is equal to the absolute value of difference between the value of the measured waveform at that time and the mean value of the measured waveform over a period of 10 ms centred on that time.

Determine waveform B such that at any time its value is the greater of the linear

interpolation of the maxima of waveform A, and waveform A.

Determine waveform C such that at any time its value is the greater of the linear

interpolation of the maxima of waveform B, and waveform B.

Determine the reference level such that it is 10% of the highest level which waveform C exceeds for 20 ms during the burst.

The pause between two bursts is the time between the last instant that waveform C is greater than the reference level for the first burst and the first instant that waveform C is greater than the reference level for the second burst.

Verdict: If all pauses have a duration greater than or equal to 90 ms Pass; if all pauses have a duration greater than or equal to 70 ms but shorter than 90 ms then Pass, but there is a reason for manufacturer’s/supplier’s warning to the TE users; else the verdict follows relevant provisions in TBR21, subclause A.4.8.2.5.

If any pause has duration of less than 60 ms then Fail;

If any pause has duration of between 60 ms and 70 ms then the test shall be

repeated 10 times, and the mean duration of the pause between each of the

pairs on characters calculated. If each mean duration is greater than 65 ms then Pass, but there is a reason for manufacturer’s/supplier’s warning to the TE users; otherwise Fail.

Guidance: The repeatability of this test is intrinsically poor because the measured duration of the burst depends on the phase relationship of the tones. Therefore averaging is needed for borderline cases.

D.3.3	Requirements Table (TBR-RT)

The requirements table of TBR 21, Appendix  B is still applicable.