ATAAB  ADVISORY NOTE

TRAC Analogue Type Approval Advisory Board

Proposed

ATAAB Advisory Note Number: CZ 03

Date: 	2000-03-15

Subject:	Certain characteristics implications on the inter-working of terminals connected to certain NTP.

APPLICABILITY

This note is applicable for Terminal Equipment intended for connection to the Public Switched Telephone Networks in the Czech Republic operated by ČESKÝ TELECOM, a.s., in addition to:

X 	"CTR 21"

This note contains specific advice concerning the relationship between the requirements and tests

of EN 301 437 and the range of network termination points parameters encountered in the Czech Republic.

Appendixes to this Advisory Note:

A: 	Additional requirements and tests for attachment to the Public Switched Telephone Network in the Czech Republic operated by ČESKÝ TELECOM, a.s. - Loop current characteristics

In consideration of the following:

-	ATAAB Advisory Notes Nr. 003 and 004 contain specific advices concerning some requirements and tests. The explicitly cited parameters do not cover all parameters that may influence successful interworking of terminals designed to meet EN 301 437  with PSTN operated by ČESKÝ TELECOM, a.s. in the Czech Republic;

-	The additional parameters that may prevent regular interworking were found as results of performed analyses of PSTN network termination points (NTPs) in the Czech Republic relates to certain loop current characteristics;

-	Though the extend of objectionable NTPs is limited to those connected to older digital telephone exchanges called E-10 (from mid 80´s), to many implemented PCM type access equipment and some access concentrator types (altogether 10 to 20% of all NTPs), the inter-working issue cannot be omitted as some of the mentioned network equipment are still being installed and also are implemented in major cities, where the density of voice terminals falling into the scope of EN 301 437 is higher then elsewhere. The number of NTPs connected to “E10s” decreases but they are expected to be in operation until 2005. Many of the PCM access systems should operate even longer time, beyond 2005;

-	Simple referring to EN 300 001 Czech national parameter values as advises ATAAB AN 003 would require significant changes in design and testing of the TEs in many cases and therefore it is appropriate to define new compromised values that should satisfy inter-working requirements of a vast majority of the objectionable NTPs;

-	Since many of EN 301 437 requirements refer to requirements in TBR 21; and as some of the referred requirements of TBR 21 are modified by Czech Advisory Notes of TBR 21, the provision both of Advisory Notes Number prCZ 01, rev.1 and prCZ 02, rev.1 are suitably used also by this Advisory Note;

-	The Advisory Note stated by this document is based on Advisory Note Number prCZ 02 rev.1, Appendix B including required values, test methods and verdicts.

ATAAB advises the following:

To ensure interworking with all NTPs of Public Switched Telephone Network in the Czech Republic operated by ČESKÝ TELECOM, a.s. in addition to the requirements  of EN 301 437,

-	subclause 4.8.1.2, 
the TE shall comply with the requirements found in Appendix A of Advisory Note Number prCZ 01, rev.1;

-	subclauses 4.5, 4.7.1 and 4.8.2.4, 
the TE shall comply with the requirements found in Appendixes A, C and D of Advisory Note Number prCZ 02, rev.1;

-	subclause 4.6.2, 
comply with the requirements found in Appendix A of this Advisory Note.

The relevant requirements related to the remaining, vast majority of NTPs are identical with requirements as stated in EN 301 437, subclauses 4.5, 4.6.2, 4.7.1, 4.8.1.2 and 4.8.2.4 if not otherwise stated in other Advisory Notes.

It is the responsibility of the supplier/manufacturer to provide information for users as to whether the Terminal Equipment complies with the additional requirements for the part of Public Switched Telephone Network operated by ČESKÝ TELECOM, a.s. as specified in this Advisory Note.

Appendix A also specifies the method to assess compliance with the additional requirement, including reference to the additional test to be performed to dynamically assess compliance with the additional requirement.

ATAAB ADVISORY NOTE

TRAC Analogue Type Approval Advisory Board

Appendix  A

to

ATAAB Advisory Note Number: 00x (CZ03)

Subject:	Additional requirements and tests for attachment to the Public Switched Telephone Network in the Czech Republic operated by ČESKÝ TELECOM, a.s.- Loop current characteristics

A.1	INTRODUCTION

Terminal Equipment approved to EN 301 437 may not inter-work properly with some of the NTPs of the Public Switched Telephone Network of the Czech Republic (operated by ČESKÝ TELECOM, a.s.).

This Appendix specifies requirements to which a TE shall comply, in addition to the requirements of EN 301 437 in order to inter-work properly with those NTPs, which connects the TE to older digital exchange E-10.

It also specifies the method to assess compliance with these requirements, including reference to additional tests to be performed to dynamically assess compliance with the additional requirements.

A.2	NORMATIVE REFERENCES

[1]	EN 301 437; Terminal Equipment (TE); Attachment requirements for pan-European approval for connection to the analogue Public Switched Telephone Networks (PSTNs) of TE supporting the voice telephony service in which network addressing, if provided, is by means of Dual Tone Multi-Frequency (DTMF) signalling. ETSI, V1.1.1, July 1999.

[2]	TBR21; Terminal Equipment (TE); Attachment requirements for pan-European approval for connection to the analogue Public Switched Telephone Networks (PSTNs) of TE (excluding TE supporting the voice Telephony Service) in which network addressing, if provided, is by means of Dual Tone Multi-Frequency (DTMF) signalling. ETSI, First Edition, 1998.

[3]	EN 300 001; Attachments to Public Switched Telephone Network (PSTN); General technical requirements for equipment connected to an analogue subscriber interface in the PSTN. ETSI, V.1.5.1, October 1998.

[4]	ATAAB Advisory Notes Number: prCZ 01 rev.1, 1999-06-03

[5]	ATAAB Advisory Notes Number: prCZ 02 rev.1, 1999-06-03

A.3	REQUIREMENTS and ASSOCIATED TESTS

A.3.1 Loop current characteristics (EN 301 437subclause 4.6.2)

Requirement: Terminals intended for connection to telephone exchange ”E10” shall perform faster transition to the loop steady state during the seizing the line as indicated by the additional line (Rf = 1600 W) in Table A.1 below.

Other requirements related to loop current characteristics (EN 301 437 subclause 4.6.2) that are not in conflict with this requirement remain as stated in EN 301 437.

If the TE fails in this additional requirement for Rf = 1600 W the manufacturer/supplier should warn to users about the TE inter-working restrictions.

| Condition | Requirements |
| --- | --- |
| Feeding voltage | Feeding resistance | Time (ms) | Current (mA) |
| Vf | Rf | t1-t0 | t2-t01 | t3-t01 | If1 | If2 |
| 50V DC | 2,8 k | 30 | 500 | 1200 | 13,1 | 12,8 |
| 50V DC | 2,3 k | 30 | 500 | 1200 | 18,2 | 17,8 |
| 50V DC | 1600 | 12 | 500 | 1 200 | 20 | 20 |
| 50V DC | 230 | 20 | 500 | 1200 | 49,6 | 49,6 |

Table A.1 (modified Table 1/EN 301 437):	TE current characteristics with feeding resistors, which are used during the loop steady state

Test: The test shall be conducted according to EN 301 437, subclause A.4.6.2, with an additional feed resistance Rf = 1600 W and requirements as shown in Table A.1 above.

Verdict: If the TE complies with requirements in EN 301 437, subclause 6.4.2, and with the additional requirement in this Appendix then Pass. If the TE complies with requirements in EN 302 437, subclause 6.4.2, and fails in the additional requirement in this Appendix then Pass but there is a reason for manufacturer’s/supplier’s warning to the TE users; else the verdict follows relevant provisions in EN 301 437, subclause A.4.6.2.

A.3.2	Requirements Table (RT)

The requirements table of EN 301 437, Appendix B is still applicable.