ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 048 rev. 2

Date:	1998-09-03

Subject:	Handling of glitches when performing tests B.2.4 and B.2.6.1 of TBR 3

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

X	CTR 33 (Commission Decision 98/521/EC)

In consideration of the following:

-	When performing tests B.2.4 and B.2.6.1 of TBR 3 glitches may appear, causing the measured pulse to fall outside the defined mask;

-	Such glitches may be caused by random noise, and cannot be avoided;

-	The assessment of whether the IUT produces glitches can therefore only be made based on whether such glitches appear in a consistent way;

-	TBR 33 references the layer 1 tests of TBR 3.

ITAAB advises the following:

When performing tests B.2.4 and B.2.6.1 of TBR 3 to verify compliance with the layer 1 requirements of TBR 3 or TBR 33, several pulses (min. 40, max. 80) shall be measured to decide whether the pulse form remains within the defined mask.

If a glitch is found during this execution, a preliminary FAIL verdict shall be allocated for that execution. If no glitches are found on two subsequent executions, the glitches are not consistent, and the final verdict PASS can be given for the execution of the test.