ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 053 rev. 2

Date:	1998-09-03

Subject:	TTCN description of preamble PRE_F3_CP

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

X	CTR 33 (Commission Decision 98/521/EC)

For the purposes of the above described applicability, this note specifically contains amendments to:

TBR 3, Amendment A1, December 1997: Attachment requirements for terminal equipment to connect to an ISDN using ISDN basic access.

TBR 33, December 1997: Attachment requirements for packet mode terminal equipment to connect to an ISDN using ISDN basic access.

In consideration of the following:

-	The preamble PRE_F3_CP in TBR 3/A1 and in TBR 33 is used in various layer 1 tests to check that IUT is brought to state F3. Within this preamble, IUT goes to F7 in order to check if a TEI is assigned or not. Then the IUT shall go back to F3 when receiving Info 0;

-	Subtree "F7toF3" in PRE_F3_CP handles the situation of bringing the IUT from state F7 to state F3;

-	Problems may occur for IUTs, which are unstable in state F3, when performing subtree "F7toF3" in PRE_F3_CP in TBR 3/A1 or TBR 33.

ITAAB advises the following:

To avoid problems with IUTs, which are unstable in state F3, a change has to be performed to the description of Subtree "F7toF3" in PRE_F3_CP, when verifying compliance with CTR 3, Amendment 1 or CTR 33.

Subtree F7toF3 of preamble PRE_F3_CP shall be replaced with the following:

| F7toF3 |
| --- |
|  | 23 |
| START TAC |
|  | 24 | L2 | L!Info_0 | I0 |
| 25 |
| ?TIMEOUT TAC |
| F |
|  | 26 |
| L?Info_3 | I3_BASIC |
| 27 |
| GOTO L2 |
|  | 28 |
| L?Info_0 CANCEL TAC, START T4 | I0 |
| 29 | L3 | L!Info_0 | I0 |
| 30 |
| ?TIMEOUT T4 |
| (P) |
|  | 31 |
| L?Info_0 | I0 |
| 32 |
| GOTO L3 |
|  | 29 |
| START T4Vmin, START T4 |
|  | 30 | L3 | L!Info_0 | I0 |
| 31 |
| ?TIMEOUT T4Vmin |
|  | 32 | L4 | L!Info_0 | I0 |
| 33 |
| ?TIMEOUT T4 |
| (P) |
|  | 34 |
| L?Info_0 | I0 |
| 35 |
| GOTO L4 |
|  | 36 |
| L?Info_1 | I1 |
| 37 |
| CANCEL T4 |
|  | 38 | L5 | L!Info_0 | I0 |
| 39 |
| L?Info_0 | I0 | (P) |
|  | 40 |
| L?Info_1 | I1 |
| 41 |
| GOTO L5 |
|  | 42 |
| L?Info_0 | I0 |
| 43 |
| GOTO L3 |