ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 054 rev. 4

Date:	1999-04-26

Subject:	Additional French attachment requirements for ISDN

APPLICABILITY

This note is specifically applicable for proper interworking with the French Euro-NUMERIS network in addition to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

X	CTR 4 Amendment 1 (Commission Decision 98/520/EC)

X	CTR 33 (Commission Decision 98/521/EC)

X	CTR 34 (Commission Decision 98/518/EC)

Annexes to this Advisory Note:

A:	Additional requirements and tests for attachment to the France Telecom ISDN Network, Euro-NUMERIS

B:	Requirement Table for Additional requirements for attachment to the France Telecom ISDN Network, Euro-NUMERIS

C:	Information about some of the differences in the Euro-NUMERIS Network not imposing special attachment requirements

In consideration of the following:

-	The France Telecom ISDN Network offers two kinds of access : Euro-NUMERIS+ and Euro-NUMERIS,

- Euro-NUMERIS+ is fully compliant with the specifications for EURO-ISDN,

- Euro-NUMERIS is not fully compliant with the specifications for EURO-ISDN;

-	A TE approved according to CTR 3 Amendment 1, CTR 4 Amendment 1, CTR 33 or CTR 34,

-	can be connected to Euro-NUMERIS+ network,

-	is required to comply with some additional attachment requirements to connect to Euro- NUMERIS network.

ITAAB advises the following:

To be able to interwork properly with the France Telecom Euro-NUMERIS network, the TE shall, in addition to the requirements of CTR 3 Amendment 1, CTR 4 Amendment 1, CTR 33 or CTR 34 as applicable, comply with the requirements found in Annex A of this Advisory Note.

Conformity to these variations is no more a subject to approval.

It is the responsibility of the supplier to inform users whether the TE is compatible or not with the Euro-NUMERIS network.

Annex A also specifies the method to assess compliance with these requirements, including reference to additional tests to be performed to dynamically assess compliance with the additional requirements.

A summary of these additional requirements is provided in the Requirement Table found in Annex B. This Requirement Table also specifies whether it is essential to implement the requirements in all circumstances, or whether the requirement is dependant on the manufacturer having chosen to support a particular optional functionality.

The Requirement Table also provides the means to undertake the static assessment of compliance with these requirements, and to select the appropriate tests for the dynamic assessment. To be used for this purpose, the manufacturer shall fill in the Requirement Table according to the capabilities of the implementation.

Some of the differences in the Euro-NUMERIS network do not impose requirements to the TE according to the Terminal Directive, 98/13/EC. ITAAB however considers the information about some of these differences to be valuable to the Implementors.

Information about these differences has therefore been included in Annex C to this Advisory Note.