ITAAB

TRAC ISDN Type Approval Advisory Board

Annex A (Normative)

to

ITAAB Advisory Note Number: 054 rev. 4

Date:	1999-04-26

Subject:	Additional requirements and tests for attachment to the France Telecom ISDN Network, Euro-NUMERIS

INTRODUCTION

The France Telecom Euro-NUMERIS network is not fully compliant with Euro-ISDN.

Some of the differences impose additional requirements to the TE according to the Terminal Directive, 98/13/EC.

This Annex specifies the requirements to which a TE shall comply, in addition to the requirements of CTR 3 Amendment 1 (Commission Decision 98/515/EC), CTR 4 Amendment  1 (Commission Decision 98/520/EC), CTR 33 (Commission Decision 98/521/EC) or CTR 34 (Commission Decision 98/518/EC), as applicable, in order to interwork properly with the France Telecom Euro-NUMERIS network. It also specifies the method to assess compliance with these requirements, including reference to additional tests to be performed to dynamically assess compliance with the additional requirements.

NORMATIVE REFERENCES

CTR 3 Amendment 1, Commission Decision 98/515/EC of 17 June 1998 on a common technical regulation for the pan-European Integrated Services Digital Network (ISDN) Basic Access (Amendment 1).

CTR 4 Amendment 1, Commission Decision 98/520/EC of 17 June 1998 on a common technical regulation for the pan-European Integrated Services Digital Network (ISDN) Primary Rate Access (Amendment 1).

CTR 33, Commission Decision 98/521/EC of 17 June 1998 on a common technical regulation for ISDN packet mode using ISDN Basic Access .

CTR 34, Commission Decision 98/518/EC of 17 June 1998 on a common technical regulation for ISDN packet mode using ISDN Primary rate Access.

TBR 3 (1995); Integrated Services Digital Network (ISDN); Attachment requirements for terminal equipment to connect to an ISDN using ISDN basic access.

TBR 4 (1995); Integrated Services Digital Network (ISDN); Attachment requirements for terminal equipment to connect to an ISDN using ISDN primary rate access.

TBR 3/A1 (1997); Integrated Services Digital Network (ISDN); Attachment requirements for terminal equipment to connect to an ISDN using ISDN basic access.

TBR 4/A1 (1997); Integrated Services Digital Network (ISDN); Attachment requirements for terminal equipment to connect to an ISDN using ISDN primary rate access.

TBR 33 (1997); Integrated Services Digital Network (ISDN); Attachment requirements for packet mode terminal equipment to connect to an ISDN using ISDN basic access.

TBR 34 (1997); Integrated Services Digital Network (ISDN); Attachment requirements for packet mode terminal equipment to connect to an ISDN using ISDN primary rate access.

ETS 300 102-1 (1992); Integrated Services Digital Network (ISDN); User-network interface layer 3 Specifications for basic call control.

LAYER 3 REQUIREMENTS

RESTART PROCEDURE MODIFICATION

Requirement: 
A terminal complying with CTR 3 Amendment 1 (1(, CTR 4 Amendment 1 (2(, CTR 33 [3] or CTR 34 [4] shall not use the RESTART procedure.

Justification: 
The Euro-NUMERIS network does not handle the RESTART procedure. According to ETS 300 102-1 (11(, no calls shall be placed or accepted over the channel or interface until a RESTART ACKNOWLEDGE message is received after a RESTART has been sent.Therefore it is not possible to establish a call, if the TE has used the RESTART procedure.

Assessment of compliance: 
Static assessment of the information provided in the Requirement Table, completed for the implementation to be assessed.

STATUS ENQUIRY PROCEDURE MODIFICATION

Requirement: 
A terminal complying with CTR 3 Amendment 1 (1(, CTR 4 Amendment 1 (2(, CTR 33 [3] or CTR 34 [4] shall only use the STATUS ENQUIRY procedure in the case where a fault condition has been detected, and where permitted recovery procedures result in call clearing.

Justification: 
The Euro-NUMERIS network does not handle the Status Enquiry procedure. A received STATUS ENQUIRY will be ignored by the network. Use of the Status Enquiry by the terminal may result in the call being cleared. In cases, where a fault condition has been detected, and where the permitted recovery procedures will result in call clearing in any case, the use of the Status Enquiry procedure will not result in additional calls being cleared.

Assessment of compliance: 
Static assessment of the information provided in the Requirement Table, completed for the implementation to be assessed.

CODESET SHIFT PROCEDURE MODIFICATION

Requirement: 
A terminal complying with CTR 3 Amendment 1 (1(, CTR 4 Amendment 1 (2(, CTR 33 [3] or CTR 34 [4]  and using the Codeset Shift procedure, shall use information element codes different from those used by Euro-NUMERIS, which are defined in Table A.1. Furthermore these codes must be arranged in increasing order.

Justification: 
Since the Euro-NUMERIS network ignores the Code Shift information element, the network will misinterprete the information elements under another codeset, using the same coding values as used by Euro-NUMERIS under codeset 0.

Assessment of compliance: 
Static assessment of the information provided in the Requirement Table, completed for the implementation to be assessed.

Table A.1: Information elements and coding used by Euro-NUMERIS

| Coding of information identifier bits (hex) | Information element |
| --- | --- |
| 00 | Segmented message |
| 04 | Bearer Capability |
| 08 | Cause |
| 10 | Call identity |
| 14 | Call state |
| 18 | Channel identification |
| 1C | Facility |
| 1E | Progress indicator |
| 20 | National facility |
| 24 | User operating mode |
| 27 | Notification indicator |
| 28 | Display |
| 29 | Date/time |
| 2C | Keypad facility |
| 34 | Signal |
| 6C | Calling party number |
| 6D | Calling party subaddress |
| 70 | Called party number |
| 71 | Called party subaddress |
| 74 | Redirecting number |
| 76 | User to PCS information |
| 77 | PCS to user information |
| 79 | Restart indicator |
| 7A | User to user facility |
| 7C | Low layer compatibility |
| 7D | High layer compatibility |
| 7E | User to user information |

EXTENSION BIT MANAGEMENT PROCEDURES MODIFICATION

Requirement: 
A terminal complying with CTR 3 Amendment 1 (1(, CTR 4 Amendment 1 (2(, CTR 33 [3] or CTR 34 [4] must not use the extension bit management procedure for mandatory information elements except for the cases explicitly described for the Bearer capability information element in Figure A.1.

Justification: 
The Euro-NUMERIS network does not handle the extension bit management procedure for information elements, except for those cases explicitly provided for. In mandatory information elements, the extension bit management procedure shall therefore only be used where the network accepts it.

Assessment of compliance: 
Static assessment of the information provided in the Requirement Table, completed for the implementation to be assessed.

| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bearer capability |
|  | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | Octet 1 |
|  | Information element identifier |
|  | Length of the bearer capability contents | Octet 2 |
| 0 | 0 | 0 | 0 | x | x | x | x |
|  | 1 ext | Coding standard | Information transfer capability | Octet 3 |
| 1 ext | Transfer mode | Information transfer rate | Octet 4 |
| 0/1 | Layer 1 ident. | User information layer 1 protocol | Octet 5 |
| ext | 0 | 1 |
| 0/1 ext | Synch./ asynch. | Negotiation | User rate | Octet 5a |
| 0/1 ext | Intermediate rate | NIC on Tx | NIC on RX | Flow control on Tx | Flow control on Rx | 0 | Octet 5b |
| 0/1 ext |

Number of stop bits

|  | Number of data bits | Parity | Octet 5c |
| --- | --- | --- | --- |
| 1 ext | Duplex mode | Modem type | Octet 5d |
| 1 | 1 | 0 | User information layer 2 protocol | Octet 6 |
| ext | Layer 2 ident. |
| 1 | 1 | 1 | User information layer 3 protocol | Octet 7 |
| ext | Layer 3 ident. |

Figure A.1: Bearer capability information element

TYPE OF NUMBER IN CALLED PARTY NUMBER INFORMATION ELEMENT

Requirement: 
When establishing a call, a terminal complying with CTR 3 Amendment 1 (1( or CTR 4 Amendment 1 (2( shall be able to use the coding "Unknown" (000B) for the Type of Number field in bits 7 to 5 of octet 3 in the Called Party Number information element.

Justification: 
The Euro-NUMERIS network does not handle other values than "unknown" for the Type of Number field in the Called Party Number information element. Attempts to establish a call using a different value will be rejected by the network.

Assessment of compliance: 
Static assessment of the information provided in the Requirement Table, completed for the implementation to be assessed.