ITAAB

TRAC ISDN Type Approval Advisory Board

Annex B (Normative)

to

ITAAB Advisory Note Number: 054 rev. 4

Date:	1999-04-26

Subject:	Requirement Table for Additional requirements for attachment to the France Telecom ISDN Network, Euro-NUMERIS

INTRODUCTION

The purpose of this Requirement Table (RT) is to state the logical inter-relationship of the various requirements stated in Annex A of this Advisory Note, and their dependence on the implementation or non-implementation of options within particular items of terminal equipment.

The contents of this RT can also perform a similar function to that of an Implementation Conformance Statement (ICS). Therefore, in order to facilitate the provision of information by the manufacturers to test laboratories and Notified Bodies, a blank column for "Support" has been added so that the RT may be copied and used as part of an ICS proforma (additional information to identify uniquely the IUT will be needed).

It is not a requirement that information is provided to laboratories and Notified Bodies in this way, and other methods for providing information may be used.

GUIDANCE FOR COMPLETION OF THE RT

For each layer, there are one or more tables of requirements.

The Number column, when taken with the table number, provides an unique identifier to each requirement (e.g., B.1/2 is item 2 in table B.1).

The Reference column lists the subclause reference in Annex A of this Advisory Note where the requirement may be found.

The Requirement column gives the clause title of the relevant Clause, supplemented by any additional information necessary to identify the requirement.

The Status column contains one of the following items:

M	support for the requirement is mandatory.

Cx	support for the requirement is mandatory if the relevant condition is met. The outcome of a condition may be any of the other status values listed.

O	support for the requirement is optional.

O.x	this status value is used for mutually exclusive or selectable options among a set. The integer "x" refer to a unique group of options within the RT. A footnote in the table where it appears state the actual requirement for each numbered group.

N/A	support for the requirement is not applicable.

The Support column is blank for the user to complete.

IMPLEMENTATION OPTIONS

The options stated in table B.1 provide conditions for the support of requirements tabled in clause B.4.

Table B.1: Implementation options table

| No. | Option | Status | Support (Y/N) | Comment |
| --- | --- | --- | --- | --- |
| 1 |

The TE is complying with CTR 3 Amendment 1

|  | O.1 |
| --- | --- |
| Used for requirements only applicable for Basic Access. |
| 2 |

The TE is complying with CTR 4 Amendment 1

|  | O.1 |
| --- | --- |
| Used for requirements only applicable for Primary Rate Access. |
| 3 |

The TE is complying with CTR 33

|  | O.1 |
| --- | --- |
| Used for requirements only applicable for Basic Access. |
| 4 |

The TE is complying with CTR 34

|  | O.1 |
| --- | --- |
| Used for requirements only applicable for Primary Rate Access. |
| 5 | The TE uses the Codeset Shift procedures | O |
| Used for layer 3 requirement |
| O.1: One or more of these options shall be supported. |

TABLES OF REQUIREMENTS

LAYER 3

Table B.2: Layer 3 requirements table

No.

Reference

| (Annex A) | Additional French Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- |
| 1 | A.3.1 | Restart procedure modification | M |
|  | 2 | A.3.2 | Status Enquiry procedure modification | M |
|  | 3 | A.3.3 | Codeset Shift procedure modification | C1 |
|  | 4 | A.3.4 | Extension Bit Management procedure modification | M |
|  | 5 | A.3.5 | Type of Number in Called Party Number Information Element | C2 |

C1: IF B.1.5 THEN M ELSE N/A

C2: IF (B.1.1 OR B.1.2) THEN M ELSE N/A