ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 055 rev. 1

Date:	1998-12-01

Subject:	Value of the state used in STATUS message

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

X	CTR 4 Amendment 1 (Commission Decision 98/520/EC)

X	CTR 33 (Commission Decision 98/521/EC)

X	CTR 34 (Commission Decision 98/518/EC)

In consideration of the following:

-	TBR 3, TBR 3/A1, TBR 4 and TBR 4/A1 in subclauses 11.4.6.6.1 and 11.4.6.6.2 states that the terminal may respond to a message containing an unrecognized information element or a Non-mandatory information element with invalid content by sending a STATUS message indicating the call state of the receiver after taking action on the message.

-	This is also stated in subclauses 11.4.6.5.1 and 11.4.6.5.2 of TBR 33 and TBR 34.

-	TC10028 and TC10029 of TBR 3/A1, TBR 4/A1, TBR 33 and TBR 34 (as well as other TTCN test cases for this requirement) allow the state prior to receiving the message to be reported.

ITAAB advises the following:

Upon receipt of an unrecognized information element or a Non-mandatory information element with invalid content, the TE may send a STATUS message before or after responding to the message. The state to report in the optional STATUS message shall correspond to the state of the terminal as seen from the interface, e.g. if the STATUS message is sent prior to a response to a SETUP, state 6 shall be reported; and if the STATUS message is sent after one of the legal responses to a SETUP message the corresponding state (25, 9, 7 or 8) as applicable, shall be reported.