ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 060 rev. 2

Date:	1999-04-26

Subject:	Testing to be performed for Basic Access layer 1, including variations of Power Sources to be applied during testing of Electrical Characteristics

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

Annexes to this Advisory Note:

A:	List of ISDN L1 Basic Access Tests and test case selection criteria

In consideration of the following:

-	The CTR 3 A1 Commission Decision references TBR 3/A1. However, according to a decision in ACTE it is not mandatory to use the tests specified in the annex B of TBR 3/A1 to verify compliance for layer 1;

-	The set of relevant tests required for regulatory testing depends on certain capabilities of the TE. The information on implementation of these capabilities has to be provided by the manufacturer;

-	For Layer 1 for Basic Access, some tests for electrical characteristics shall be repeated with various values of the PS1 supply voltage;

-	For the measurement of Jitter Characteristics according to Clause B.2.2.1 and B.2.2.2 of TBR 3/A1, uncertainty of the measurements play a larger role than the variations of the power supply;

-	For several tests, the influence of the power supply variations is considered small, and if it has influence, the worst case results are expected with minimum power available;

-	A TE, which is not powered from PS1 may be equipped with a connection detector, that checks the connection to the S-bus by detecting the presence of the PS1 supply voltage. Such TEs will require presence of the PS1 supply voltage to perform tests requiring the TE to be active;

ITAAB advises the following:

Annex B of TBR 3/A1, December 1997, including the Abstract Test Suite for layer 1 attached in electronic form, can be used to verify compliance for Basic Access layer 1 for type approval according to the CTR 3 A1 Commission Decision.

Other test specifications may be applied, provided the test laboratory ensures its Accreditation Body that the verification of compliance is at least as for the tests specified in TBR 3/A1, i.e. the tests shall perform at least the same checks of the same requirements.

The selection of tests for Basic Access layer 1, including variations of PS1 supply voltage for the measurement of Electrical Characteristics, shall be performed as described in Annex A to this Advisory Note.

The selection shall be based on the declaration of the manufacturer on the capabilities of the TE, as described in Annex A to this Advisory Note.

A TE not powered from PS1 shall have PS1 applied at all time during testing. When no other specific voltage to be applied is specified for electrical characteristics layer 1 testing, a PS1 voltage of -32 V shall be applied. This also applies for the tests to be performed in layer 1 state F1.