ITAAB

TRAC ISDN Type Approval Advisory Board

Annex B

to

ITAAB Advisory Note Number:  066 rev. 3

Date:	1999-05-21

Subject:	List of tests and Test Case Selection Criteria for ISDN Layer 3 Basic Access and Primary Rate Access

1.	TEST CASE SELECTION CRITERIA

The set of tests required to verify compliance with the layer 3 requirements of CTR 3 Amendment 1 for Basic Access and CTR 4 Amendment 1 for Primary Rate Access are described in clause 2.

The set of tests relevant for a specific implementation depends on certain capabilities of the TE. The information on implementation of these capabilities has to be provided by the manufacturer.

Corresponding to the declaration made by the manufacturer concerning each of these capabilities, a corresponding conditioning parameter is given the value TRUE or FALSE. The conditioning parameters are used in Boolean expressions to define the conditions for relevance of each test.

The abbreviations used for the Boolean expressions and the value associated with the implemented capabilities appear from the following table:

| Abbreviation | TBR 3 TBR-RT/PIXIT reference | TBR 4 TBR-RT/PIXIT reference | Corresponding conditioning parameter |
| --- | --- | --- | --- |
| IBCC |

A.16.4  (p-t-p)

A.16.5 (p-t-mp)

A.16.3

|  | TRUE if the TE performs checking of the Bearer capability IE in an incoming SETUP PDU |
| --- | --- |
| IHLCC |

A.16.6 (p-t-mp)

| Note 1 (p-t-p) | E.8.14 (Note 1) | TRUE if the TE performs checking of the High layer compatibility IE in an incoming SETUP PDU |
| --- | --- | --- |
| BSPRE | A.18.1 | FALSE | TRUE if the TE supports the Call rearrangement procedure |
| EBS_SC | A.15.2 (Note 3) | A.15.2 | TRUE if the TE uses en-bloc sending, and includes the Sending complete IE in an outgoing SETUP message |
| EBS_NSC | A.15.3 (Note 3) | A.15.3 | TRUE if the TE uses en-bloc sending, and does not include the Sending complete IE in an outgoing SETUP message |
| OVS | A.15.4 (Note 3) | A.15.4 | TRUE if the TE uses overlap sending |
| OVR | A.16.10 | A.16.5 | TRUE if the TE supports the Overlap Receiving procedure |
| BAL | E.8.9 | E.8.9 | TRUE if the TE is capable of sending the ALERT PDU |
| U7_MAINT | E.8.1 | E.8.1 | TRUE if the TE maintains state U7 for more than 3 seconds |
| BCP | E.8.8 | E.8.8 | TRUE if the TE is capable of sending the CALL PROCEEDING PDU |
| U9_MAINT | E.8.2 | E.8.2 | TRUE if the TE maintains state U9 for more than 3 seconds |
| BDL | NOT A.8.1 (Note 2) | FALSE | TRUE: if the IUT is being tested in a point-to-multipoint data link mode. |
| BA | TRUE | FALSE | TRUE if the TE is intended for Basic Access |

Note 1:	There is no TBR-RT or PIXIT item indicating whether the IUT checks the high layer compatibility IE for a SETUP message delivered in the point-to-point data link. For testing to TBR 4 it can be assumed that the HLC is checked if a value for an incompatible HLC is supplied (PIXIT item E.8.14). For testing to TBR 3 of a TE in the point-to-point data link mode the necessary information is not available from the TBR-RT and PIXIT.

Note 2:	Where the TE supports more than one mode of operation this parameter shall be set to TRUE for testing in point-to-multipoint data link mode and FALSE for testing in point-to-point data link mode. If only one mode is supported it should be set according to the TBR-RT (See ITAAB AN 096).

Note 3:	The test suite parameters EBS_SC, EBS_NSC and OVS have been added by ITAAB AN 087.

2.	TEST CASE SELECTION

The tables in the following subclauses describe the set of relevant tests required to verify compliance with the layer 3 requirements of CTR 3 Amendment 1 for Basic Access and CTR 4 Amendment 1 for Primary Rate Access.

Column 1, Requirement from TBR 3 / TBR 4, references the requirements in TBR 3 as amended by TBR 3/A1 and TBR 4 as amended by TBR 4/A1.

Column 2, Description, provides a brief description of the test case.

Column 3, Test case identifier, provides the reference to the relevant TTCN test case in TBR 3/A1 and TBR 4/A1.

Column 4, Condition, provides the test selection criteria. The condition is described as a Boolean expression of the conditioning parameters. When the Boolean expression evaluates to TRUE, the test is relevant. When the condition is blank, the test is always relevant.

Column 5, Reference to Notes, provides reference to notes describing problems with one or more of the test descriptions in TBR 3/A1 or TBR 4/A1 and/or reference to relevant Advisory Notes.

Column 6, Annex A ETS 300 104 (ETS 300 156), is an informative reference to the old tests for the I-CTRs, provided for reference purposes with old test campaigns.

2.1	INCOMING CALL HANDLING TESTS STATE U00

Requirement from TBR 3 / TBR 4

| Description | Test case identifier | Condition | Reference to notes |
| --- | --- | --- | --- |

Annex A

ETS 300 104

| (ETS 300 156) |
| --- |
| 11.4.6.2(c) | Ensure that on receipt of a REL PDU, the IUT responds with REL_COM PDU and remains in the same state. | TC10002 |

A.2.1

| (A.3.2) |
| --- |
| 11.4.6.8(a) | Ensure that on receipt of a STATUS PDU indicating any state except the null state, the IUT responds with either a REL or REL_COM PDU with the cause #101. | TC10004 |

A.2.4.2

(A.3.2)

11.4.2.1

11.4.2.4

| 11.4.2.5.1 | Ensure that on receipt of a valid SETUP without the sending complete IE the IUT responds with either SETUP_ACK, CALL_PROC, ALERT or CONN PDU and moves to the relevant state 25, 9, 7 or 8. | TC10005 |
| --- | --- | --- |
| Note 4 |

A.1.1.1.1

(A.3.1)

11.4.2.1

| 11.4.2.5.1 | Ensure that on receipt of a valid SETUP PDU with the sending complete IE the IUT responds with either a CALL_PROC, ALERT or CONN PDU and moves to the relevant state 9, 7 or 8. | TC10006 |
| --- | --- | --- |
| Note 4 |

A.1.1.1.2

(A.3.1)

11.4.2.2

Ensure that on receipt of a valid SETUP PDU containing an incompatible Bearer Capability IE (mandatory parameter) the IUT:

-responds by sending a REL_COM PDU or ignore the SETUP PDU /PTMP

| -responds by sending a REL_COM PDU /PTP | TC10008 | IBCC | Note 4 |
| --- | --- | --- | --- |

A.1.1.2.1

(A.3.1)

11.4.2.2.1

Ensure that on receipt of a valid SETUP PDU containing an incompatible High Layer Compatibility IE (optional parameter) the IUT:

-responds by sending a REL_COM  PDU or ignore the SETUP PDU /PTMP

| -responds by sending a REL_COM PDU /PTP | TC10009 | IHLCC | Note 4 |
| --- | --- | --- | --- |

A.1.1.2.2

| (A.3.1) |
| --- |
| 11.4.6.2(a) | Ensure that the IUT responds to an inopportune PDU (DISC) with a REL PDU or REL_COM PDU. | TC10010 |
| Note 4 |

A.2.3.1

| (A.3.2) |
| --- |
| 11.4.6.2(d) | Ensure that on receipt of a repeated valid SETUP with the same call reference as the initial SETUP, the IUT ignores the second SETUP and remains in the same state. | TC10011 |
| Note 4 |

A.1.2

| (A.3.1) |
| --- |
| 11.4.6.5.1 | Ensure that on receipt of a SETUP without a mandatory IE the IUT responds with a REL_COM PDU and remains in the same state. | TC10015 |
| Note 4 |

A.1.3.3

| (A.3.1) |
| --- |
| 11.4.6.4 | Ensure that on receipt of a PDU with invalid duplicated IE, the IUT ignores the invalid duplication and processes the remaining contents of the PDU as valid. | TC10024 |
| Note 4 | - |
| 11.4.6.6.1 | Ensure that the IUT responds to the receipt of a SETUP PDU with unrecognised optional IE coded "comprehension required" by sending a REL_COM PDU and remains in the same state. | TC10027 |
| Note 4 |

A.1.3.4

(A.3.1)

Requirement from TBR 3 / TBR 4

| Description | Test case identifier | Condition | Reference to notes |
| --- | --- | --- | --- |

Annex A

ETS 300 104

| (ETS 300 156) |
| --- |
| 11.4.6.6.1 | Ensure that the IUT on receipt of a compa-tible SETUP PDU with all the mandatory information correctly coded and an unre-cognised optional IE with comprehension not required responds with a STATUS PDU (optional) followed by either a SETUP_ACK, CALL_PROC, ALERT or CONN PDU and moves to the relevant state 25, 9, 7 or 8. | TC10028 |
| Note 4 |

A.1.3.5

| (A.3.1) |
| --- |
| 11.4.6.6.2 | Ensure that the IUT on receipt of a SETUP PDU with non mandatory IE content error the IUT processes the PDU and its remaining contents as valid and optionally sense a STATUS PDU with cause value 100. | TC10029 |
| Note 4 |

A.1.3.6

| (A.3.1) |
| --- |
| 11.4.4.4 | Ensure that on sending of a RESUME PDU the IUT enters the Resume Request state U17. | TC20001 | BSPRE AND BA |
| A.2.5 |
| 11.4.1.1 | Ensure that the IUT transmits a valid SETUP and enters the Call Initiated state U1. | TC20002 |
| Note 5 |

A.9.1

(A.3.9)

2.2	CALL INITIATED STATE TESTS, STATE 1

Requirement from TBR 3 / TBR 4

| Description | Test case identifier | Condition | Reference to notes |
| --- | --- | --- | --- |

Annex A

ETS 300 104

| (ETS 300 156) |
| --- |
| 11.4.1.3.1 | Ensure that on receipt of a CALL_PROC PDU the IUT enters the state U3. | TC10101 |
| Note 6 |

A.10.5

| (A.3.10) |
| --- |
| 11.4.6.3 | Ensure that on receipt of a REL_COM PDU the IUT does not respond but returns to the state U0. | TC10102 |
| Note 6 |

A.10.2

| (A.3.10) |
| --- |
| 11.4.6.3 | Ensure that on receipt of a REL PDU the IUT responds with a REL_COM PDU and enters the state U0. | TC10103 |
| Note 6 |

A.10.1

| (A.3.10) |
| --- |
| 11.4.1.2 | Ensure that on receipt of a SETUP_ACK PDU the IUT enters the Overlap Sending state. | TC10104 | OVS OR EBS_NSC | Note 6 |

A.10.6

| (A.3.10) |
| --- |
| 11.4.6.8(c) | Ensure that on receipt of a STATUS PDU specifying the state U0, the IUT enters the state U0. | TC10105 |
| Note 6 |

A.10.4.1

| (A.3.10) |
| --- |
| 11.4.6.3 | Ensure that the IUT responds to an inopportune PDU with a STATUS PDU with cause value 98 or 101, or ST_ENQ PDU and remains in the same state. | TC10107 |
| Note 6 |

A.10.3.1

| (A.3.10) |
| --- |
| 11.4.6.3 | Ensure that the IUT responds to a syntactically invalid message type with a STATUS PDU with cause value 98 or 101, or ST_ENQ PDU and remains in the same state. | TC10120 |
| Note 6 |

A.10.3.2

| (A.3.10) |
| --- |
| 11.4.6.2(c) | Ensure that on receipt of a REL_COM PDU the IUT does not respond and remains in the same state. | TC10125 |
| Note 6 | - |

2.3	OVERLAP SENDING STATE TESTS, STATE 2

Requirement from TBR 3 / TBR 4

| Description | Test case identifier | Condition | Reference to notes |
| --- | --- | --- | --- |

Annex A

ETS 300 104

| (ETS 300 156) |
| --- |
| 11.4.1.4 | Ensure that on receipt of an ALERT PDU the IUT enters the State U4. | TC10201 | OVS OR EBS_NSC | Note 6 |

A.11.9

| (A.3.11) |
| --- |
| 11.4.1.5 | Ensure that on receipt of a CONN PDU the IUT enters the state U10. | TC10202 | OVS OR EBS_NSC | Note 6 |

A.11.10

| (A.3.11) |
| --- |
| 11.4.1.3.2 | Ensure that on receipt of a CALL_PROC PDU the IUT enters the state U3. | TC10203 | OVS OR EBS_NSC | Note 6 |

A.11.8

| (A.3.11) |
| --- |
| 11.4.3.4.2 | Ensure that the IUT responds to a DISC PDU with a RELEASE PDU and enters the Release Request state U19. | TC10204 | OVS OR EBS_NSC | Note 6 |

A.11.1

| (A.3.11) |
| --- |
| 11.4.3.3 | Ensure that the IUT transmits a DISC PDU and enters the Disconnect Request state. | TC20203 | OVS OR EBS_NSC | Note 6 |

A.11.12

| (A.3.11) |
| --- |
| 11.4.1.2 | Ensure that the IUT transmits an INFO PDU and remains in the same state. | TC20204 | OVS | Note 6 |

A.11.11

(A.3.11)

2.4	OUTGOING CALL PROCEEDING STATE TESTS, STATE 3

Requirement from TBR 3 / TBR 4

| Description | Test case identifier | Condition | Reference to notes |
| --- | --- | --- | --- |

Annex A

ETS 300 104

| (ETS 300 156) |
| --- |
| 11.4.1.4 | Ensure that on receipt of an ALERT PDU the IUT enters the state U4. | TC10301 | NOT (OVS OR EBS_NSC) | Note 6 |

A.12.8

| (A.3.12) |
| --- |
| 11.4.1.5 | Ensure that on receipt of a CONN PDU the IUT enters the state U10. | TC10302 |
| Note 6 |

A.12.9

| (A.3.12) |
| --- |
| 11.4.3.4.2 | Ensure that the IUT responds to a DISC PDU with a REL PDU and enters the Release Request state U19. | TC10303 |
| Note 6 |

A.12.1

| (A.3.12) |
| --- |
| 11.4.3.3 | Ensure that the IUT transmits a DISC PDU and enters the Disconnect Request state. | TC20301 |
| Note 6 |

A.12.10

(A.3.12)

2.5	CALL DELIVERED STATE TESTS, STATE 4

Requirement from TBR 3 / TBR 4

| Description | Test case identifier | Condition | Reference to notes |
| --- | --- | --- | --- |

Annex A

ETS 300 104

| (ETS 300 156) |
| --- |
| 11.4.1.5 | Ensure that on receipt of a CONN PDU the IUT enters the state U10. | TC10401 |
| Note 6 |

A.13.8

| (A.3.13) |
| --- |
| 11.4.3.4.2 | Ensure that the IUT responds to a DISC PDU with a REL PDU and enters the Release Request state U19. | TC10402 |
| Note 6 |

A.13.1

| (A.3.13) |
| --- |
| 11.4.3.3 | Ensure that the IUT transmits a DISC PDU and enters the state U11. | TC20401 |
| Note 6 |

A.13.9

(A.3.13)

2.6	CALL RECEIVED STATE TESTS, STATE 7

Requirement from TBR 3 / TBR 4

| Description | Test case identifier | Condition | Reference to notes |
| --- | --- | --- | --- |

Annex A

ETS 300 104

| (ETS 300 156) |
| --- |
| 11.4.3.4.2 | Ensure that the IUT responds to a DISC PDU with a REL PDU and enters the Release Request state U19. | TC10701 | BAL AND U7_MAINT |

A.6.1

(A.3.6)

2.7	CONNECT REQUEST STATE TESTS, STATE 8

Requirement from TBR 3 / TBR 4

| Description | Test case identifier | Condition | Reference to notes |
| --- | --- | --- | --- |

Annex A

ETS 300 104

| (ETS 300 156) |
| --- |
| 11.4.2.7 | Ensure that the IUT will enter the state U10 on receipt of a CONN_ACK PDU. | TC10801 |

A.7.7

| (A.3.7) |
| --- |
| 11.4.3.4.2 | Ensure that the IUT responds to a DISC PDU with a REL PDU and enters the Release Request state U19. | TC10802 |

A.7.1

(A.3.7)

11.4.2.8

| 11.4.6.3 | Ensure that on receipt of a REL PDU the IUT responds with a REL_COM PDU and enters the state U0. | TC10805 | BA AND BDL |
| --- | --- | --- | --- |
| A.7.2 |

2.8	INCOMING CALL PROCEEDING STATE TESTS, STATE 9

Requirement from TBR 3 / TBR 4

| Description | Test case identifier | Condition | Reference to notes |
| --- | --- | --- | --- |

Annex A

ETS 300 104

| (ETS 300 156) |
| --- |
| 11.4.3.4.2 | Ensure that the IUT responds to a DISC PDU with a REL PDU and enters the Release Request state U19. | TC10901 | BCP AND U9_MAINT |

A.5.1

(A.3.5)

2.9	ACTIVE STATE TESTS, STATE 10

Requirement from TBR 3 / TBR 4

| Description | Test case identifier | Condition | Reference to notes |
| --- | --- | --- | --- |

Annex A

ETS 300 104

| (ETS 300 156) |
| --- |
| 11.4.7 | Ensure that on receipt of a NOTIFY PDU the IUT does not respond and remains in the same state. | TC11003 |

A.8.7

| (A.3.8) |
| --- |
| 11.4.6.3 | Ensure that on receipt of a REL_COM PDU the IUT does not respond but returns to the null state. | TC11004 |

A.8.3

| (A.3.8) |
| --- |
| 11.4.6.3 | Ensure that on receipt of a REL PDU the IUT responds with a REL_COM PDU and enters the state U0. | TC11005 |

A.8.2

| (A.3.8) |
| --- |
| 11.4.6.8(c) | Ensure that on receipt of a STATUS PDU specifying the state U0, the IUT enters the state U0. | TC11007 |

A.8.6.1

| (A.3.8) |
| --- |
| 11.4.6.3 | Ensure that the IUT responds to an inopportune CONN PDU with a STATUS PDU with the cause 98 or 100 or with a ST_ENQ and remains in the same state. | TC11008 |

A.8.4.1

| (A.3.8) |
| --- |
| 11.4.6.3 | Ensure that the IUT responds to a syntactically invalid message type with a STATUS PDU with the cause 98 or 97 and that no change of state occurs. | TC11021 |

A.8.4.2.1

| (A.3.8) |
| --- |
| 11.5 | Ensure timer T308 is within the range 3 s to 15 s. | TC21001 |

A.19.4

| (A.3.19) |
| --- |
| 11.4.3.3 | Ensure that the IUT transmits a DISC PDU and enters the Disconnect Request state U11. | TC21003 |

A.8.8

| (A.3.8) |
| --- |
| 11.4.4.1 | Ensure that on transmission of a SUSP PDU the IUT enters the Suspend Request state U15. | TC21005 | BSPRE AND BA |
| A.8.9 |
| 11.5 | Ensure timer T305 is within the range 15 s to 45 s. | TC21006 |

A.19.3

(A.3.19)

2.10	DISCONNECT REQUEST STATE TESTS, STATE 11

Requirement from TBR 3 / TBR 4

| Description | Test case identifier | Condition | Reference to notes |
| --- | --- | --- | --- |

Annex A

ETS 300 104

| (ETS 300 156) |
| --- |
| 11.4.3.5 | Ensure that the IUT responds to a DISC PDU with a REL PDU and enters the Release Request state U19. | TC11101 |
| Note 6 |

A.14.1

| (A.3.14) |
| --- |
| 11.4.7 | Ensure that on receipt of a NOTIFY PDU the IUT does not respond or returns a STATUS PDU and remains in the same state. | TC11103 |
| Note 6 |

A.14.7

| (A.3.14) |
| --- |
| 11.4.3.3 | Ensure that on receipt of a REL PDU the IUT responds with a REL_COM PDU and enters the state U0. | TC11105 |
| Note 6 |

A.14.2

(A.3.14)

11.4.6.3

| 11.4.6.7 | Ensure that the IUT responds to an inopportune PDU with a STATUS PDU with the cause 98 or 101 or with a ST_ENQ PDU and remains in the same state . | TC11107 |
| --- | --- | --- |
| Note 6 |

A.14.4.1

| (A.3.14) |
| --- |
| 11.4.6.6.1 | Ensure that on receipt of a REL PDU with unrecognised IE (coded comprehension not required) THE IUT sends a REL_COM PDU and enters the state U0. | TC11118 |
| Note 6 | - |

2.11	SUSPEND REQUEST STATE TESTS, STATE 15

Requirement from TBR 3 / TBR 4

| Description | Test case identifier | Condition | Reference to notes |
| --- | --- | --- | --- |

Annex A

ETS 300 104

| (ETS 300 156) |
| --- |
| 11.4.3.4.2 | Ensure that the IUT responds to a DISC PDU with a REL PDU and enters the Release Request state U19. | TC11501 | BSPRE AND BA |
| A.17.1 |
| 11.4.7 | Ensure that on receipt of a NOTIFY PDU the IUT does not respond or returns a STATUS PDU and remains in the same state. | TC11503 | BSPRE AND BA |
| A.17.7 |
| 11.4.4.2 | Ensure that on receipt of a SUSP_ACK the IUT enters to the state U0. | TC11504 | BSPRE AND BA |
| A.17.9 |
| 11.4.4.3 | Ensure that on receipt of a SUSP_REJ PDU the IUT returns to the state U10. | TC11508 | BSPRE AND BA |
| A.17.8 |

2.12	RESUME REQUEST STATE TESTS, STATE 17

Requirement from TBR 3 / TBR 4

| Description | Test case identifier | Condition | Reference to notes |
| --- | --- | --- | --- |

Annex A

ETS 300 104

| (ETS 300 156) |
| --- |
| 11.4.3.4.2 | Ensure that the IUT responds to a DISC PDU with a REL PDU and enters the Release Request state U19. | TC11701 | BSPRE AND BA |
| A.18.1 |
| 11.4.4.4 | Ensure that on receipt of a RES_ACK PDU IUT returns to the state U10. | TC11703 | BSPRE AND BA |
| A.18.8 |
| 11.4.4.5 | Ensure that on receipt of a RES_REJ PDU the IUT returns to the state U0. | TC11706 | BSPRE AND BA |
| A.18.7 |

2.13	RELEASE REQUEST STATE TESTS, STATE 19

Requirement from TBR 3 / TBR 4

| Description | Test case identifier | Condition | Reference to notes |
| --- | --- | --- | --- |

Annex A

ETS 300 104

(ETS 300 156)

11.4.3.4.3

|  | Ensure that on receipt of a REL_COM PDU the IUT does not respond but returns to the state U0. | TC11903 |
| --- | --- | --- |

A.16.2

(A.3.16)

11.4.3.5

|  | Ensure that on receipt of a REL PDU the IUT does not respond and enters the state U0. This is a test of RELEASE collision handling. | TC11904 |
| --- | --- | --- |

A.16.1

| (A.3.16) |
| --- |
| 11.4.6.8(c) | Ensure that on receipt of a STATUS PDU specifying the state U0, the IUT enters the state U0. | TC11906 |

A.16.5.1

| (A.3.16) |
| --- |
| 11.4.6.3 | Ensure that the IUT responds to an inopportune PDU with a STATUS PDU with the cause 98 or 101 or with a ST_ENQ and remains in the same state. | TC11908 |

A.16.3.1

| (A.3.16) |
| --- |
| 11.4.6.3 | Ensure that the IUT responds to a syntactically invalid message type with a STATUS PDU with the cause 98 or 97 or with a ST_ENQ and remains in the same state. | TC11909 |

A.16.3.2

(A.3.16)

2.14	OVERLAP RECEIVING STATE TESTS, STATE 25

Requirement from TBR 3 / TBR 4

| Description | Test case identifier | Condition | Reference to notes |
| --- | --- | --- | --- |

Annex A

ETS 300 104

| (ETS 300 156) |
| --- |
| 11.4.3.4.2 | Ensure that the IUT responds to a DISC PDU with a REL PDU and enters the Release Request state U19. | TC12501 | OVR |

A.4.1

(A.3.4)

11.4.2.4

| 11.4.2.5.1 | Ensure that on receipt of an INFO PDU with sufficient called number information the IUT responds with either a CALL_PROC, ALERT or CONN PDU and moves to the relevant state U9, U7 or U8. | TC12503 | OVR |
| --- | --- | --- | --- |

A.4.5.2

(A.3.4)

2.15	RESTART NULL STATE TESTS, REST 0

Requirement from TBR 3 / TBR 4

| Description | Test case identifier | Condition | Reference to notes |
| --- | --- | --- | --- |

Annex A

ETS 300 104

| (ETS 300 156) |
| --- |
| 11.4.8 | Ensures that on receipt of a RESTART message the specified channel is returned to the Idle condition, the Call Reference is returned to the Null state and a RESTART_ACK is sent. | TC19003 | NOT BA OR ((NOT BDL) AND BA) | Note 7 | A.1.3.7 (A.3.20.3) |

Note 4:	If the TE supports both a point-to-point data link mode and a point-to-multipoint data link mode test cases TC10005 to TC10029 shall be repeated in each mode (See ITAAB AN 096).

Note 5:	If the values of compatibility information elements (i.e. BCAP, HLC and LLC) differ for incoming and outgoing calls different values of the corresponding test suite parameters may need to be used for TC20002 (see ITAAB AN 085).

Note 6:	For some TE which support more than one dialling mode and/or use en-bloc sending without sending complete the preambles in TBR 3/A1 and TBR 4/A1 for states U01, U02, U03, U04 and U11 may be inappropriate. For alternative preambles and further information see ITAAB AN 087.

Note 7:	The TTCN description for TC19003 in TBR3/A1 and TBR3/A1 incorrectly checks the preferred/exclusive bit in the Channel identification IE in the RESTART ACKNOWLEDGE message. For a correction concerning this see ITAAB AN 080.