ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 067 rev. 1

Date:	1999-04-28

Subject:	Testing to be performed for Primary Rate Access layer 1

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 4 Amendment 1 (Commission Decision 98/520/EC)

Annexes to this Advisory Note:

A:	List of ISDN L1 Primary Rate Access Tests and Test Case Selection Criteria

In consideration of the following:

-	The set of relevant tests required for regulatory testing depends on certain capabilities of the TE. The information on implementation of these capabilities has to be provided by the manufacturer;

-	The CTR 4 Amendment 1, Commission decision on a common technical regulation for the pan-European Integrated Services Digital Network (ISDN) Primary Rate Access, does not provide information of this kind;

-	The CTR 4 Commission decision does not make the test annexes of TBR 4 including Amendment 1 mandatory. The test method used to verify compliance is not restricted to the method specified in the annexes.

-	However, when another test method applies, the environmental conditions described in that test specification applies. Due to the larger temperature range specified in the alternative test specifications, the comparability of results is reduced.

ITAAB advises the following:

For type approval according to the CTR 4 Amendment 1 Commission Decision, the selection of tests for Primary Rate Access layer 1 shall be performed as described in Annex A to this Advisory Note.

The selection shall be based on the declaration of the manufacturer on the capabilities of the TE, as described in Annex A to this Advisory Note.

The test method used to verify the requirement shall be taken from TBR 4 as modified by TBR 4/A1 or ETS 300 011. The appropriate test methods as shown in the appendix.

To ensure repeatability and reproducibility of results, the verification of compliance with the requirements shall be performed within the environmental limits defined in subclause B.1.5 in Annex B of TBR 4 as modified by TBR 4/A1.