ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 068 rev. 1

Date:	1998-09-07

Subject:	CRC processing and generation of CRC error reports:

Monitoring contiguous E-bits

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 4 Amendment 1 (Commission Decision 98/518/EC)

X	CTR 34 (Commission Decision 98/520/EC)

In consideration of the following:

-	In TBR 4 subclause 9.5.5.5 the requirement for CRC alignment is specified. One method of testing is given in Annex B subclause B.4.2. and involves monitoring contiguous E-bits;

-	The two E-bits are not allocated to the CRC check for specific sub-multiframes;

-	The term "contiguous E-bits" can be interpreted in various ways, either as

-	the E-bits in the same frame number in consecutive multiframes, or as

-	the consecutive E-bits in a sequence consisting of the E-bit pairs from the sequence of multiframes, where the order of the two E-bits in the pair is unspecified;

-	Depending on the interpretation made for the implementation, the order in which the contiguous E-bits appear may be different. The order may also depend on whether the first change among sub-multiframes with and without CRC error appears in a sub-multiframe 1 or in a sub-multiframe 2;

-	TBR 34 references the layer 1 tests of TBR 4 for equipment using on-demand access.

ITAAB advises the following:

When performing test B.4.2 of TBR 4 to verify compliance with TBR 4, as amended by TBR 4/A1, or TBR 34, the test result can be considered a PASS, when the order of the E-bits reporting successive sub-multiframes with CRC error are separated by a maximum of two other E-bits.

For the requirement to monitor "Two contiguous E-bits set to zero", this allows the following order of E-bits:

. . . 1 1 1 0 0 1 1 1 . . .   or   . . . 1 1 0 1 0 1 1 1 . . .   or   . . . 1 1 0 1 1 0 1 1 . . .

For the requirement to monitor "No E-bit set to zero" followed by "914 contiguous E-bits set to zero", this allows the following order of E-bits:

. . . 1 1 1 1 0 0 0 0 . . .   or   . . . 1 1 1 0 1 0 0 0 . . .   or   . . . 1 1 0 1 1 0 0 0 . . .

For the requirement to monitor "914 contiguous E-bits set to zero" followed by "No E-bit set to zero", this allows the following order of E-bits:

. . . 0 0 0 0 1 1 1 1 . . .   or   . . . 0 0 0 1 0 1 1 1 . . .   or   . . . 0 0 1 0 0 1 1 1 . . .