ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 069 rev. 1

Date:	1998-09-07

Subject:	Basic Access Layer 1 tests with problems for Unstable state S4 at Layer 2

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

X	CTR 33 (Commission Decision 98/521/EC)

In consideration of the following:

-	Some types for Basic Access TE's, e.g. routers, will send an SABME at layer 2, as soon as layer 1 has been activated, if a TEI value already is available. These TEs are unstable in layer 2 state S4.

-	Such TE's will get a FAIL verdict when certain of the layer 1 tests are performed, although nothing in the base standards prevents such behaviour. There is no definition of a minimum time for a TE to be stable in state S4.

ITAAB advises the following:

Until TTCN test descriptions have been defined, allowing a TE (with a TEI value available) to send SABME when state F7 at layer 1 is entered, the test operator shall perform a manual verdict assignment based on the information available in the test log for the tests having this problem, as described below:

For test F8/CPF8PHDI_I0T3

For a TE automatically sending SABME when in layer 1 state F7 and layer 2 state S4, a PASS verdict shall also be assigned if INFO3 frames with D-channel information, containing an SABME frame, is sent, when state F7 is entered in subtree SendI4_I0T3.

For tests F6/CPF6PHARa and F8/CPF8PHARa

If TAPPLI1 is implemented, the activation request is deleted after expiry of TAPPLI1 and the call is not established (no SETUP is sent). The testcases expect no D-channel information - i.e. no SABME and no SETUP.
For a TE automatically sending SABME when in layer 1 state F7 and layer 2 state S4, a PASS verdict shall also be assigned if INFO3 frames with D-channel information, containing an SABME frame, is sent, when state F7 is entered in subtree D_WATCHa or D_WATCH_F8a, respectively.

If TAPPLI1 is not implemented, the activation request is not deleted and the call is established (SABME and SETUP will be sent). The testcases expect SABME and SETUP.
There will be no problem in this case.