ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 070 rev. 1

Date:	1998-09-07

Subject:	CRC processing Test Procedure Change

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 4 Amendment 1 (Commission Decision 98/518/EC)

X	CTR 34 (Commission Decision 98/520/EC)

This note specifically contains amendments to:

TBR 4; November 1995; ISDN; Attachment requirements for terminal equipment to connect to an ISDN using primary rate access

In consideration of the following:

- 	One option for testing requirement 9.5.5.4 of TBR 4 is the test of annex B clause B.4.2 of TBR 4;

-	Test B.4.2 of TBR 4 includes a test that 915 CRC errors out of 1000 cause RAI;

-	The test allows for apparatus which uses window sampling by having 2 blocks of 915 CRC errors separated by 85 without errors;

-	The test allows for more than one alarm because 2 sets of 915 errors are received;

-	The test includes a check that RAI is removed after the error condition ends;

-	Delays between the error condition and RAI is covered by Note 1 to the test method;

-	The test does not allow for the second RAI when checking RAI has cleared;

-	TBR 34 references the layer 1 requirements and tests of TBR 4 for equipment using on-demand access.

ITAAB advises the following:

When performing test B.4.2 of TBR 4 to verify compliance with TBR 4, as amended by TBR 4/A1, or TBR 34, the test that RAI has ceased should not be implemented until 85 submultiframes after the last errored submultiframe.

Note: In practice this is unlikely to affect the test sequence used by testers, it only affects the interpretation of results.

The following changes shall be performed in Annex B of TBR 4:

Table B.1 shall be modified as follows:

Table B.1: Test procedure

| Stimulus | Monitor (see NOTES 1 and 2) |
| --- | --- |
| SMF A | No E bit set to zero |
| # Repeat more than 1 second |
|  | SMF B | One E bit set to zero |
| SMF A | No E bit set to zero |
| # |
|  | SMF B, SMF B | Two contiguous E bits set to zero |
| SMF A | No E bit set to zero |
| # Repeat more than 1 second |
|  | 914 X SMF B |

914 contiguous E bits set to zero

| (note 4) |
| --- |
| 86 X SMF A | 86 contiguous E bits set to ONE |
| 914 X SMF B |

914 contiguous E bits set to zero

| (note 4) |
| --- |
| SMF A | No E bit set to zero |
| # Repeat more than 1 second |
|  | 915 X SMF B |
|  | 85 X SMF A | Temporarily RAI (note 3) |
| 915 X SMF B |
|  | 85 X SMF A |
|  | SMF A | NOF, no E bit set to zero |
| # |
|  | /FAS,BIT 2 = 1,/FAS,BIT 2 = 1, | RAI, no E bit set to zero |
| /FAS,BIT 2 = 1 |
|  | # | RAI, no E bit set to zero |

NOTE 1:	The change in the setting of RAI shall occur within 30 ms of the of the stimulus being applied. The variation in the delay between stimulus and response shall be no greater than 6 ms.

NOTE 2:	Where no response is specified opposite a stimulus, the last described response shall continue to be sent.

NOTE 3:	The vertical bar indicates that the given monitor result shall appear at least once during application of the stimulus.

NOTE 4: In a free-running implementation, because the output bit rate does not match the input bit rate, the number of E-bits set to zero may not exactly match the number of errored sub-multiframes received. In such cases, a discrepancy of one or two in the number of E-bits set to zero shall not be considered to be a failure.