ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number:  071 rev. 1

Date:	1998-09-03

Subject:	Requirements to EURO-ISDN basic access terminal equipment capable of handling only incoming or only outgoing calls.

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

For the purposes of the above described applicability, this note specifically contains supplements to:

TBR 3, Amendment A1, December 1997: Attachment requirements for terminal equipment to connect to an ISDN using ISDN basic access.

TBR 3, November 1995: Attachment requirements for terminal equipment to connect to an ISDN using ISDN basic access.

Annexes to this Advisory Note:

A:	TBR-RT for EURO-ISDN basic access terminal equipment capable of handling only incoming or only outgoing calls

In consideration of the following:

-	TBR 3, as amended by TBR 3/A1, is only applicable to terminal equipment capable of handling both incoming and outgoing calls (at layer 3).

-	TRAC has asked ITAAB to develop an Advisory Notes showing the set of requirements applicable for oneway TEs.

ITAAB advises the following:

For type approval of terminal equipment capable of handling only incoming or only outgoing calls (at layer 3) according to CTR 3 Amendment 1, the TBR-RT requirements and conditions tables contained in Annex A of this Advisory Note shall be applied instead of the corresponding ones of TBR 3/A1.

The methods of verifying compliance with the requirements are not specified in this Advisory Note.

The TBR-RT in Annex A is based on the TBR-RT of Amendment A1 to TBR 3 and includes the requirements tables and conditions tables. The introductory text and clause A.1 of TBR 3 are not changed, and therefore not included in Annex A to this Advisory Note.

The differences to TBR 3/A1 are indicated with revision marks.

The error in the TBR-RT corrected by Advisory Note 086 rev. 1 is also included and indicated with revision marks.