ITAAB

TRAC ISDN Type Approval Advisory Board

Annex A (Normative)

to

ITAAB Advisory Note Number: 071 rev. 1

Date:	1998-09-03

Subject:	TBR-RT for EURO-ISDN basic access terminal equipment capable of handling only incoming or only outgoing calls.

TBR Requirements Table (TBR-RT)

A.2	General type, Layer 1 and overvoltage requirements TBR-RT

Table A.1: General type, Layer 1 and overvoltage conditions table

| Reference | Condition | Status | Support (Y/N) | Comment |
| --- | --- | --- | --- | --- |
| 1 | Is the TE mains powered? | o |
| Affects requirements in clause 8. |
| 2 | Is the TE PS1 powered? | o |
| Affects requirements in subclauses 9.4 and 9.5. |
| 3 | Is the TE intended to operate as a designated TE? | c1 |
| Affects requirements in subclause 9.5. |
| 4 | Does the TE have a connection to earth? | o |
| Affects requirements in subclause 9.5. |
| 5 | Is the TE intended for use only in a physical point-to-point configuration? | o |
| Affects requirements in subclauses 9.2 and 9.4. |
| 6 | Is the TE capable of transmitting INFO 3 within 5 ms of receipt of INFO 2 or INFO 4 in state F4? |

o

| Note |
| --- |
| Affects requirements in subclause 9.4. |
| 7 | Is the TE able to operate with ISDN incoming calls? | o1 |
| Affects requirements in clause 9, 10 and 11. |
| 8 | Is the TE able to operate with ISDN outgoing calls? | o1 |
| Affects requirements in clause 9, 10 and 11. |

c1 = o if A.1.2 else n/a.

o1 = Only one option shall be chosen

Note: TEs which do not need the capability to initiate activation of a deactivated interface (Incoming only TEs) need not have the capability to send INFO 1 and thereby need not enter state F4 and F5.

Table A.2: Overvoltage requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 8.1 | Impulse transfer from mains, common mode. | c1 |
|  | 2 | 8.2 | Impulse transfer from mains, transverse mode. | c1 |
|  | 3 | 8.3 | Conversion of common mode to transverse mode. | m |
|  | c1 = m if A.1.1 else n/a. |

Table A.3: Layer 1 physical characteristics requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 9.1.1 | Case A | o1 |
|  | 2 | 9.1.2 | Case B | o1 |
|  | 3 | 9.1.3 | Case C | o1 |
|  | o1 = One or more options shall be chosen. |

Table A.4: Layer 1 electrical characteristics requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 9.2.1 | Bit rate |

c2m

| Note |
| --- |
|  | 2 | 9.2.2.2 | Timing extraction jitter, configuration 1) | m |
|  | 3 | 9.2.2.2 | Timing extraction jitter, configuration 2) | c1 |
|  | 4 | 9.2.2.2 | Timing extraction jitter, configuration 3a) | c1 |
|  | 5 | 9.2.2.2 | Timing extraction jitter, configuration 3b) | c1 |
|  | 6 | 9.2.2.2 | Timing extraction jitter, configuration 4) | m |
|  | 7 | 9.2.2.3 | Total phase deviation input to output, configuration 1) | m |
|  | 8 | 9.2.2.3 | Total phase deviation input to output, configuration 2) | c1 |
|  | 9 | 9.2.2.3 | Total phase deviation input to output, configuration 3a) | c1 |
|  | 10 | 9.2.2.3 | Total phase deviation input to output, configuration 3b) | c1 |
|  | 11 | 9.2.2.3 | Total phase deviation input to output, configuration 4) | m |
|  | 12 | 9.2.3 a) | TE transmitter output impedance, requirement (a) | m |
|  | 13a | 9.2.3 b) | TE transmitter output impedance, requirement (b) at 50 ohm load | m |
|  | 13b | 9.2.3 b) | TE transmitter output impedance, requirement (b) at 400 ohm load | c1 |
|  | 14 | 9.2.4 | Pulse shape and amplitude (binary ZERO) | m |
|  | 15 | 9.2.5.1 | Pulse amplitude when transmitting a high density pattern | m |
|  | 16 | 9.2.5.2 | Pulse unbalance of an isolated couple of pulses | m |
|  | 17 | 9.2.6.1 | Voltage on other test loads: 400 ohm load | c1 |
|  | 18 | 9.2.6.2 | Voltage on other test loads: 5,6 ohm load | c1 |
|  | 19 | 9.2.7 | Longitudinal Conversion Loss (LCL) of the transmitter output | m |
|  | 20 | 9.2.8 | TE receiver input impedance | m |
|  | 21 | 9.2.9 (1) | Receiver sensitivity - Noise and distortion immunity, configuration (1) | m |
|  | 22 | 9.2.9 (2) | Receiver sensitivity - Noise and distortion immunity, configuration (2) | c1 |
|  | 23 | 9.2.9 (3a) | Receiver sensitivity - Noise and distortion immunity, configuration (3a) | c1 |
|  | 24 | 9.2.9 (3b) | Receiver sensitivity - Noise and distortion immunity, configuration (3b) | c1 |
|  | 25 | 9.2.9 (4) | Receiver sensitivity - Noise and distortion immunity, configuration (4) | m |
|  | 26 | 9.2.10 | Longitudinal Conversion Loss (LCL) of the receiver input | m |

c1 = n/a if A.1.5 else m.

c2=m if A.1.8 else o

Note: TEs which do not need the capability to initiate activation of a deactivated interface (Incoming only TEs) need not have the capability to send INFO 1 and thereby need not enter state F4 and F5.

Table A.5: Layer 1 functional characteristics requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 9.3.1.1 | TE to NT | m |
|  | 2 | 9.3.1.3 | Relative bit positions | m |
|  | 3 | 9.3.2 | Line code | m |

Table A.6: Layer 1 interface procedure requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 9.4.1.1 | Interframe (Layer 2) time fill | m |
|  | 2 | 9.4.1.2 | Multipoint contention resolution mechanism | c1 |
|  | 3 | 9.4.1.3 | Collision detection | c1 |
|  | 4 | 9.4.2.3.1 | Activation/deactivation procedure for TEs powered from PS1, not including tests in state F5 (table 9.7). |

c2

| Note |
| --- |
|  | 5 | 9.4.2.3.1 | Activation/deactivation procedure for TEs powered from PS1, state F5 tests (table 9.7). |

c3

| Note |
| --- |
|  | 6 | 9.4.2.3.1 | Activation/deactivation procedure for TEs locally powered, not including tests in state F5 (table 9.8). |

c4

| Note |
| --- |
|  | 7 | 9.4.2.3.1 | Activation/deactivation procedure for TEs locally powered, state F5 tests (table 9.8). |

c5

| Note |
| --- |
|  | 8 | 9.4.2.3.2 | Timer values |

m

| Note |
| --- |
|  | 9 | 9.4.2.4 | TE activation times, not including tests in state F5. | m |
|  | 10 | 9.4.2.4 | TE activation times, state F5 tests. |

c6

| Note |
| --- |
|  | 11 | 9.4.2.5 | Deactivation times | m |
|  | 12 | 9.4.3 | Frame alignment procedures | m |
|  | 13 | 9.4.4 | Multiframing | m |
|  | 14 | 9.4.5 | Idle Channel Code on the B-channels | c1 |

c1 = n/a if A.1.5 else m.

c2 = m if A.1.2 else n/a.

c3 = m if A.1.2 and not A.1.6 else n/a.

c4 = m if not A.1.2 else n/a.

c5 = m if A.1.2 and not A.1.6 else n/a.

c6 = m if not A.1.6 else n/a.

Note: TEs which do not need the capability to initiate activation of a deactivated interface (Incoming only TEs) need not have the capability to send INFO 1 and thereby need not enter state F4 and F5.

Table A.7: Layer 1 power feeding requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 9.5.2 | Current transient | c1 |
|  | 2 | 9.5.3.1 | Normal power conditions, PS1 powered terminal | c1 |
|  | 3 | 9.5.3.1 | Normal power conditions, locally powered terminal | c2 |
|  | 4 | 9.5.3.2.1 | Power available to the TE "designated" for restricted power operation | c3 |
|  | 5 | 9.5.3.2.2 | Power available to locally powered and "non-designated" TEs | c4 |
|  | 6 | 9.5.4 | Galvanic isolation | c5 |
|  | 7 | 9.5.5.1.1a | Current/time limitations for remotely powered TEs in normal mode, option a) | c6 |
|  | 8 | 9.5.5.1.1b | Current/time limitations for remotely powered TEs in normal mode, option b) | c6 |
|  | 9 | 9.5.5.1.2a | Current/time limitations for designated TEs in restricted mode, option a) | c7 |
|  | 10 | 9.5.5.1.2b | Current/time limitations for designated TEs in restricted mode, option b) | c7 |
|  | 11 | 9.5.5.1.3 | Current/time limitations for non-designated and locally powered TEs in restricted mode. | c8 |
|  | 12 | 9.5.5.2.1 | Minimum TE start up current, restricted power mode | c3 |
|  | 13 | 9.5.5.2.1 | Minimum TE start up current, normal power mode | c1 |
|  | 14 | 9.5.5.2.2 | Protection against short term interruptions, restricted power mode | c3 |
|  | 15 | 9.5.5.2.2 | Protection against short term interruptions, normal power mode | c1 |
|  | 16 | 9.5.5.2.3 | Behaviour at the switch-over | c3 |
|  | 17 | 9.5.5.3.1 | DC unbalance of power sink 1 | c1 |
|  | 18 | 9.5.5.3.2 | Current unbalance in a pair | m |

c1 = m if A.1.2 else n/a.

c2 = n/a if A.1.2 else m.

c3 = m if A.1.3 else n/a.

c4 = n/a if A.1.3 else m.

c5 = m if A.1.4 else n/a.

c6 = o1 if A.1.2 else n/a.

c7 = o2 if A.1.3 else n/a.

c8 = n/a if A.1.3 else m.

o1 = Only one option shall be chosen.

o2 = Only one option shall be chosen.

A.3	Layer 2 TBR-RT

Table A.8: Layer 2 point-to-point configuration requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 10.3 | Does the TE support a configuration using only a single point-to-point data link? | o |
|  | 2 | 10 | Does the TE activate a physical layer connection between the TE and the network before the procedures of clause 10 are invoked? | m |

Table A.9: Layer 2 unacknowledged operation requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 10.4.1 | Transmission of unacknowledged information | c1 |
|  | 2 | 10.4.2 | Receipt of unacknowledged information | c1 |
|  | c1 = n/a if A.8.1 else m. |

Table A.10: Layer 2 TEI management requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 10.5.2 | TEI assignment procedure, automatic TEIs | c1 |
|  | 2 | 10.5.2 | TEI assignment procedure, non-automatic TEIs | c1 |
|  | 3 | 10.5.2.1 | Expiry of timer T202 | c2 |
|  | 4 | 10.5.3 | Operation of the TEI check procedure | c3 |
|  | 5 | 10.5.4.1 | Action taken by the data link layer entity receiving the MDL-REMOVE-REQUEST primitive | c2 |
|  | 6 | 10.5.4.2 | Conditions for TEI removal, receipt of an identity remove message | c2 |
|  | 7 | 10.5.4.2 | Conditions for TEI removal, receipt of MDL-ERROR INDICATION indicating possible multiple TEI assignment | c4 |
|  | 8 | 10.5.5.2 | Operation of the TEI identity verify procedure | c4 |
|  | 9 | 10.5.1 | General TEI management procedures | m |

c1 = n/a if A.8.1 else o1.

c2 = m if A.10.1 else n/a.

c3 = n/a if A.8.1 else m.

c4 = o21 if A.10.1 else n/a

o1 = One or more option shall be chosen.

o2 = One or more option shall be chosen.

Table A.11: Layer 2 establishment and release procedures requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 10.6.1.1 | General; Initiate DL on receipt of DL-Estab. Req | c3m |
|  | 2a | 10.6.1.2 | Establishment procedures; Data link establishment initiated (SABME send) by the TE | c1m |
|  | 2b | 10.6.1.2 | Establishment procedures; Data link establishment initiated (SABME send) by the network | c2 |
|  | 3 | 10.6.1.3 | Procedure on expiry of timer T200 | c3m |
|  | 4 | 10.6.2 | Termination of multiple frame operation | m |

c1 = m if A.1.8 or (A.1.7 and not A.1.5) else o

c2 = m if A.1.7 and A.1.5 else o

c3 = m if A.11.2a else n/a

Table A.12: Layer 2 multiple frame operation requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 10.7.1 | Transmitting I-frames | m |
|  | 2 | 10.7.2 | Receiving I-frames | m |
|  | 3 | 10.7.2.1 | P bit set to 1 | m |
|  | 4 | 10.7.2.2 | P bit set to 0 | m |
|  | 5 | 10.7.3 | Receiving acknowledgements | m |
|  | 6 | 10.7.4 | Receiving REJ frames | m |
|  | 7 | 10.7.5.1 | Receiving a valid RNR command or response | m |
|  | 8 | 10.7.5.2 | Expiry of timer T200 during "peer receiver busy" | m |
|  | 9 | 10.7.5.3 | Receiving a valid RNR command or response during "peer receiver busy" | m |
|  | 10 | 10.7.5.4 | Receiving a valid RR or REJ command during "peer receiver busy" | m |
|  | 11 | 10.7.5.5 | Appropriate supervisory response frame | m |
|  | 12 | 10.7.6 | Waiting acknowledgement | m |
|  | 13a | 10.8 | Re-establishment of multiple frame operation; Data link re-establishment initiated (SABME send) by the TE | m |
|  | 13b | 10.8 | Re-establishment of multiple frame operation; Data link re-establishment initiated (SABME send) by the network | m |

Table A.13: Layer 2 exception condition requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 10.9.1 | N(S) sequence error | m |
|  | 2 | 10.9.2 | Invalid frame condition | m |
|  | 3 | 10.9.3 | Frame rejection condition | m |
|  | 4 | 10.9.4 | Multiple-assignment of TEI value | c1 |
|  | c1 = m if A.10.1 else n/a. |

Table A.14: Layer 2 system parameters requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 10.10.7 | Layer 2 response time, TE not operating in accordance with subclause 10.3 (200 ms). | c1 |
|  | 2 | 10.10.7 | Layer 2 response time, TE operating in accordance with subclause 10.3 (500 ms). | c2 |

c1 = n/a if A.8.1 else m.

c2 = m if A.8.1 else n/a.

A.4	Layer 3 TBR-RT

Table A.15: Layer 3 Call establishment at the originating interface requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 11.4.1 | Call establishment at the originating interface | c3m |
|  | 2 | 11.4.1.1 | Call request, SETUP message with Sending Complete information element | c4o1 |
|  | 3 | 11.4.1.1 | Call request, SETUP message with all called party address information, but without Sending Complete information element | c4o1 |
|  | 4 | 11.4.1.1 | Call request, SETUP message without all called party address information | c4o1 |
|  | 5 | 11.4.1.2 | Overlap sending, enter Overlap sending state | c1 |
|  | 6 | 11.4.1.2 | Overlap sending, send INFORMATION messages | c2 |
|  | 7 | 11.4.1.3.1 | Call proceeding, en-bloc sending | c3m |
|  | 8 | 11.4.1.3.2 | Call proceeding, overlap sending | c1 |
|  | 9 | 11.4.1.4 | Call confirmation indication | c3m |
|  | 10 | 11.4.1.5 | Call connected | c3m |

c1 = m if A.1.8 and (A.15.3 or A.15.4) else n/a.

c2 = m if A.1.8 and A.15.4 else n/a.

c3 = m if A.1.8 else n/a.

c4 = o1 if A.1.8 else n/a.

o1 = One or more options shall be chosen.

Table A.16: Layer 3 Call establishment at the destination interface requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 11.4.2 | Call establishment at the destination interface | c5m |
|  | 2 | 11.4.2.1 | Incoming call, SETUP message delivered by point-to-point data link | c1 |
|  | 3 | 11.4.2.1 | Incoming call, SETUP message delivered by broadcast data link | c2 |
|  | 4 | 11.4.2.2.1 | Compatibility checking on Bearer capability information element, SETUP message delivered by point-to-point data link | c3 |
|  | 5 | 11.4.2.2.1 | Compatibility checking on Bearer capability information element, SETUP message delivered by broadcast data link | c4 |
|  | 6 | 11.4.2.2.1 | Compatibility checking on High layer compatibility information element, SETUP message delivered by broadcast data link | c4 |
|  | 7 | 11.4.2.2.1 | Compatibility checking on Low layer compatibility information element, SETUP message delivered by broadcast data link | c4 |
|  | 8 | 11.4.2.3.1 | B-channel selection-destination, SETUP message delivered by point-to-point data link | c1 |
|  | 9 | 11.4.2.3.2 | B-channel selection-destination, SETUP message delivered by broadcast data link. | c2 |
|  | 10 | 11.4.2.4 | Overlap receiving | c6o |
|  | 11 | 11.4.2.5.1 | Response to en-bloc SETUP or completion of overlap receiving | c5m |
|  | 12 | 11.4.2.6 | Call accept | c5m |
|  | 13 | 11.4.2.7 | Active indication | c5m |
|  | 14 | 11.4.2.8 | Non-selected user clearing | c4 |

c1 = m if A.1.7 and A.8.1 else n/a.

c2 = mn/a if A.1.7 and not A.8.1 else n/am.

c3 = o if A.1.7 and A.8.1 else n/a.

c4 = on/a if A.1.7 and not A.8.1 else n/ao.

c5 = m if A.1.7 else n/a

c6 = o if A.1.7 else n/a

Table A.17: Layer 3 Call clearing requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 11.4.3.2 | Exception conditions; case a) (Note 1) | c1m |
|  | 2 | 11.4.3.3 | Clearing initiated by the user | c2m |
|  | 3 | 11.4.3.4.1 | Clearing when tones/announcements provided, Disconnect Indication state entered | o1 |
|  | 4 | 11.4.3.4.1 | Clearing when tones/announcements provided, Release Request state entered | o1 |
|  | 5 | 11.4.3.4.2 | Clearing when tones/announcements not provided | m |
|  | 6 | 11.4.3.4.3 | Completion of clearing | m |
|  | 7a | 11.4.3.5 | Clear collision; DISCONNECT collision | c3m |
|  | 7b | 11.4.3.5 | Clear collision; RELEASE collision | m |

o1 = One or more options shall be chosen.

c1 = m if A.1.8 and A.1.5 else o

c2 = m if A.1.8 else o

c3 = m if A.17.2 else n/a

Note 1: Add the following text to case a): An outgoing only p-to-p TE shall reject an incoming SETUP with a RELEASE COMPLETE, release CR and go to state 0. An outgoing only p-to-mp TE shall either ignore an incoming SETUP or shall reject an incoming SETUP with a RELEASE COMPLETE, release CR and go to state 0.

Table A.18: Layer 3 Call rearrangements requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 11.4.4.1 | Call suspension | o |
|  | 2 | 11.4.4.2 | Call suspended | c1 |
|  | 3 | 11.4.4.3 | Call suspend error | c1 |
|  | 4 | 11.4.4.4 | Call re-establishment | c1 |
|  | 5 | 11.4.4.5 | Call resume errors | c1 |
|  | c1 = m if A.18.1 else n/a. |

Table A.19: Layer 3 error conditions requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 11.4.6.2 | Call reference procedural errors | m |
|  | 2 | 11.4.6.3 | Message type or message sequence errors | m |
|  | 3 | 11.4.6.4 | Duplicated information elements | m |
|  | 4a | 11.4.6.5.1 | Mandatory information element missing in SETUP message | c2m |
|  | 4b | 11.4.6.5.1 | Mandatory information element missing in RELEASE message | m |
|  | 5 | 11.4.6.6.1 | Unrecognized information element | m |
|  | 6 | 11.4.6.6.2 | Non-mandatory information element content error | m |
|  | 7 | 11.4.6.7 | Status enquiry procedure | m |
|  | 8 | 11.4.6.8 | Receiving a STATUS message | m |
|  | 9 | 11.4.7 | User notification procedure | m |
|  | 10 | 11.4.8 | Restart procedure | c1 |
|  | 11 | 11.5 | TE Timer T305 | c3m |
|  | 12 | 11.5 | TE Timer T308 | m |

c1 = m if A.8.1 else n/a.

c2 = m if A.1.7 else n/a.

c3 = m if A.17.2 else n/a