ITAAB

TRAC ISDN Type Approval Advisory Board

Annex A (Normative)

to

ITAAB Advisory Note Number: 072 rev. 1

Date:	1998-09-03

Subject:	TBR-RT applicable to EURO-ISDN primary rate access terminal equipment capable of handling only incoming or only outgoing calls.

TBR Requirements Table (TBR-RT)

A.2	General type, Llayer 1 and overvoltage requirements TBR-RT

Table A.1: General type, Llayer 1 and overvoltage conditions table

| Reference | Condition | Status | Support (Y/N) | Comment |
| --- | --- | --- | --- | --- |
| 1 | Is TE mains powered? | o |
| Affects requirements in clause 8. |
| 2 | Is the TE able to operate with ISDN incoming calls? | o1 |
| Affects requirements in clause 10 and 11. |
| 3 | Is the TE able to operate with ISDN outgoing calls? | o1 |
| Affects requirements in clause 10 and 11. |
| o1 = Only one option shall be chosen |

Table A.2: Overvoltage requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 8.1 | Impulse transfer from mains, common mode | c1 |
|  | 2 | 8.2 | Impulse transfer from mains, transverse mode | c1 |
|  | 3 | 8.3 | Conversion of common mode to transverse mode | m |
|  | c1 = m if A.1.1 else n/a |

Table A.3: Layer 1 physical characteristics requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 9.1.1 | Hardwiring | m |
|  | 2 | 9.1.2 | Alternative connection method | o |

Table A.4: Layer 1 output port electrical requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 9.2.1 | Waveform shape | m |
|  | 2 | 9.2.2 | Impedance towards ground | m |
|  | 3 | 9.2.3 | Clock accuracy | m |
|  | 4 | 9.2.4a | Output jitter, input timing derived from the same primary rate access | o1 |
|  | 5 | 9.2.4b | Output jitter, input timing derived from a different primary rate access | o1 |
|  | 6 | 9.2.4c | Output jitter, input timing derived from a non-ISDN 2 048 kbit/s access | o1 |
|  | 7 | 9.2.4d | Output jitter, input timing derived from internal source. | o1 |
|  | 8 | 9.2.4e | Output jitter, input timing derived from dedicated external reference | o1 |
|  | o1 = One or more options shall be chosen. |

Table A.5: Layer 1 input port electrical requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 9.3.1 | Return loss | m |
|  | 2 | 9.3.2 | Immunity to attenuation and reflections | m |
|  | 3 | 9.3.3 | Jitter tolerance | m |
|  | 4 | 9.3.4 | Tolerable longitudinal voltage | m |
|  | 5 | 9.3.5 | Impedance towards ground | m |

Table A.6: Layer 1 frame structure requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 9.4.4 | Allocation of bits number 1 to 8 of the frame | m |
|  | 2 | 9.4.8 | Use of bit 1 in 2 048 kbit/s CRC-4 multiframe | m |
|  | 3 | 9.4.9 | D-channel | m |

Table A.7: Layer 1 operational functions requirements table

| No | Ref | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 9.5.4.2.1 | Anomalies and defect detection | m |
|  | 2 | 9.5.4.2.2 | Detection of defect indication signals | m |
|  | 3 | 9.5.4.2.3 | Consequent actions | m |
|  | 4 | 9.5.5.1 | Loss of frame alignment | m |
|  | 5 | 9.5.5.2 | Strategy for frame alignment recovery | m |
|  | 6 | 9.5.5.3 | CRC multiframe alignment using information in bit 1 of the basic frame | m |
|  | 7 | 9.5.5.4 | CRC bit monitoring | m |
|  | 8 | 9.5.5.5 | Monitoring for false frame alignment | m |

A.3	Layer 2 TBR-RT

Table A.8 Layer 2 point-to-point configuration requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 10.3 | Does the TE support a configuration using only a single point-to-point data link? | o |

Table A.9 Layer 2 unacknowledged operation requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 10.4.1 | Transmission of unacknowledged information | c1 |
|  | 2 | 10.4.2 | Receipt of unacknowledged information | c1 |
|  | c1 = n/a if A.8.1 else m |

Table A.10 Layer 2 TEI management requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 10.5.2 | TEI assignment procedure, automatic TEIs | c1 |
|  | 2 | 10.5.2 | TEI assignment procedure, non-automatic TEIs | c1 |
|  | 3 | 10.5.2.1 | Expiry of timer T202 | c2 |
|  | 4 | 10.5.3 | Operation of the TEI check procedure | c3 |
|  | 5 | 10.5.4.1 | Action taken by the data link layer entity receiving the MDL-REMOVE-REQUEST primitive | c2 |
|  | 6 | 10.5.4.2 | Conditions for TEI removal, receipt of an identity remove message | c2 |
|  | 7 | 10.5.4.2 | Conditions for TEI removal, receipt of MDL-ERROR INDICATION indicating possible multiple TEI assignment | c4 |
|  | 8 | 10.5.5.2 | Operation of the TEI identity verify procedure | c4 |
|  | 9 | 10.5.1 | General TEI management procedures | m |

c1 = n/a if A.8.1 else o1

c2 = m if A.10.1 else n/a

c3 = n/a if A.8.1 else m

c4 = o21 if A.10.1 else n/a

o1 = One or more option shall be chosen.

o2 = One or more option shall be chosen.

Table A.11: Layer 2 establishment and release procedures requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 10.6.1.1 | General; Initiate DL on receipt of DL-Estab. Req. | c3m |
|  | 2a | 10.6.1.2 | Establishment procedures; Data link establishment initiated (SABME send) by the TE | c1m |
|  | 2b | 10.6.1.2 | Establishment procedures; Data link establishment initiated (SABME send) by the network | c2 |
|  | 3 | 10.6.1.3 | Procedure on expiry of timer T200 | c3m |
|  | 4 | 10.6.2 | Termination of multiple frame operation | m |

c1 = m if A.1.3 else o.

c2 = m if A.1.2 else o

c3 = m if A.11.2a else n/a

Table A.12: Layer 2 multiple frame operation requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 10.7.1 | Transmitting I-frames | m |
|  | 2 | 10.7.2 | Receiving I-frames | m |
|  | 3 | 10.7.2.1 | P bit set to 1 | m |
|  | 4 | 10.7.2.2 | P bit set to 0 | m |
|  | 5 | 10.7.3 | Receiving acknowledgements | m |
|  | 6 | 10.7.4 | Receiving REJ frames | m |
|  | 7 | 10.7.5.1 | Receiving a valid RNR command or response | m |
|  | 8 | 10.7.5.2 | Expiry of timer T200 during "peer receiver busy" | m |
|  | 9 | 10.7.5.3 | Receiving a valid RNR command or response during "peer receiver busy" | m |
|  | 10 | 10.7.5.4 | Receiving a valid RR or REJ command during "peer receiver busy" | m |
|  | 11 | 10.7.5.5 | Appropriate supervisory response frame | m |
|  | 12 | 10.7.6 | Waiting acknowledgement | m |
|  | 13a | 10.8 | Re-establishment of multiple frame operation; Data link re-establishment initiated (SABME send) by the TE | m |
|  | 13b | 10.8 | Re-establishment of multiple frame operation; Data link re-establishment initiated (SABME send) by the network | m |

Table A.13: Layer 2 exception condition requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 10.9.1 | N(S) sequence error | m |
|  | 2 | 10.9.2 | Invalid frame condition | m |
|  | 3 | 10.9.3 | Frame rejection condition | m |
|  | 4 | 10.9.4 | Multiple-assignment of TEI value | c1 |
|  | c1 = m if A.10.1 else n/a |

Table A.14: Layer 2 system parameters requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 10.10.7 | Layer 2 response time, TE not operating in accordance with 10.3 (200 ms) | c1 |
|  | 2 | 10.10.7 | Layer 2 response time, TE operating in accordance with 10.3 (500 ms) | c2 |

c1 = n/a if A.8.1 else m

c2 = m if A.8.1 else n/a

A.4	Layer 3 TBR-RT

Table A.15: Layer 3 Call establishment at the originating interface requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 11.4.1 | Call establishment at the originating interface | c3m |
|  | 2 | 11.4.1.1 | Call request, SETUP message with Sending Complete information element | c4o1 |
|  | 3 | 11.4.1.1 | Call request, SETUP message with all called party address information, but without Sending Complete information element | c4o1 |
|  | 4 | 11.4.1.1 | Call request, SETUP message without all called party address information | c4o1 |
|  | 5 | 11.4.1.2 | Overlap sending, enter Overlap sending state | c1 |
|  | 6 | 11.4.1.2 | Overlap sending, send INFORMATION messages | c2 |
|  | 7 | 11.4.1.3.1 | Call proceeding, en-bloc sending | c3m |
|  | 8 | 11.4.1.3.2 | Call proceeding, overlap sending | c1 |
|  | 9 | 11.4.1.4 | Call confirmation indication | c3m |
|  | 10 | 11.4.1.5 | Call connected | c3m |

c1 = m if A.1.3 and (A.15.3 or A.15.4) else n/a.

c2 = m if A.1.3 and A.15.4 else n/a.

c3 = m if A.1.3 else n/a.

c4 = o1 if A.1.3 else n/a.

o1 = One or more options shall be chosen.

Table A.16: Layer 3 Call establishment at the destination interface requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 11.4.2 | Call establishment at the destination interface | c1m |
|  | 2 | 11.4.2.1 | Incoming call, SETUP message delivered by point-to-point data link | c1m |
|  | 3 | 11.4.2.2.1 | Compatibility checking on Bearer capability information element, SETUP message delivered by point-to-point data link | c2o |
|  | 4 | 11.4.2.3.1 | B-channel selection-destination, SETUP message delivered by point-to-point data link | c1m |
|  | 5 | 11.4.2.4 | Overlap receiving | c2o |
|  | 6 | 11.4.2.5.1 | Response to en-bloc SETUP or completion of overlap receiving | c1m |
|  | 7 | 11.4.2.6 | Call accept | c1m |
|  | 8 | 11.4.2.7 | Active indication | c1m |

c1 = m if A.1.2 else n/a.

c2 = o if A.1.2 else n/a

Table A.17: Layer 3 Call clearing requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 11.4.3.2 | Exception conditions; case a) (Note 1) | c1m |
|  | 2 | 11.4.3.3 | Clearing initiated by the user | c2m |
|  | 3 | 11.4.3.4.1 | Clearing when tones/announcements provided, Disconnect Indication state entered | o1 |
|  | 4 | 11.4.3.4.1 | Clearing when tones/announcements provided, Release Request state entered | o1 |
|  | 5 | 11.4.3.4.2 | Clearing when tones/announcements not provided | m |
|  | 6 | 11.4.3.4.3 | Completion of clearing | m |
|  | 7a | 11.4.3.5 | Clear collision; DISCONNECT collision | c3m |
|  | 7b | 11.4.3.5 | Clear collision; RELEASE collision | m |

o1 = One or more options shall be chosen.

c1 = m if A.1.3 else o

c2 = m if A.1.8 else o

c3 = m if A.17.2 else n/a

Note 1: Add the following text to case a): An outgoing only p-to-p TE shall reject an incoming SETUP with a RELAESE COMPLETE, release CR and go to state 0

Table A.18: Layer 3 error conditions requirements table

| No. | Reference | TBR Requirement | Status | Support (Y/N) |
| --- | --- | --- | --- | --- |
| 1 | 11.4.6.2 | Call reference procedural errors | m |
|  | 2 | 11.4.6.3 | Message type or message sequence errors | m |
|  | 3 | 11.4.6.4 | Duplicated information elements | m |
|  | 4a | 11.4.6.5.1 | Mandatory information element missing in SETUP message | c1m |
|  | 4b | 11.4.6.5.1 | Mandatory information element missing in RELEASE message | m |
|  | 5 | 11.4.6.6.1 | Unrecognized information element | m |
|  | 6 | 11.4.6.6.2 | Non-mandatory information element content error | m |
|  | 7 | 11.4.6.7 | Status enquiry procedure | m |
|  | 8 | 11.4.6.8 | Receiving a STATUS message | m |
|  | 9 | 11.4.7 | User notification procedure | m |
|  | 10 | 11.4.8 | Restart procedure | m |
|  | 11 | 11.5 | TE Timer T305 | c2m |
|  | 12 | 11.5 | TE Timer T308 | m |

c1 = m if A.1.2 else n/a.

c2 = m if A.17.2 else n/a