ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 076 rev. 1

Date:	1998-09-07

Subject:	Problem with performing the functional characteristics tests at Basic Access Layer 1 for TEs with an unstable state F3

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

X	CTR 33 (Commission Decision 98/521/EC)

In consideration of the following:

-	The TTCN test cases of TBR 3 as amended by TBR 3/A1 are originally written for IUTs which only activate at request from the user or the network;

-	The TTCN test cases of TBR 33 are based on the test descriptions from TBR 3, and therefore also intended for IUTs which only activate at request from the user or the network;

-	There are IUTs (e.g. PBXs) which activate layer 1 (i.e. send INFO 1) automatically. These IUTs are unstable in state F3;

-	This activation can be forced by layer 1, layer 2 or higher layers;

-	To perform some of the functional characteristics tests at Basic Access layer 1, it is required that the TE is stable in state F3 for a definite time;

-	There is no definition of a minimum time for a TE to be stable in state F3;

-	Some of the TTCN tests have problems with such IUTs.

ITAAB advises the following:

Definition of a minimum time:
Due to the testability it is recommended to implement a time of min. 1600 ms (between PH-DI and PH-AR) to be stable in state F3.

This behaviour (unstable state F3) will force an "automatic call request". It is in the knowledge of the test laboratory to decide whether this is an allowed behaviour or not (problem is under investigation). In any case, a "manual call request" can be forced by setting timer TWAIT to a value less than the implemented repetition rate.

In tests CPF6PHARa, CPF8PHARa and CPF8PHDI_I0T3 unexpected Lap-D-Frames may occur. This is covered by Advisory Note 069 rev. 1.

If the implemented repetition rate is less than Timer T3_S, there will be problems with test AD15_CHK_T3: An IUT which is unstable in state F3 may execute a new physical activation request while timer T3 is running. If this new physical activation request is forced by layer 2 (or higher layers) and not by layer 1, this is an allowed behaviour. If the analysis of the behaviour shows that test AD15_CHK_T3 fails due to this behaviour, a manual verdict of PASS shall be assigned to this test.