ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 080 rev. 1

Date:	1999-02-16

Subject:	Use of preferred/exclusive bit in the RESTART ACK PDU in TC19003

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

X	CTR 4 Amendment 1 (Commission Decision 98/518/EC)

X	CTR 33 (Commission Decision 98/521/EC)

X	CTR 34 (Commission Decision 98/520/EC)

For the purposes of the above described applicability, this note specifically contains amendments to:

TBR 3, Amendment A1, December 1997: Attachment requirements for terminal equipment to connect to an ISDN using ISDN basic access.

TBR 4, Amendment A1, December 1997: Attachment requirements for terminal equipment to connect to an ISDN using ISDN primary rate access.

TBR 33, December 1997: Attachment requirements for packet mode terminal equipment to connect to an ISDN using ISDN basic access.

TBR 34, December 1997: Attachment requirements for packet mode terminal equipment to connect to an ISDN using ISDN primary rate access.

In consideration of the following:

-	The RESTART PDU in TC19003 is sent with "exclusive" B-channel.

-	If the TE answers RESTART ACK with "preferred" B-channel, the test fails and the check state CS50001 is not executed.

-	There is no indication in the requirements concerning the use of the preferred/exclusive bit in RESTART ACK PDU.

ITAAB advises the following:

The preferred/exclusive bit in the received RESTART ACK PDU is allowed to have any value.

The following changes shall be performed in the layer 3 Abstract Test Suite of TBR 3/A1:

Structured Type Constraint CHI11 shall be replaced with the following:

| Structured Type Constraint |
| --- |
| Constraint Name: | CHI11(PAR:BITSTRING) |
| Structured Type: | CHI_T |
| Derivation Path: |
|  | Encoding Variation: |
|  | Comments: |
|  | Element Name | Element Value | Comments |
| CHI_I | '00011000'B |
|  | CHI_L | '00000001'B |
|  | CHI_E3_P1 | '1000'B |
|  | CHI_E3_PE | '1?'B |
|  | CHI_E3_P3 | '0'B |
|  | CHI_E3_P4 | PAR |
|  | Detailed Comments: Used in RESTART ACKNOWLEDGE PDU. Indicates specific B-channel which has been restarted (LT <--- IUT). |

The following changes shall be performed in the layer 3 Abstract Test Suite of TBR 4/A1:

Structured Type Constraint CHI11 shall be replaced with the following:

| Structured Type Constraint |
| --- |
| Constraint Name: | CHI11(PAR:BITSTRING) |
| Structured Type: | CHI_T |
| Derivation Path: |
|  | Encoding Variation: |
|  | Comments: |
|  | Element Name | Element Value | Comments |
| CHI_I | '00011000'B |
|  | CHI_L | '00000011'B |
|  | CHI_E3_P1 | '1010'B |
|  | CHI_E3_PE | '?1'B |
|  | CHI_E3_P3 | '001'B |
|  | CHI_E4 | '83'O |
|  | CHI_E5_CH1 | '1'B |
|  | CHI_E5_CH2 | PAR |

Detailed Comments:

Used in RESTART ACKNOWLEDGE PDU. Indicates a specific B-channel which has been restarted (LT <--- IUT).

The following changes shall be performed in the layer 3 Abstract Test Suite of TBR 33:

Structured Type Constraint Declaration CHI11 shall be added:

| Structured Type Constraint Declaration |
| --- |
| Constraint Name: | CHI11(PAR:BITSTRING) |
| Structured Type: | CHI_T |
| Derivation Path: |
|  | Encoding Variation: |
|  | Comments: |
|  | Element Name | Element Value | Comments |
| CHI_I | '00011000'B |
|  | CHI_L | '00000001'B |
|  | CHI_E3_P1 | '1000'B |
|  | CHI_E3_PE | '?'B |
|  | CHI_E3_P3 | '0'B |
|  | CHI_E3_P4 | PAR |
|  | Detailed Comments: Used in RESTART ACKNOWLEDGE PDU. Indicates specific B-channel which has been restarted (LT <--- IUT). |

PDU Constraint Declaration RSA6shall be replaced with the following:

| PDU Constraint Declaration |
| --- |
| Constraint Name: | RSA6 (PAR:BITSTRING) |
| PDU Type: | B_PDU |
| Derivation Path: | BASE. |
| Comments: | Direction: LT <--- IUT |
| Field Name | Field Value | Comments |
| CR | CR51 |
|  | MT | '01001110'B |
|  | CHI | CHI110 (PAR) |
|  | RI | RI4 |
|  | Detailed Comments: |

PDU without optional parameters;

CHI mandatory if RI is "indicated channels";

DSP optional LT parameter; no IUT parameter;

RI indicates 'single interface' or 'all interfaces'; mandatory LT and IUT parameter;

The following changes shall be performed in the layer 3 Abstract Test Suite of TBR 34:

Structured Type Constraint Declaration CHI11 shall be added:

| Structured Type Constraint Declaration |
| --- |
| Constraint Name: | CHI11(PAR:BITSTRING) |
| Structured Type: | CHI_T |
| Derivation Path: |
|  | Encoding Variation: |
|  | Comments: |
|  | Element Name | Element Value | Comments |
| CHI_I | '00011000'B |
|  | CHI_L | '00000011'B |
|  | CHI_E3_P1 | '1010'B |
|  | CHI_E3_PE | '?'B |
|  | CHI_E3_P3 | '001'B |
|  | CHI_E4 | '83'O |
|  | CHI_E5_CH1 | '1'B |
|  | CHI_E5_CH2 | PAR |
|  | Detailed Comments: Used in RESTART ACKNOWLEDGE PDU. Indicates specific B-channel which has been restarted (LT <--- IUT). |

PDU Constraint Declaration RSA6shall be replaced with the following:

| PDU Constraint Declaration |
| --- |
| Constraint Name: | RSA6 (PAR:BITSTRING) |
| PDU Type: | B_PDU |
| Derivation Path: | BASE. |
| Comments: | Direction: LT <--- IUT |
| Field Name | Field Value | Comments |
| CR | CR51 |
|  | MT | '01001110'B |
|  | CHI | CHI110 (PAR) |
|  | RI | RI4 |
|  | Detailed Comments: |

PDU without optional parameters;

CHI mandatory if RI is "indicated channels";

DSP optional LT parameter; no IUT parameter;

RI indicates 'single interface' or 'all interfaces'; mandatory LT and IUT parameter;