ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 082 rev. 1

Date:	1998-09-07

Subject:	Connection of the simulator to the IUT:

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 4 Amendment 1 (Commission Decision 98/518/EC)

X	CTR 34 (Commission Decision 98/520/EC)

For the purposes of the above described applicability, this note specifically contains amendments to:

TBR 4, November 1995: Attachment requirements for terminal equipment to connect to an ISDN using ISDN primary rate access.

In consideration of the following:

TBR 4 subclause 9.1 defines the connection points for testing;

The first sentence specifies “For testing the electrical characteristics the simulator, or its relevant part, shall be connected directly to the interconnecting points for the interface wiring at the IUT unless otherwise stated;

There is no requirement for the IUT to support interconnecting points other than complying with TBR 4 subclause 9.1;

-	The list of electrical tests in TBR 4 Clause B.1.3 for which the connection cord may be removed does not include test B.3.3 which may experience similar impairments due to cable characteristics to the listed tests;

-	TBR 34 references the layer 1 tests of TBR 4 for equipment using on-demand access.

ITAAB advises the following:

When performing the test given in subclause B.3.3 of TBR 4 to verify compliance with TBR 4, as amended amended by TBR 4/A1, or TBR 34, a cord connected at the IUT shall be removed.

The following changes shall be performed in TBR 4:

Subclause B.1.3 shall be modified as follows:

B.1.3	Connection of the simulator to the IUT

Reference: ETS 300 011, annex C, subclause C.1.3.

For testing the electrical characteristics of the IUT, the simulator, or its relevant part, shall be connected directly to the interconnecting points for the interface wiring at the IUT unless otherwise stated. For the tests given in subclauses B.2.1, B.2.2, B.3.1, B.3.2, B.3.3, B.3.4 and B.3.5 a cord connected at an IUT shall be removed since a cord is regarded as integral part of the interface wiring.

All other tests may be performed with interface wiring complying with the requirements given in subclause 9.1.