ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 084 rev. 1

Date:	1998-09-07

Subject:	Layer 3 response time in Primary Rate Access layer 2 tests

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 4 Amendment 1 (Commission Decision 98/518/EC)

X	CTR 34 (Commission Decision 98/520/EC)

For the purposes of the above described applicability, this note specifically contains amendments to:

TBR 4, Amendment A1, December 1997: Attachment requirements for terminal equipment to connect to an ISDN using ISDN primary rate access.

TBR 34, December 1997: Attachment requirements for packet mode terminal equipment to connect to an ISDN using ISDN primary rate access.

In consideration of the following:

-	In the layer 2 test cases in TBR 4/A1 and in TBR 34 the time allowed for layer 3 in the SUT to respond to messages sent by the tester is 30s. In some test cases the IUT is held in state 7.4 for a period to allow time for layer 3 to respond to two or more messages. Since the time allowed for each message is 30s, the IUT will be held in state 7.4 for a period of 60s or longer before the test continues;

-	In some test cases (e.g. TC27076) this can result in the test having an unreasonably long duration and the trace being unnecessarily large;

-	A TE with a long response time may not interwork satisfactorily with the network and therefore such TEs are unlikely to be produced.

ITAAB advises the following:

When the layer 2 tests from TBR 4/A1 or TBR 34 are used for compliance verification, the duration of timer TWL3 may be reduced. If the client has indicated the maximum layer 3 response time of the IUT then this value should be used as the duration of TWL3. If no such time has been indicated then a value chosen by the test laboratory should be used; however, if any fail or inconclusive verdicts are obtained, which may be due to a slow layer 3 response, the value used should be increased and the test repeated.

The corresponding modifications to the ATS in TBR 4/A1 are as follows:

| Test Suite Parameter Declarations |
| --- |
| Parameter Name | Type | PICS/PIXIT Ref | Comments |
| PC_PTMP_L2 | BOOLEAN | A.8.1 | TRUE if the IUT does not use a single point to point data link. |
| ... | ... | ... | ... |
| PX_COMPAT_SETUP | OCTETSTRING | E.6.1 |

A compatible SETUP PDU without Channel identification information element.

| TWL3_MAX | INTEGER | E.6.1 | Maximum layer 3 response time (seconds) |
| --- | --- | --- | --- |

| Test Suite Constant Declarations |
| --- |
| Constant Name | Type | Value | Comments |
| ... | ... | ... | ... |
| T202VMIN | INTEGER | 1900 |

T202 lower limit 1,9 s

| TWL3_MAX | INTEGER | 32 |
| --- | --- | --- |

Layer 3 response time 32 s

| N200 | INTEGER | 3 | Maximum number of re-transmissions |
| --- | --- | --- | --- |
| ... | ... | ... | ... |

The corresponding modifications to the ATS in Annex C of TBR 34 are as follows:

| Test Suite Parameter Declarations |
| --- |
| Parameter Name | Type | PICS/PIXIT Ref | Comments |
| ... | ... | ... | ... |
| PX_L3_SOL_RSP | L3_INFO_TYPE | E.6.4 |

Soliciting Message Command to the IUT  (4)

| TWL3_MAX | INTEGER | E.6.5 | Maximum layer 3 response time (seconds) |
| --- | --- | --- | --- |
|  | ... |

| Test Suite Constant Declarations |
| --- |
| Constant Name | Type | Value | Comments |
| ... | ... | ... | ... |
| T200VMIN | INTEGER | 950 |

T200 lower limit 0,95 s

| TWL3_MAX | INTEGER | 32 |
| --- | --- | --- |

Layer 3 response time 32 s

| N200 | INTEGER | 3 | Maximum number of retransmissions |
| --- | --- | --- | --- |
| ... | ... | ... | ... |

The following changes shall be performed in Annex E of TBR 34:

Table E.3, Suppliers's additional information, shall be modified as follows:

| Item | Description |
| --- | --- |
| ... | ... |
| E.6.4 |

Indicate a coding of an information field containing a response message to the soliciting message as given in subclause E.6.3.

(Example codings:

SAPI = 0: RELEASE COMPLETE message '080280015A'O

SAPI = 16: RESTART CONFIRM message '1000FF'O)

E.6.5

Indicate the maximum layer 3 response time for the SUT to respond to a layer 3 message.