ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 085 rev. 1

Date:	1998-09-07

Subject:	Information element checking in layer 3 TC20002

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

X	CTR 4 Amendment 1 (Commission Decision 98/518/EC)

In consideration of the following:

-	Layer 3 test case TC20002 checks that the BCAP, HLC and LLC IEs in the SETUP message sent by the IUT are as indicated in the PIXIT;

-	In the PIXIT there are different items for the IEs sent by the IUT in the SETUP message and the compatible IEs to be sent to the IUT by the tester. The ATSs in TBR 3/A1 and TBR 4/A1 only have one parameter for each of these items and the PIXIT reference given is to the IE to be sent to the IUT;

-	This could result in incorrect verdicts if the IUT includes one of these IEs in SETUP messages it sends, but does not require it for compatibility checking (and hence no value is required in the parameter relating to incoming SETUPs), or if different values are declared for outgoing and incoming SETUPs.

ITAAB advises the following:

If possible, the IUT should be configured so that the compatible value of each of BCAP, HLC and LLC, to be included in SETUP messages sent to the IUT, is the same as the value included in outgoing SETUP messages sent by the IUT.

The test suite parameters BCAPV, HLCV and LLCV should be set as described below:

-	if the value of the "Incoming PIXIT item" and the "Outgoing PIXIT item" for the Information Element corresponding to the parameter (as indicated in the table below) are the same, or a value is only given for one of them, the parameter should be set to that value; or

-	if different values are provided for the Incoming and Outgoing PIXIT items, the parameter should be set to the value of the Outgoing PIXIT item for TC20002 and the Incoming PIXIT item for other Test Cases.

| Information Element | Parameter | Incoming PIXIT item | Outgoing PIXIT item |
| --- | --- | --- | --- |
| Bearer Capability | BCAPV | E.8.11 | E.8.3 |
| High Layer Compatibility | HLCV | E.8.13 | E.8.5 |
| Low layer Compatibility | LLCV | E.8.15 | E.8.7 |