ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 086 rev 1

Date:	1998-09-07

Subject:	Layer 2 test case TC27031

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

X	CTR 4 Amendment 1 (Commission Decision 98/518/EC)

X	CTR 33 (Commission Decision 98/521/EC)

X	CTR 34 (Commission Decision 98/520/EC)

For the purposes of the above described applicability, this note specifically contains amendments to:

TBR 3 Amendment A1, December 1997: Attachment requirements for terminal equipment to connect to an ISDN using ISDN basic access

TBR 4 Amendment A1, December 1997: Attachment requirements for terminal equipment to connect to an ISDN using ISDN primary rate access.

TBR 34, December 1997: Attachment requirements for packet mode terminal equipment to connect to an ISDN using ISDN primary rate access.

In consideration of the following:

-	It is permissible for a TE to support both TEI removal and TEI identity verify on detecting possible multiple TEI assignment, and if both are supported the circumstances in which each is used are not indicated in the TBR-RT;

-	Test case TC27031 in TBR 3/A1, TBR 4/A1, TBR 33 and TBR 34, which tests the behaviour of the IUT on receiving an unsolicited UA F=1 frame in state 7.0 (i.e. a situation in which the IUT should detect multiple TEI assignment), gives a Fail verdict if the IUT removes its TEI and support for TEI identity verify is declared even if removal of TEI on detecting possible multiple TEI assignment is also supported;

-	It is essential that a TE supporting automatic TEI assignment supports at least one of TEI removal or TEI identity verify on detecting possible multiple TEI assignment;

-	The TBR-RT in TBR 3/A1 and TBR 4/A1 does not decribe correctly that at least one of these procedures shall be supported;

-	The TBR-RT in TBR 34 does not describe the condition for TEI removal on MDL-ERROR INDICATION correctly.

ITAAB advises the following:

The following changes shall be performed in the standards forming basis of the compliance verification:

-	The TBR-RT in TBR 3/A1 and TBR 4/A1 shall be corrected by changing the notes to table A.10 as follows:

c4 = o21 if A.10.1 else n/a

o2 = One or more option shall be chosen.

-	The TBR-RT in TBR 34 shall be corrected by changing item 7 of table A.17 as follows:

| 7 | 10.5.4.2 | Conditions for TEI removal, receipt of MDL-ERROR INDICATION indicating possible multiple TEI assignment | c42 |
| --- | --- | --- | --- |

The following advice applies during the compliance verification:

-	If both A.10.7 and A.10.8 are TRUE when performing compliance verification according to TBR 3, as amended by TBR 3/A1, or acording to TBR 4, as amended by TBR 4/A1, or

-	If both A.20.7 and A.20.8 are TRUE when performing compliance verification according to TBR 33, or

-	If both A.17.7 and A.17.8 are TRUE when performing compliance verification according to TBR 34,

(i.e the IUT supports both the procedures for TEI removal and for TEI identity verify on detecting possible multiple TEI assignment) and a FAIL verdict is obtained for TC27031 with the parameter PC_VER_TEI_C set to TRUE then this test case should be re-run with the parameter PC_VER_TEI_C set to FALSE. A PASS verdict should be issued for TC27031 if a PASS verdict  is obtained for either value of this parameter.