ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 088 rev. 1

Date:	1998-09-07

Subject:	Postamble CHECK_F1

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

X	CTR 33 (Commission Decision 98/521/EC)

For the purposes of the above described applicability, this note specifically contains amendments to:

TBR 3, Amendment A1, December 1997: Attachment requirements for terminal equipment to connect to an ISDN using ISDN basic access.

TBR 3, November 1995: Attachment requirements for terminal equipment to connect to an ISDN using ISDN basic access.

TBR 33, December 1997: Attachment requirements for packet mode terminal equipment to connect to an ISDN using ISDN basic access.

In consideration of the following:

-	Tests AD3aF2_PS_OFF, AD9aF3_PS_OFF, AD16aF4_PS_OFF, AD22aF5_PS_OFF, AD28aF6_PS_OFF, AD35aF7_PS_OFF and AD40aF8_PS_OFF in TBR 3/A1 and TBR 33 check state F1 after switching off power source 1.

-	Tests AD3bF2_LP_OFF, AD9bF3_LP_OFF, AD16bF4_LP_OFF, AD22bF5_LP_OFF, AD28bF6_LP_OFF, AD35bF7_LP_OFF and AD40bF8_LP_OFF in TBR 3/A1 and TBR 33 check state F1 after switching off the local power supply.

-	No maximum time to reach F1 after switching off PS1 or LP is specified.

-	Due to the characteristics of the feeding circuit or the local power supply of some IUTs a delay may be necessary.

-	In postamble CHECK_F1 in TBR 3/A1 and TBR 33 there is no delay between switching off PS1 and checking F1. For the characteristics of a feeding circuit a delay may be necessary.

-	In postamble CHECK_F1 in TBR 3/A1 and TBR 33 there is no delay between switching off LP and checking F1. (In postamble CHECK_F1 of TBR 3 there was a delay, TNOAC, between switching off LP and checking F1.) For the characteristics of a local power supply a delay longer than TNOAC may be necessary.

-	When testing IUTs according to TBR 3/A1 or TBR 33 these tests may fail.

ITAAB advises the following:

The following changes shall be performed in the layer 1 Abstract Test Suites of TBR 3/A1:

The Test Suite Parameter Declarations shall be modified as follows:

| Test Suite Parameter Declarations |
| --- |
| Parameter Name | Type | PICS/PIXIT Ref | Comments |
| ... | ... | ... | ... |
| T3_4T200 | BOOLEAN | - | TRUE if T3 > 4xT200 |
| PX_T_F1 | INTEGER | E.3.9 | Duration to reach F1 after switch off PS1 or LP (s) |

The Timer Declarations shall be modified as follows:

| Timer Declarations |
| --- |
| Timer Name | Duration | Unit | Comments |
| ... | ... | ... | ... |
| T4 | T4VMAX | ms | Value of T4 max plus 5%. |
| T_F1 | PX_T_F1 | s | Ensure that F1 has been reached |

Postamble CHECK_F1 shall be modified as follows:

| Test Step Dynamic Behaviour |
| --- |
| Test Step Name: | CHECK_F1 |
| Group: | ISDN1_TS/MISCELLANEOUS/ |
| Objective: | To check that IUT is in state F1. |
| Default: | DEF_1 |
| Nr | Label | Behaviour Description | CRef | V | Comments |
| 1 |
| START T_F1 |
|  | 2 | L1 | L!Info_0 | I0 |
| 3 |
| ?TIMEOUT T_F1 |
|  | 4 |
| +F1_I4 |
|  | 5 |
| L?OTHERWISE |
|  | 6 |
| GOTO L1 |
| F1_I4 |
|  | 71 |
| START TNOAC |
|  | 82 | L21 | L!Info_n | I4_BASIC |
| 93 |
| ?TIMEOUT TNOAC |
| R |
|  | 104 |
| L ? Info_0 | I0 |
| 115 |
| GOTO L21 |

The following changes shall be performed in the amended Annex E of TBR 3:

Table E.3 of TBR 3/A1, Implemented values shall be modified as follows:

| Item | Reference | Description | Value |
| --- | --- | --- | --- |
| ... | ... | ... | ... |
| E.3.7 | 9.5.5.2.3 | State the time needed for the TE to restrict its power consumption after the switch-over from normal mode to restricted mode PS1 (applicable to designated terminals only). |
|  | E.3.8 | 9.4.2.3 | State the value of timer T_F1, which represents the time needed to reach F1 after switch off PS1 or LP (s). |

The following changes shall be performed in the layer 1 Abstract Test Suites of TBR 33:

The Test Suite Parameter Declarations shall be modified as follows:

| Test Suite Parameter Declarations |
| --- |
| Parameter Name | Type | PICS/PIXIT Ref | Comments |
| ... | ... | ... | ... |
| T3_4T200 | BOOLEAN | - | TRUE if T3 > 4xT200 |
| PX_T_F1 | INTEGER | E.3.8 | Duration to reach F1 after switch off PS1 or LP (s) |
| Detailed Comments: |

The Timer Declarations shall be modified as follows:

| Timer Declarations |
| --- |
| Timer Name | Duration | Unit | Comments |
| ... | ... | ... | ... |
| T4 | T4VMAX | ms | Value of T4 max plus 5%. |
| T_F1 | PX_T_F1 | s | Ensure that F1 has been reached |
| Detailed Comments: |

Postamble CHECK_F1 shall be modified as follows:

| Test Step Dynamic Behaviour |
| --- |
| Test Step Name: | CHECK_F1 |
| Group: | ISDN1_TS/MISCELLANEOUS/ |
| Objective: | To check that IUT is in state F1. |
| Default: | DEF_1 |
| Nr | Label | Behaviour Description | CRef | V | Comments |
| 1 |
| START T_F1 |
|  | 2 | L1 | L!Info_0 | I0 |
| 3 |
| ?TIMEOUT T_F1 |
|  | 4 |
| +F1_I4 |
|  | 5 |
| L?OTHERWISE |
|  | 6 |
| GOTO L1 |
| F1_I4 |
|  | 71 |
| START TNOAC |
|  | 82 | L21 | L!Info_n | I4_BASIC |
| 93 |
| ?TIMEOUT TNOAC |
| R |
|  | 104 |
| L ? Info_0 | I0 |
| 115 |
| GOTO L21 |
|  | Detailed Comments: |

The following changes shall be performed in Annex E of TBR 33:

Table E.3, Implemented values shall be modified as follows:

| Item | Reference | Description | Value |
| --- | --- | --- | --- |
| ... | ... | ... | ... |
| E.3.7 | 9.5.5.2.3 | State the time needed for the TE to restrict its power consumption after the switch-over from normal mode to restricted mode PS1 (applicable to designated terminals only). |
|  | E.3.8 | 9.4.2.3 | State the value of timer T_F1, which represents the time needed to reach F1 after switch off PS1 or LP (s). |