ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 091

Date:	1998-09-07

Subject:	Data Rates for testing

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 1 (Commission Decision 97/544/EC)

X	CTR 2 (Commission Decision 97/545/EC)

In consideration of the following:

-	That the scope of TBR 1 covers interfaces with signalling rates up to and including 1984 kbit/s and the scope of TBR 2 covers interfaces with signalling rates up to and including 1920 kbit/s;

-	That TBR 2 Clause 7.1.7 states  “Except where stated otherwise, tests shall be conducted at the highest signalling rate declared by the client for which approval is sought.";

-	That TBR 1 makes no stipulation of the signalling rate at which tests should be performed;

-	That many Public Telecommunications Networks offer X.21 and X.21bis interfaces operating in excess of 1984 and 1920 kbit/s;

-	That many TE for which approval is being sought to either CTR 1 or CTR 2 can additionally be configured to higher data rates than stipulated in the TBRs using the same circuits;

-	That many TE operate Control circuits at lower signalling rates than those used for the transmission and timing circuits in the same configuration;

-	That the essential requirements as expressed in TBRs 1 and 2 apply the same to data rates in excess of the specified limits as to those at or below the specified limits.

ITAAB advises the following:

That where a TE is being tested to TBR 1 then, except where clarified further in this note, the tests shall be conducted at the highest signaling rate declared by the client for which approval is sought.

That where a TE supports a number of circuits the highest signalling rate for which approval is sought shall be determined on a per circuit basis.

That where a TE supports signalling rates in excess of 1984 kbit/s for TBR 1 and 1920 kbit/s for TBR 2 then the supplier may nominate a data rate for testing above the specified limit, and results obtained testing at that higher rate may be used to support evaluation to the respective TBR.

That approval may be granted to CTR 1 or CTR 2 for TE which supports data rates in excess of the stipulated limits provided they are compliant to the respective standards when tested at the highest data rate intended for such connections.