ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 094

Date:	1998-09-07

Subject:	Timer TWAIT in the S0 Layer 1 Testsuite

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

X	CTR 33 (Commission Decision 98/521/EC)

For the purposes of the above described applicability, this note specifically contains amendments to:

TBR 3, Amendment A1, December 1997: Attachment requirements for terminal equipment to connect to an ISDN using ISDN basic access.

TBR 3, November 1995: Attachment requirements for terminal equipment to connect to an ISDN using ISDN basic access.

TBR 33, December 1997: Attachment requirements for packet mode terminal equipment to connect to an ISDN using ISDN basic access.

In consideration of the following :

-	Timer TWAIT is used by the tester for test synchronization with external procedure, i.e. the actions to be done by the test personal or automatical actions done by the IUT;

-	In the layer 1 TTCN test description of TBR 3/A1 and TBR 33 timer TWAIT has a constant value of 189s;

-	Such a long time increases the test time unnecessarily;

-	In the test suite of the tester K1403 the timer TWAIT is a PIXIT value.

ITAAB advises the following :

The following changes shall be performed in the layer 1 Abstract Test Suite of TBR 3/A1:

The Test Suite Parameter Declarations shall be modified as follows:

| Test Suite Parameter Declarations |
| --- |
| Parameter Name | Type | PICS/PIXIT Ref | Comments |
| ... | ... | ... | ... |
| T3_4T200 | BOOLEAN | - | TRUE if T3 > 4xT200 |
| PX_T_F1 | INTEGER | E.3.9 | Duration to reach F1 after switch off PS1 or LP (s) |
| PX_TWAIT | INTEGER | E.3.10 | Timer for user actions |

NOTE: The addition of PX_T_F1, as described in Advisory Note 088 rev. 1, has been included in this table.

The Timer Declarations shall be modified as follows:

| Timer Declarations |
| --- |
| Timer Name | Duration | Unit | Comments |
| T3_S | T3VMAX | ms | Activation request by TE, T3_S must exceed T3. |
| TWAIT | PX_TWAIT189 | s | Used by the tester for test synchronization with external procedure. |
| ... | ... | ... | ... |

The following changes shall be performed in the amended Annex E of TBR 3:

Table E.3 of TBR 3/A1, Implemented values shall be modified as follows:

| Item | Reference | Description | Value |
| --- | --- | --- | --- |
| ... | ... | ... | ... |
| E.3.7 | 9.5.5.2.3 | State the time needed for the TE to restrict its power consumption after the switch-over from normal mode to restricted mode PS1 (applicable to designated terminals only). |
|  | E.3.8 | 9.4.2.3 | State the value of timer T_F1, which represents the time needed to reach F1 after switch off PS1 or LP (s). |
|  | E.3.9 |
| State the value of timer TWAIT, which represents the time needed to perform an action on the IUT (s). |

NOTE: The addition of T_F1, as described in Advisory Note 088 rev. 1, has been included in this table.

The following changes shall be performed in the layer 1 Abstract Test Suite of TBR 33:

The Test Suite Parameter Declarations shall be modified as follows:

| Test Suite Parameter Declarations |
| --- |
| Parameter Name | Type | PICS/PIXIT Ref | Comments |
| ... | ... | ... | ... |
| T3_4T200 | BOOLEAN | - | TRUE if T3 > 4xT200 |
| PX_T_F1 | INTEGER | E.3.8 | Duration to reach F1 after switch off PS1 or LP (s) |
| PX_TWAIT | INTEGER | E.3.9 | Timer for user actions |
| Detailed Comments: |

NOTE: The addition of PX_T_F1, as described in Advisory Note 088 rev. 1, has been included in this table.

The Timer Declarations shall be modified as follows:

| Timer Declarations |
| --- |
| Timer Name | Duration | Unit | Comments |
| T3_S | T3VMAX | ms | Activation request by TE, T3_S must exceed T3. |
| TWAIT | PX_TWAIT189 | s | Used by the tester for test synchronization with external procedure. |
| ... | ... | ... | ... |

The following changes shall be performed in Annex E of TBR 33:

Table E.3, Implemented values shall be modified as follows:

| Item | Reference | Description | Value |
| --- | --- | --- | --- |
| ... | ... | ... | ... |
| E.3.7 | 9.5.5.2.3 | State the time needed for the TE to restrict its power consumption after the switch-over from normal mode to restricted mode PS1 (applicable to designated terminals only). |
|  | E.3.8 | 9.4.2.3 | State the value of timer T_F1, which represents the time needed to reach F1 after switch off PS1 or LP (s). |
|  | E.3.9 |
| State the value of timer TWAIT, which represents the time needed to perform an action on the IUT (s). |

NOTE: The addition of T_F1, as described in Advisory Note 088 rev. 1, has been included in this table.