ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 095

Date:	1998-08-18

Subject:	Test description for Receiver effective shunt capacitance 
for CCITT V.28 interchange circuits ( 7.5.2.1 )

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 2 (Commission Decision 95/545/EC)

In consideration of the following:

-	The test description for test 7.5.2.1 is unclear;

-	The abbreviation e.m.f can be misleading;

-	The Correct  interpretation is deemed to be 14 V peak to peak, based on the justification provided in Draft prTBR 2:1994, Annex D.1. This annex includes the following statement:

“ across the reference circuit VL is 10 volts (peak to peak) which is the limiting situation from CCITT Recommendation V.28.”

ITAAB advises the following:

Change the TBR 2 text on page 37 of TBR2 in the subclauses :

“Test configuration” and “Test stimulus and action“ into:

“The signal source is set to provide a binary 1:1 pattern at the rate of 9 600 bit/s with an output voltage of 14 Vpp, measured on open circuit, balanced in voltage about point C’.”