ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 097

Date:	1999-02-15

Subject:	Power Source 1 voltage to be supplied to a TE during testing

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 33 (Commission Decision 98/521/EC)

In consideration of the following:

-	TBR 33 references the layer 1 electrical characteristics tests of TBR 3, as amended by TBR 3/A1.

-	The PS1 voltage to be applied to TEs is not stated unambigously for all tests specified in TBR 3, as amended by TBR 3/A1.

-	A TE, which is not powered from PS1 may be equipped with a connection detector, that checks the connection to the S-bus by detecting the presence of the PS1 supply voltage. Such TEs will require presence of the PS1 supply voltage to perform tests requiring the TE to be active;

ITAAB advises the following:

When performing testing according to TBR 33 to verify compliance with TBR 33, the following additional information applies:

Test B.5.4.7 shall be performed with a PS1 voltage of +24 V;

Test B.5.5 shall be performed with a PS1 voltages of +42 V, +24 V, -42 V and -32 V;

A TE not powered from PS1 shall have PS1 applied at all time during testing. When no other specific voltage to be applied is specified for electrical characteristics layer 1 testing, a PS1 voltage of -32 V shall be applied. This also applies for the tests to be performed in layer 1 state F1 (i.e. in tests B.2.3.4, B.2.3.5, B.2.7, B.2.8.1.3, B.2.8.1.4 and B.2.8.3).