ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 103

Date:	1999-05-20

Subject:	Information element checking in TBR 33/34 layer 3 TC20002

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 33 (Commission Decision 98/521/EC)

X	CTR 34 (Commission Decision 98/518/EC)

In consideration of the following:

-	Layer 3 test case TC20002 checks that the bearer capability IE in the SETUP message sent by the IUT is as indicated in the PIXIT;

-	It is possible that an IUT may use a different bearer capability in its outgoing SETUP message from that which the IUT accepts in an incoming SETUP message for the purpose of compatibility checking of incoming calls;

-	The bearer capability parameters in the ATSs of TBR 33 and TBR 34 refer only to those which the IUT accepts in an incoming SETUP;

-	This could result in incorrect verdicts if the IUT includes a particular bearer capability IE in the SETUP messages it sends, but does not require it for compatibility checking (and hence no value is required in the parameter relating to incoming SETUPs), or if different values are declared for outgoing and incoming SETUPs.

ITAAB advises the following:

If possible, the IUT should be configured so that the compatible value of BCAP to be included in SETUP messages sent to the IUT, is the same as the value included in outgoing SETUP messages sent by the IUT.

The test suite parameter BCAPV should be set as described below:

if the value of the bearer capability for the outgoing SETUP message is the same as that required for compatibility checking then, the parameter should be set to that value;

or

-	if the value of the bearer capability for the outgoing SETUP message is different to that required for compatibility checking, then the value used for the outgoing SETUP message should be used for TC20002 and the value used for compatibility checking should be used for all other test cases.