ITAAB

TRAC ISDN Type Approval Advisory Board

Annex B

to

ITAAB Advisory Note Number: 104

Date:	2000-02-08

Subject:	List of tests and Test Case Selection Criteria for Packet Mode ISDN Layer 3 Basic Access

TEST CASE SELECTION CRITERIA

The set of tests required to verify compliance with the layer 3 requirements of CTR 33 for Basic Access are described in clause 2.

The set of tests relevant for a specific implementation depends on certain capabilities of the TE. The information on implementation of these capabilities has to be provided by the manufacturer.

Corresponding to the declaration made by the manufacturer concerning each of these capabilities, a corresponding conditioning parameter is given the value TRUE or FALSE. The conditioning parameters are used in Boolean expressions to define the conditions for relevance of each test.

The abbreviations used for the Boolean expressions and the value associated with the implemented capabilities appear from the following table:

| Abbreviation | Corresponding conditioning parameter |
| --- | --- |
| INCOMING_CALL | TRUE, if the IUT is able to operate with ISDN incoming calls |
| OUTGOING_CALL | TRUE, if the IUT is able to operate with ISDN outgoing calls |
| PH_ACCESS_D_CHANNEL | TRUE, if the IUT is able to operate PH access over the D-channel |
| PH_ACCESS_D_CHN_ONLY | TRUE, if the IUT is able to operate PH access over the D-channel only |
| INCOMING_VIRTUAL_CALL | TRUE, if the IUT is able to handle incoming virtual calls |
| OUTGOING_VIRTUAL_CALL | TRUE, if the IUT is able to handle outgoing virtual calls |
| TE_ACTIVATED_SAPI16 | TRUE, if the IUT is capable of TE demand data link activation (SAPI 16) |
| NT_ACTIVATED_SAPI16 | TRUE, if the IUT is capable of NT demand data link activation (SAPI 16) |
| BDL | FALSE, if the IUT supports a configuration using only a single point-to-point data link |
| IBCC | TRUE if the TE performs checking of the Bearer capability IE in an incoming SETUP PDU |
| SETUP_PROVOCABLE | TRUE, if the IUT can be provoked to send a SETUP message |
| CONNECT_PROVOCABLE | TRUE, if the IUT can be provoked to send a CONNECT message |
| DISCONNECT_PROVOCABLE | TRUE, if the IUT can be provoked to send a DISCONNECT message |
| SAPI0_PROVOCABLE | TRUE, if the IUT can be provoked to set up a data link connection on SAPI 0 |
| SAPI16_PROVOCABLE | TRUE, if the IUT can be provoked to set up a data link connection on SAPI 16 |
| ACCEPT_ON_B_CHANNEL | TRUE, if the IUT can be set to accept incoming virtual calls on the B-channel |
| U7_MAINT | TRUE, if U7 > 3s and U7 ability = YES, FALSE, if U7 < 3s or U7 ability = NO |
| U9_MAINT | TRUE, if U9 > 3s and U9 ability = YES, FALSE, if U9 < 3s or U9 ability = NO |
| KEEP_B_CHANNEL | TRUE, if the IUT is able to keep a B-channel connection set up, if no virtual call is active |
| BCP | TRUE, if the TE is capable of sending the CALL PROCEEDING PDU |
| BAL | TRUE, if the TE is capable of sending the ALERT PDU |

TEST CASE SELECTION

The tables in the following subclauses describe the set of relevant tests required to verify compliance with the layer 3 requirements of CTR 33 for Basic Access.

Column 1, Requirement from TBR 33, references the requirements in TBR 33.

Column 2, Description, provides a brief description of the test case.

Column 3, Test case identifier, provides the reference to the relevant TTCN test case in TBR 33.

Column 4, Condition, provides the test selection criteria. The condition is described as a Boolean expression of the conditioning parameters. When the Boolean expression evaluates to TRUE, the test is relevant. When the condition is blank, the test is always relevant.

INCOMING CALL HANDLING TESTS STATE U00

Requirement from TBR 33

| Description | Test case identifier | Condition |
| --- | --- | --- |
| 11.4.6.1 | Ensure that on receipt of a REL PDU, the IUT responds with REL_COM PDU and remains in the same state. | TC10002 |
|  | 11.4.6.7 | Ensure that on receipt of a STATUS PDU indicating any state except the null state, the IUT responds with either a REL or REL_COM PDU with the cause #101. | TC10004 |

11.4.2.1

| 11.4.2.5 | Ensure that on receipt of a valid SETUP without the sending complete IE the IUT responds with either SETUP_ACK, CALL_PROC, ALERT or CONN PDU and moves to the relevant state 25, 9, 7 or 8. | TC10005 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL |
| --- | --- | --- | --- |
| 11.4.2.2 |

Ensure that on receipt of a valid SETUP PDU containing an incompatible Bearer Capability IE (mandatory parameter) the IUT:

-responds by sending a REL_COM PDU or ignore the SETUP PDU /PTMP

| -responds by sending a REL_COM PDU /PTP | TC10008 | IBCC AND INCOMING_CALL AND INCOMING_VIRTUAL_CALL |
| --- | --- | --- |
| 11.4.6.1 | Ensure that the IUT responds to an inopportune PDU (DISC) with a REL PDU or REL_COM PDU. | TC10010 |
|  | 11.4.6.1 | Ensure that on receipt of a repeated valid SETUP with the same call reference as the initial SETUP, the IUT ignores the second SETUP and remains in the same state. | TC10011 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL |
| 11.4.6.4.1 | Ensure that on receipt of a SETUP without a mandatory IE the IUT responds with a REL_COM PDU and remains in the same state. | TC10015 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL |
| 11.4.6.3 | Ensure that on receipt of a PDU with invalid duplicated IE, the IUT ignores the invalid duplication and processes the remaining contents of the PDU as valid. | TC10024 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL |
| 11.4.6.5.1 | Ensure that the IUT responds to the receipt of a SETUP PDU with unrecognised optional IE coded "comprehension required" by sending a REL_COM PDU and remains in the same state. | TC10027 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL |
| 11.4.6.5.1 | Ensure that the IUT on receipt of a compa-tible SETUP PDU with all the mandatory information correctly coded and an unre-cognised optional IE with comprehension not required responds with a STATUS PDU (optional) followed by either a SETUP_ACK, CALL_PROC, ALERT or CONN PDU and moves to the relevant state 25, 9, 7 or 8. | TC10028 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL |
| 11.4.6.5.2 | Ensure that the IUT on receipt of a SETUP PDU with non mandatory IE content error the IUT processes the PDU and its remaining contents as valid and optionally sense a STATUS PDU with cause value 100. | TC10029 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL |

Requirement from TBR 33

| Description | Test case identifier | Condition |
| --- | --- | --- |
| 11.4.6.5.2 | Ensure that on receipt of a SETUP PDU with non-mandatory information element exceeding the maximum length the IUT processes the PDU and its remaining contents as valid and optionally sends a STATUS PDU with cause value 100. | TC100x1 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL |
| 11.4.2.3 | Ensure that on receipt of a SETUP PDU indicating in the Channel Identification information element an idle B-channel, “exclusive: only the indicated channel is acceptable” with the D-channel indicator set to “the channel is not the D-channel”, the IUT accepts the virtual call on a channel that is compatible to the channel(s) offered by the network. | TC100x2 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL AND NOT PH_ACCESS_D_CHN_ONLY |
| 11.4.2.3 | Ensure that on receipt of a SETUP PDU indicating in the Channel Identification information element an idle B-channel, “exclusive: only the indicated channel is acceptable” with the D-channel indicator set to “the channel is the D-channel”, the IUT accepts the virtual call on a channel that is compatible to the channel(s) offered by the network. | TC100x3 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL |
| 11.4.2.3 | Ensure that on receipt of a SETUP PDU indicating in the Channel Identification information element an idle B-channel, “indicated channel is preferred” with the D-channel indicator set to “the channel is not the D-channel”, the IUT accepts the virtual call on a channel that is compatible to the channel(s) offered by the network. | TC100x4 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL AND NOT PH_ACCESS_D_CHN_ONLY |
| 11.4.2.3 | Ensure that on receipt of a SETUP PDU indicating in the Channel Identification information element an idle B-channel, “indicated channel is preferred” with the D-channel indicator set to “the channel is the D-channel”, the IUT accepts the virtual call on a channel that is compatible to the channel(s) offered by the network. | TC100x5 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL |
| 11.4.2.3 | Ensure that on receipt of a SETUP PDU indicating in the Channel Identification information element no B-channel, “the indicated channel is preferred” with the D-channel indicator set to “the channel is not the D-channel”, the IUT accepts the virtual call on a channel that is compatible to the channel(s) offered by the network. | TC100x6 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL AND NOT PH_ACCESS_D_CHN_ONLY AND KEEP_B_CHANNEL |
| 11.4.2.3 | Ensure that on receipt of a SETUP PDU indicating in the Channel Identification information element no B-channel, “the indicated channel is preferred” with the D-channel indicator set to “the channel is the D-channel”, the IUT accepts the virtual call on a channel that is compatible to the channel(s) offered by the network. | TC100x7 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL AND PH_ACCESS_D_CHANNEL |
| 11.4.2.3 | Ensure that on receipt of a SETUP PDU indicating in the Channel Identification information element no B-channel, “the indicated channel is preferred” with the D-channel indicator set to “the channel is the D-channel”, when a B-channel connection is already established, the IUT accepts the virtual call on a channel that is compatible to the channel(s) offered by the network. | TC100x8 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL AND NOT PH_ACCESS_D_CHN_ONLY AND KEEP_B_CHANNEL |

Requirement from TBR 33

| Description | Test case identifier | Condition |
| --- | --- | --- |
| 11.4.2.3 | Ensure that on receipt of a SETUP PDU indicating in the Channel Identification information element no B-channel, “exclusive: only the indicated channel is acceptable” with the D-channel indicator set to “the channel is the D-channel”, the IUT accepts the virtual call on a channel that is compatible to the channel(s) offered by the network. | TC100x9 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL AND PH_ACCESS_D_CHANNEL |
| 11.4.1.1 | Ensure that the IUT transmits a valid SETUP and enters the Call Initiated state U1. | TC20002 | OUTGOING_CALL AND OUTGOING_VIRTUAL_CALL AND SETUP_PROVOCABLE |

CALL INITIATED STATE TESTS, STATE 1

Requirement from TBR 33

| Description | Test case identifier | Condition |
| --- | --- | --- |
| 11.4.1.3 | Ensure that on receipt of a CALL_PROC PDU the IUT enters the state U3. | TC10101 | OUTGOING_CALL AND OUTGOING_VIRTUAL_CALL AND SETUP_PROVOCABLE |
| 11.4.6.2 | Ensure that on receipt of a REL_COM PDU the IUT does not respond but returns to the state U0. | TC10102 | OUTGOING_CALL AND OUTGOING_VIRTUAL_CALL AND SETUP_PROVOCABLE |
| 11.4.6.2 | Ensure that on receipt of a REL PDU the IUT responds with a REL_COM PDU and enters the state U0. | TC10103 | OUTGOING_CALL AND OUTGOING_VIRTUAL_CALL AND SETUP_PROVOCABLE |
| 11.4.6.7 | Ensure that on receipt of a STATUS PDU specifying the state U0, the IUT enters the state U0. | TC10105 | OUTGOING_CALL AND OUTGOING_VIRTUAL_CALL AND SETUP_PROVOCABLE |
| 11.4.6.2 | Ensure that the IUT responds to an inopportune PDU with a STATUS PDU with cause value 98 or 101, or ST_ENQ PDU and remains in the same state. | TC10107 | OUTGOING_CALL AND OUTGOING_VIRTUAL_CALL AND SETUP_PROVOCABLE |
| 11.4.6.2 | Ensure that the IUT responds to a syntactically invalid message type with a STATUS PDU with cause value 98 or 101, or ST_ENQ PDU and remains in the same state. | TC10120 | OUTGOING_CALL AND OUTGOING_VIRTUAL_CALL AND SETUP_PROVOCABLE |
| 11.4.6.1 | Ensure that on receipt of a REL_COM PDU the IUT does not respond and remains in the same state. | TC10125 | OUTGOING_CALL AND OUTGOING_VIRTUAL_CALL AND SETUP_PROVOCABLE |

OUTGOING CALL PROCEEDING STATE TESTS, STATE 3

Requirement from TBR 33

| Description | Test case identifier | Condition |
| --- | --- | --- |
| 11.4.1.5 | Ensure that on receipt of a CONN PDU the IUT enters the state U10. | TC10302 | OUTGOING_CALL AND OUTGOING_VIRTUAL_CALL AND SETUP_PROVOCABLE |
| 11.4.3.4.2 | Ensure that the IUT responds to a DISC PDU with a REL PDU and enters the Release Request state U19. | TC10303 | OUTGOING_CALL AND OUTGOING_VIRTUAL_CALL AND SETUP_PROVOCABLE |
| 11.4.3.3 | Ensure that the IUT transmits a DISC PDU and enters the Disconnect Request state. | TC20301 | (OUTGOING_CALL AND OUTGOING_VIRTUAL_CALL AND SETUP_PROVOCABLE) AND DISCONNECT_PROVOCABLE |

CALL RECEIVED STATE TESTS, STATE 7

Requirement from TBR 33

| Description | Test case identifier | Condition |
| --- | --- | --- |
| 11.4.3.4.2 | Ensure that the IUT responds to a DISC PDU with a REL PDU and enters the Release Request state U19. | TC10701 | BAL AND U7_MAINT |

CONNECT REQUEST STATE TESTS, STATE 8

Requirement from TBR 33

| Description | Test case identifier | Condition |
| --- | --- | --- |
| 11.4.2.7 | Ensure that the IUT will enter the state U10 on receipt of a CONN_ACK PDU. | TC10801 | (INCOMING CALL AND NOT PH_ACCESS_D_CHN_ONLY AND ACCEPT_ON_B_CHANNEL) AND CONNECT_PROVOCABLE |
| 11.4.3.4.2 | Ensure that the IUT responds to a DISC PDU with a REL PDU and enters the Release Request state U19. | TC10802 | (INCOMING CALL AND NOT PH_ACCESS_D_CHN_ONLY AND ACCEPT_ON_B_CHANNEL) AND CONNECT_PROVOCABLE |
| 11.4.2.8 | Ensure that on receipt of a REL PDU the IUT responds with a REL_COM PDU and enters the state U0. | TC10805 | (INCOMING CALL AND NOT PH_ACCESS_D_CHN_ONLY AND ACCEPT_ON_B_CHANNEL AND BDL) AND CONNECT_PROVOCABLE |
| 11.4.3.4.2 | Ensure that on receipt of a RELEASE PDU with cause value #7 “call awarded and being delivered in an established channel”, the IUT which has requested that the virtual call is set up in the D-channel responds with a RELEASE COMPLETE PDU, enters the null state U0 and accepts the incoming virtual call. | TC108x1 | (INCOMING_CALL AND INCOMING_VIRTUAL_CALL AND PH_ACCESS_D_CHANNEL AND (NT_ACTIVATED_SAPI16 OR (TE_ACTIVATED_SAPI16 AND SAPI16_PROVOCABLE))) AND CONNECT_PROVOCABLE |
| 11.4.3.4.2 | Ensure that on receipt of a RELEASE PDU with cause value #7 “call awarded and being delivered in an established channel”, the IUT which has requested that the virtual call is set up in an already established B-channel responds with a RELEASE COMPLETE PDU, enters the null state U0 and accepts the incoming virtual call. | TC108x2 | (INCOMING_CALL AND INCOMING_VIRTUAL_CALL AND NOT PH_ACCESS_D_CHN_ONLY AND KEEP_B_CHANNEL) AND CONNECT_PROVOCABLE |

INCOMING CALL PROCEEDING STATE TESTS, STATE 9

Requirement from TBR 33

| Description | Test case identifier | Condition |
| --- | --- | --- |
| 11.4.3.4.2 | Ensure that the IUT responds to a DISC PDU with a REL PDU and enters the Release Request state U19. | TC10901 | BCP AND U9_MAINT |

ACTIVE STATE TESTS, STATE 10

Requirement from TBR 33

| Description | Test case identifier | Condition |
| --- | --- | --- |
| 11.4.6.2 | Ensure that on receipt of a REL_COM PDU the IUT does not respond but returns to the null state. | TC11004 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL AND NOT PH_ACCESS_D_CHN_ONLY AND KEEP_B_CHANNEL |
| 11.4.6.2 | Ensure that on receipt of a REL PDU the IUT responds with a REL_COM PDU and enters the state U0. | TC11005 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL AND NOT PH_ACCESS_D_CHN_ONLY AND KEEP_B_CHANNEL |
| 11.4.6.7 | Ensure that on receipt of a STATUS PDU specifying the state U0, the IUT enters the state U0. | TC11007 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL AND NOT PH_ACCESS_D_CHN_ONLY AND KEEP_B_CHANNEL |
| 11.4.6.2 | Ensure that the IUT responds to an inopportune CONN PDU with a STATUS PDU with the cause 98 or 100 or with a ST_ENQ and remains in the same state. | TC11008 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL AND NOT PH_ACCESS_D_CHN_ONLY AND KEEP_B_CHANNEL |
| 11.4.6.2 | Ensure that the IUT responds to a syntactically invalid message type with a STATUS PDU with the cause 98 or 97 and that no change of state occurs. | TC11021 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL AND NOT PH_ACCESS_D_CHN_ONLY AND KEEP_B_CHANNEL |
| 11.5 | Ensure timer T308 is within the range 3 s to 15 s. | TC21001 | INCOMING_CALL AND INCOMING_VIRTUAL_CALL AND NOT PH_ACCESS_D_CHN_ONLY AND KEEP_B_CHANNEL |
| 11.4.3.3 | Ensure that the IUT transmits a DISC PDU and enters the Disconnect Request state U11. | TC21003 | (INCOMING_CALL AND INCOMING_VIRTUAL_CALL AND NOT PH_ACCESS_D_CHN_ONLY AND KEEP_B_CHANNEL) AND DISCONNECT_PROVOCABLE |
| 11.5 | Ensure timer T305 is within the range 15 s to 45 s. | TC21006 | (INCOMING_CALL AND INCOMING_VIRTUAL_CALL AND NOT PH_ACCESS_D_CHN_ONLY AND KEEP_B_CHANNEL) AND DISCONNECT_PROVOCABLE |

DISCONNECT REQUEST STATE TESTS, STATE 11

Requirement from TBR 33

| Description | Test case identifier | Condition |
| --- | --- | --- |
| 11.4.3.5 | Ensure that the IUT responds to a DISC PDU with a REL PDU and enters the Release Request state U19. | TC11101 | DISCONNECT_PROVOCABLE |
| 11.4.3.3 | Ensure that on receipt of a REL PDU the IUT responds with a REL_COM PDU and enters the state U0. | TC11105 | DISCONNECT_PROVOCABLE |
| 11.4.6.6 | Ensure that the IUT responds to an inopportune PDU with a STATUS PDU with the cause 98 or 101 or with a ST_ENQ PDU and remains in the same state . | TC11107 | DISCONNECT_PROVOCABLE |
| 11.4.6.5.1 | Ensure that on receipt of a REL PDU with unrecognised IE (coded comprehen-sion not required) THE IUT sends a REL_COM PDU and enters the state U0. | TC11118 | DISCONNECT_PROVOCABLE |

RELEASE REQUEST STATE TESTS, STATE 19

Requirement from TBR 33

| Description | Test case identifier | Condition |
| --- | --- | --- |

11.4.3.4.3

|  | Ensure that on receipt of a REL_COM PDU the IUT does not respond but returns to the state U0. | TC11903 |
| --- | --- | --- |

11.4.3.5

|  | Ensure that on receipt of a REL PDU the IUT does not respond and enters the state U0. This is a test of RELEASE collision handling. | TC11904 |
| --- | --- | --- |
|  | 11.4.6.7 | Ensure that on receipt of a STATUS PDU specifying the state U0, the IUT enters the state U0. | TC11906 |

11.4.6.2

| 11.4.6.3 | Ensure that the IUT responds to an inopportune PDU with a STATUS PDU with the cause 98 or 101 or with a ST_ENQ and remains in the same state. | TC11908 |
| --- | --- | --- |

11.4.6.2

| 11.4.6.3 | Ensure that the IUT responds to a syntactically invalid message type with a STATUS PDU with the cause 98 or 97 or with a ST_ENQ and remains in the same state. | TC11909 |
| --- | --- | --- |

RESTART NULL STATE TESTS, REST 0

Requirement from TBR 33

| Description | Test case identifier | Condition |
| --- | --- | --- |
| 11.4.8 | Ensures that on receipt of a RESTART message the specified channel is returned to the Idle condition, the Call Reference is returned to the Null state and a RESTART_ACK is sent. | TC19003 | NOT BDL |