ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 106

Date:	1999-05-20

Subject:	Correction of editorial error in TBR 33 layer 3 TC11101

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 33 (Commission Decision 98/521/EC)

For the purposes of the above described applicability, this note specifically contains amendments to:

TBR 33, December 1997: Attachment requirements for packet mode terminal equipment to connect to an ISDN using ISDN basic access.

In consideration of the following:

-	An editorial error has been discovered in test case TC11101 of the TBR 33 Layer 3 abstract test suite attached in electronic form to TBR 33, December 1997. With reference to the Test Case Dynamic Behaviour for TC11101, for the case where the IUT is the originator of the call (INCOMING_CALL set to FALSE), line 13 of the TTCN expects a RELEASE PDU from the IUT with the call reference flag CR_F set to 1. This would indicate that the IUT is not the originator of the call and is incorrect.

ITAAB advises the following:

Line 13 of the TTCN description of TC11101 shall be amended such that, for the case where the IUT is the originator of the call (INCOMING_CALL set to FALSE), the expected RELEASE PDU from the IUT shall have the call reference flag CR_F set to 0.

The corresponding amendment to the TTCN description of TC11101 is:

| Test Case Dynamic Behaviour |
| --- |
| Test Case Name | : | TC11101 |
| Group | : | TBR33L3/U11/PS/ |
| Purpose | : |

DISCONNECT REQUEST STATE TESTS – STATE U11 – PASSIVE IUT BEHAVIOUR VALID TEST EVENTS

| Ensure that on receipt of a DISCONNECT PDU the IUT responds with a RELEASE PDU and enters the Release Request state U19 |
| --- |
| Configuration | : |
|  | Default | : | DF69901 (FLAG) |
| Comments | : |
|  | Nr | Label | Behaviour Description | Constraints Ref | Verdict | Comments |
|  | (1) |
| 1 |
| [INCOMING_CALL] |
|  | 2 |
| (FLAG:=’0’B) |
|  | 3 |
| +PR31101 |
|  | preamble to state U11 |
| 4 |
| L!DISCs START TAC | Ms (DI2(cr)) |
| (2) |
| 5 |

L?RELEASEr[B_PDU.CR.CR_F=

| ’1’B] CANCEL TAC | Mr (RL1(cr)) | (P) | (3) |
| --- | --- | --- | --- |
| 6 |
| +CS59901(19, ‘0’B) |
|  | (4) |
| 7 |
| ?TIMEOUT TAC |
| (F) | no response |
| 8 |
| +PO49901(‘0’B) |
|  | postamble to state U0 |
|  | 9 |
| [NOT INCOMING_CALL] |
|  | (1) |
| 10 |
| (FLAG:=’1’B) |
|  | 11 |
| +PR31101 |
|  | preamble to state U11 |
| 12 |
| L!DISCs START TAC | Ms (DI2a(cr)) |
| (2) |
| 13 |

L?RELEASEr[B_PDU.CR.CR_F=

| ’ 10’B] CANCEL TAC | Mr (RL1(cr)) | (P) | (3) |
| --- | --- | --- | --- |
| 14 |
| +CS59901(19, ‘1’B) |
|  | (4) |
| 15 |
| ?TIMEOUT TAC |
| (F) | no response |
| 16 |
| +PO49901(‘1’B) |
|  | postamble to state U0 |
| Detailed comments | : |

The distinction, if state U11 is tested for an incoming call or an outgoing call is done with the test suite parameter INCOMING_CALL

Valid DISCONNECT PDU

Valid RELEASE PDU

The subtree CS59901 is used to check the IUT state U19

Reference to requirements : subclause 11.4.3.5