ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 111

Date:	1999-05-20

Subject:	Alternative means of connection for attachment to V-series interfaces

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 1 (Commission Decision 97/544/EC)

X	CTR 2 (Commission Decision 97/545/EC)

In consideration of the following:

-	TBR 1 and TBR 2 requires specific types of connectors to be used, depending on actual electrical interface implemented;

-	It is sometimes more practical to use a different type of connector;

-	The user may anyway use an additional cable to connect the TE to the DCE;

-	prEN 301 401, which is to replace TBR 1 and TBR 2, allows the TE to be equipped with alternative means of connection.

ITAAB advises the following:

A TE to be approved according to CTR 1 or CTR 2 may be equipped with alternative means of connection than the possibilities specified in TBR 1 or TBR 2.

A manufacturer employing such an alternative means of connection shall declare details of this arrangement, including details of circuit allocation.

This declaration shall be in a format similar to the Requirements Tables contained in Annex A of TBR 1, TBR 2 or prEN 301 401.