ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 114

Date:	1999-05-21

Subject:	Clarification of the term “Mains Powered“, used in the TBR-RT’s for selection of Protection tests

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

X	CTR 4 Amendment 1 (Commission Decision 98/520/EC)

X	CTR 12 Amendment 1 (Commission Decision 97/520/EC)

X	CTR 13 (Commission Decision 97/521/EC)

X	CTR 14 Amendment 1 (Commission Decision 97/522/EC)

X	CTR 33 (Commission Decision 98/521/EC)

X	CTR 34 (Commission Decision 98/518/EC)

In consideration of the following:

-	Clause 5.7.1 of ETS 300 046-3 and ETS 300 047-3 shall be used for testing for protection testing of "Mains Powered" equipment;

-	Interface cards to be installed in rack or PC's can be certified as a single units independently from the rack or PC they are designed to operate in conjunction with;

-	It is not clear if this kind of interface cards without directly mains power connection shall be subject to protection testing;

-	The TBRs do not contain a definition of the concept "Mains Powered";

-	A definition is needed to ensure a common understanding of the concept "Mains Powered" for types of interface cards which operate at low DC voltage.

ITAAB advise the following:

A TE which is integrated with a nominal 230 VAC power unit, is defined as a "Mains Powered" equipment, and the TE shall therefore be subject to protection testing.

A TE which is powered by batteries, power from the telecommunication lines or other external power supplies, including PC/racks, is not defined as a "Mains Powered" equipment, and the TE shall therefore not be subject to protection testing.