ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 118

Date:	1999-09-25

Subject:	Error in TBR 3 test cases TIF4info2 and TIF4 info4

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

X	CTR 33 (Commission Decision 98/521/EC)

For the purposes of the above described applicability, this note specifically contains amendments to:

TBR 3, Amendment A1, December 1997: Attachment requirements for terminal equipment to connect to an ISDN using ISDN basic access.

In consideration of the following:

-	TBR 3 clause 9.4.2.4 specifies that a TE in state F4 upon receipt of INFO 2 or INFO 4 shall cease transmission of INFO 1 and initiate transmission of INFO 0 within 5 ms and then respond to INFO 2 or INFO 4 within 100 ms;

-	TBR 33 clause 9.4.2.2 references TBR 3 clause 9.4.2.4;

-	This behaviour shall be checked with test cases TIF4info2 and TIF4 info4;

-	For a TE implementing state F5, there is however an error, because the tests checks that INFO 3 is not sent before 5 ms for such TEs.

ITAAB advises the following:

A TE implementing state F5 is allowed to send INFO 3 before 5 ms have elapsed after receipt of INFO 2 or INFO 4 in state F4.

The following changes shall be performed in test case TIF4info2 of TBR 3/A1 and TBR 33:

| Test Case Dynamic Behaviour |
| --- |
| Test Case Name: | TIF4info2 |
| Group: | ISDN1/TI/F4/ |
| Purpose: | To check the value of the TE activation times in the waiting for signal state. |
| Default: | DEF_1 |
| Comments: |
|  | Nr | Label | Behaviour Description | CRef | V | Comments |
| 1 |
| +PRE_F4 |
|  | 2 |
| START TIMER_1 |
|  | (1) |
| 3 | L1 | L!Info_n | I2 |
| 4 |
| ?TIMEOUT TIMER_1 |
| F |
|  | 5 |
| L?Info_1 | I1 |
| 6 |
| READTIMER TIMER_1(CHRONO) |
|  | 7 |
| [CHRONO <= (TB + TFRAME)] |
|  | 8 |
| GOTO L1 |
|  | 9 |
| [CHRONO >(TB + TFRAME)] |
|  | 10 |
| CANCEL TIMER_1 |
| F | (2) |
| 11 |
| L?Info_0 | I0 |
| 12 |
| GOTO L1 |
|  | 13 |
| L?Info_3 | I3_SFL |
| 14 |
| GOTO L1 |
|  | 15 |
| L?Info_3 CANCEL TIMER_1 | I3_BASIC |
| 16 |
| READTIMER TIMER_1(CHRONO) |
|  | 17 |
| [CHRONO <= (TB + TFRAME)] |
| P |
|  | 18 |
| [PC_STATE_F5] |
| F |
|  | 19 |
| [NOT PC_STATE_F5] |
| P |
|  | 1820 |
| [CHRONO >(TB + TFRAME)] |
|  | 1921 |
| [PC_STATE_F5] |
| P |
|  | 202 |
| [NOT PC_STATE_F5] |
| F |
|  | Detailed Comments: |

(1) Timer duration is 100.250ms.

(2) Maximal duration is 5.250ms.

References to Requirements:

Subclause 9.4.2.4.

The following changes shall be performed in test case TIF4info4 of TBR 3/A1 and TBR 33:

| Test Case Dynamic Behaviour |
| --- |
| Test Case Name: | TIF4info4 |
| Group: | ISDN1/TI/F4/ |
| Purpose: | To check the value of the TE activation times in the waiting for signal state. |
| Default: | DEF_1 |
| Comments: |
|  | Nr | Label | Behaviour Description | CRef | V | Comments |
| 1 |
| +PRE_F4 |
|  | 2 |
| START TIMER_1 |
|  | (1) |
| 3 | L1 | L!Info_n | I4_BASIC |
| 4 |
| ?TIMEOUT TIMER_1 |
| F |
|  | 5 |
| L?Info_1 | I1 |
| 6 |
| READTIMER TIMER_1(CHRONO) |
|  | 7 |
| [CHRONO <= (TB + TFRAME)] |
|  | 8 |
| GOTO L1 |
|  | 9 |
| [CHRONO >(TB + TFRAME)] |
|  | 10 |
| CANCEL TIMER_1 |
| F | (2) |
| 11 |
| L?Info_0 | I0 |
| 12 |
| GOTO L1 |
|  | 13 |
| L?Info_3 | I3_SFL |
| 14 |
| GOTO L1 |
|  | 15 |
| L?Info_3 CANCEL TIMER_1 | I3_BASIC |
| 16 |
| READTIMER TIMER_1(CHRONO) |
|  | 17 |
| [CHRONO <= (TB + TFRAME)] |
| P |
|  | 18 |
| [PC_STATE_F5] |
| F |
|  | 19 |
| [NOT PC_STATE_F5] |
| P |
|  | 1820 |
| [CHRONO >(TB + TFRAME)] |
|  | 1921 |
| [PC_STATE_F5] |
| P |
|  | 202 |
| [NOT PC_STATE_F5] |
| F |
|  | Detailed Comments: |

(1) Timer duration is 100.250ms.

(2) Maximal duration is 5.250ms.

References to Requirements:

Subclause 9.4.2.4.