ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number:  119 rev. 1

Date:	2000-01-17

Subject:	Overvoltage Protection

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

X	CTR 4 Amendment 1(Commission Decision 98/520/EC)

X	CTR 12 Amendment 1(Commission Decision 97/520/EC)

X	CTR 13 (Commission Decision 97/521/EC)

X	CTR 14 Amendment 1(Commission Decision 97/522/EC)

X	CTR 33 (Commission Decision 98/521/EC)

X	CTR 34 (Commission Decision 98/518/EC)

Annexes to this Advisory Note:

A:	Overvoltage Protection Tests from ETS 300 046-3

B:	Overvoltage Protection Tests from ETS 300 047-3

In consideration of the following:

-	TBR 3 clause 8, and TBR 33 Clause 8 specify overvoltage protection requirements based upon ETS 300 047-3;

-	TBR 4 clause 8, TBR 12 Clause 5.4, TBR 13 Clause 4.4, TBR 14 Clause 5.4, and TBR 34 Clause 8 specify overvoltage protection requirements based upon ETS 300 046-3;

-	ETS 300 046 and ETS 300 047 are scheduled to be obsoleted by ETSI on the basis they are covered by other LVD or EMC standards;

-	Testing to the overvoltage protection requirements can readily be conducted in conjunction with safety testing;

-	TBR 1: October 1995, Clause 5.1.8.1 permitted declarations of conformity with supporting information to be sent to the Test laboratory for assessment, as an alternative to testing.

ITAAB advises the following:

Compliance to TBR 4 clause 8, TBR 12 Clause 5.4, TBR 13 Clause 4.4, TBR 14 Clause 5.4, or TBR 34 Clause 8, may be established either:

by the tests invoked in Annex A of this Advisory Note or

b) 	by agreement between the client and the test laboratory or notified body, the submission by the client to that test laboratory or notified body of a declaration of conformance, including circuit diagrams, component specifications and other relevant information. That test laboratory or notified body shall, on the basis of the evidence accompanying the declaration, be responsible for satisfying itself that the declaration gives assurance of conformity not less than that achieved by method a) above.

Compliance to TBR 3 clause 8, or TBR 33 Clause 8, may be established either:

a)	by the tests invoked in Annex B of this Advisory Note; or

b) 	by agreement between the client and the test laboratory or notified body, the submission by the client to that test laboratory or notified body of a declaration of conformance, including circuit diagrams, component specifications and other relevant information. That test laboratory or notified body shall, on the basis of the evidence accompanying the declaration, be responsible for satisfying itself that the declaration gives assurance of conformity not less than that achieved by method a) above.