ITAAB

TRAC ISDN Type Approval Advisory Board

Annex B

to

ITAAB Advisory Note Number: 119 rev. 1

Date:	2000-01-17

Subject:	Overvoltage Protection Tests from ETS 300 047-3

Introduction.

These tests are extracted from ETS 300 047-3 with additional data from ETS 300 047-4.  The correction from ITAAB Advisory Note 115 is also applied.

The figure and clause numbering is retained from the original standards.

Declarations

Extract from ETS 300 047-4 Clause 5.3

Note:	An NT2 is often a complex installation with numerous and varied interfaces. Each interface can carry a touch current of up to 0.25 mA. With multiple interfaces, touch currents can sum up at a common point, such as a common power source or a common connection point for several interface cable shields. The following methods have been identified for avoiding an excessive touch current at any one interface:

separating all interfaces from each other so that no summing of touch current can occur;

bonding of common power or shield connection points to earth.

For test purposes, the manufacturer shall declare which of the following  methods shall be used to limit touch current:

separation of interface Ib from all auxiliary interfaces;

bonding of common power or shield connection points to an earth potential reference.

Tests

5.7.1	Impulse transfer from mains to interface Ia

Except where "bonding" is declared by the manufacturer for equipment with auxiliary interfaces (see subclause 5.3 of ETS 300 047-4), the test shall be carried out with no connection to connection point 1.

Test circuit:	figures 7 and 8.

Test voltage Uc:	2,5 kV.

Pulse form:	10/700 µs.

Number of applications:	two; one for each polarity.

Compliance criteria:	at the terminating network, figure D.1.

the voltage between:

-	E and G shall not exceed 1 kV peak;

-	F and G shall not exceed 1 kV peak;

-	E and F shall not exceed 250 V peak.

For the tests in transverse mode, the tests shall be repeated with "x" and "y" interchanged.

1)	User-accessible part or metal foil.

Figure 7: Test circuit for impulse transfer from mains; common mode

1)	User-accessible part or metal foil.

2)	See Clause 5 of ETS 300 047-1 [3].

Figure 8: Test circuit for impulse transfer from mains; transverse mode

5.7.3	Conversion of common mode to transverse mode

Test circuit:	figure 1.

Test voltage:	1 kV peak.

Pulse form:	1, 2/50 µs.

Number of pulses:	two; one for each polarity.

Compliance criterion:	at the coupling network, figure C.1, the

voltage between C and D1 + D2, disregarding

the dc component, shall not exceed 250 V peak.

1)	User-accessible part or metal foil.

Figure 1: Test circuit for overvoltage surge simulation; common mode, mains powered EUT