ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 120

Date:	2000-01-18

Subject:	TBR3 Test Cases TIF7COMPDEACT1 and TIF8COMPDEACT1

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

X	CTR 33 (Commission Decision 98/521/EC)

For the purposes of the above described applicability, this note specifically contains amendments to:

TBR 3, Amendment A1, December 1997: Attachment requirements for terminal equipment to connect to an ISDN using ISDN basic access.

TBR 33, December 1997: Attachment requirements for packet mode terminal equipment to connect to an ISDN using ISDN basic access.

In consideration of the following:

-	The TTCN test case description of TIF7COMPDEACT1 and TIF8COMPDEACT1 in TBR 3/A1 and TBR 33 states that these tests shall verify that the IUT does not send PH-DI to layer 2, when state F7 or state F8 is left upon the reception of Info 0, and state F7 is entered before Timer T4 has elapsed;

-	The TTCN test case description does not take into account that the tests can only be performed, if state F7 has reached a stable condition before CHK_F7_L2 is entered to check that Layer 2 is still established.

ITAAB advises the following:

The procedure CHK_F7_L2 shall not be called until an INFO3_BASIC message has been received in test case TIF7COMPDEACT1 and TIF8COMPDEACT1.

The corresponding amendments to be performed in TBR 3/A1 are:

TIF7COMPDEACT1 shall be modified as follows:

| Test Case Dynamic Behaviour |
| --- |
| Test Case Name: | TIF7compdeact1 |
| Group: | ISDN1/TI/F7/ |
| Purpose: | To check the value of the timer when leaving state F7 upon the reception of Info 0. |
| Default: | DEF_1 |
| Comments: |
|  | Nr | Label | Behaviour Description | CRef | V | Comments |
| 1 |
| +PRE_F7_COM |
|  | 2 |
| START TCDmin, START TIMER_4 |
|  | 3 | L1 | L!Info_0 | I0 |
| 4 |
| ?TIMEOUT TIMER_4 |
|  | 5 |
| CANCEL TCDmin |
| (F) | (2) |
| 6 |
| L?Info_3 | I3_BASIC |
| 7 |
| GOTO L1 |
|  | 8 |
| L?Info_3 | I3_SFAL |
| 9 |
| GOTO L1 |
|  | 10 |
| L?Info_0 CANCEL TIMER_4 | I0 |
| 11 | L2 | L!Info_0 | I0 |
| 12 |
| ?TIMEOUT TCDmin |
|  | 13 |
| L!Info_n START TAC | I4_BASIC | (P) |
|  | 14 | L3 | ?TIMEOUT TAC |
| (F) | (3) |
| 15 |
| L?Info_0 | I0 |
| 16 |
| L!Info_n | I4_BASIC | (P) |
|  | 17 |
| GOTO L3 |
|  | 18 |
| L?Info_3 | I3_SFL |
| 19 |
| L!Info_n | I4_BASIC | (P) |
|  | 20 |
| GOTO L3 |
|  | 21 |
| L?Info_3 CANCEL TAC | I3_BASIC |
| 2214 |
| +CHK_F7_L2 |
|  | (1) |
| 2315 |
| L?Info_0 | I0 |
| 2416 |
| GOTO L2 |
|  | Detailed Comments: |

(1) To check that the connection is still established.

(2) IUT didn't send Info_0 within 25.250ms.

(3) IUT must send Info 3 within TAC

References to Requirements:

Subclause 9.4.2.5

TIF8COMPDEACT1 shall be modified as follows:

| Test Case Dynamic Behaviour |
| --- |
| Test Case Name: | TIF8compdeact1 |
| Group: | ISDN1/TI/F8/ |
| Purpose: | To check the value of the timer when leaving state F8 upon the reception of Info 0. |
| Default: | DEF_1 |
| Comments: |
|  | Nr | Label | Behaviour Description | CRef | V | Comments |
| 1 |
| +PRE_F7_COM |
|  | 2 |
| START TAC |
|  | 3 | L1 | +SendIX |
|  | 4 |
| ?TIMEOUT TAC |
| (F) | (3) |
| 5 |
| L?Info_3 | I3_BASIC |
| 6 |
| GOTO L1 |
|  | 7 |
| L?Info_0 CANCEL TAC | I0 |
| (1) |
| 8 |
| START TCDmin |
|  | 9 | L2 | L!Info_0 | I0 |
| 10 |
| ?TIMEOUT TCDmin |
|  | 11 |
| L!Info_n START TAC | I4_BASIC | (P) |
|  | 12 | L3 | ?TIMEOUT TAC |
| (F) | (4) |
| 13 |
| L?Info_0 | I0 |
| 14 |
| L!Info_n | I4_BASIC | (P) |
|  | 15 |
| GOTO L3 |
|  | 16 |
| L?Info_3 | I3_SFL |
| 17 |
| L!Info_n | I4_BASIC | (P) |
|  | 18 |
| GOTO L3 |
|  | 19 |
| L?Info_3 CANCEL TAC | I3_BASIC |
| 2012 |
| +CHK_F7_L2 |
|  | (2) |
| 2193 |
| L?Info_0 | I0 |
| 2214 |
| GOTO L2 |
|  | Detailed Comments: |

(1) Loss of frame alignment : IUT shall be in state F8.

(2) To check that the connection is still established.

(3) Not loss of frame alignment within TAC.

(4) IUT must send Info 3 within TAC

References to Requirements:

Subclause 9.4.2.5.

The corresponding amendments to be performed in TBR 33 are:

TIF7COMPDEACT1 shall be modified as follows:

| Test Case Dynamic Behaviour |
| --- |
| Test Case Name: | TIF7compdeact1 |
| Group: | TBR33_L1/ISDN1/TI/F7/ |
| Purpose: | To check the value of the timer when leaving state F7 upon the reception of Info 0. |
| Default: | DEF_1 |
| Nr | Label | Behaviour Description | CRef | V | Comments |
| 1 |
| +PRE_F7_COM |
|  | 2 |
| START TCDmin, START TIMER_4 |
|  | 3 | L1 | L!Info_0 | I0 |
| 4 |
| ?TIMEOUT TIMER_4 |
|  | 5 |
| CANCEL TCDmin |
| (F) | (2) |
| 6 |
| L?Info_3 | I3_BASIC |
| 7 |
| GOTO L1 |
|  | 8 |
| L?Info_3 | I3_SFAL |
| 9 |
| GOTO L1 |
|  | 10 |
| L?Info_0 CANCEL TIMER_4 | I0 |
| 11 | L2 | L!Info_0 | I0 |
| 12 |
| ?TIMEOUT TCDmin |
|  | 13 |
| L!Info_n START TAC | I4_BASIC | (P) |
|  | 14 | L3 | ?TIMEOUT TAC |
| (F) | (3) |
| 15 |
| L?Info_0 | I0 |
| 16 |
| L!Info_n | I4_BASIC | (P) |
|  | 17 |
| GOTO L3 |
|  | 18 |
| L?Info_3 | I3_SFL |
| 19 |
| L!Info_n | I4_BASIC | (P) |
|  | 20 |
| GOTO L3 |
|  | 21 |
| L?Info_3 CANCEL TAC | I3_BASIC |
| 2214 |
| +CHK_F7_L2 |
|  | (1) |
| 2315 |
| L?Info_0 | I0 |
| 2416 |
| GOTO L2 |
|  | Detailed Comments: |

(1) To check that the connection is still established.

(2) IUT didn't send Info_0 within 25.250ms.

(3) IUT must send Info 3 within TAC

References to Requirements:

Subclause 9.4.2.5

TIF8COMPDEACT1 shall be modified as follows:

| Test Case Dynamic Behaviour |
| --- |
| Test Case Name: | TIF8compdeact1 |
| Group: | TBR33_L1/ISDN1/TI/F8/ |
| Purpose: | To check the value of the timer when leaving state F8 upon the reception of Info 0. |
| Default: | DEF_1 |
| Nr | Label | Behaviour Description | CRef | V | Comments |
| 1 |
| +PRE_F7_COM |
|  | 2 |
| START TAC |
|  | 3 | L1 | +SendIX |
|  | 4 |
| ?TIMEOUT TAC |
| (F) | (3) |
| 5 |
| L?Info_3 | I3_BASIC |
| 6 |
| GOTO L1 |
|  | 7 |
| L?Info_0 CANCEL TAC | I0 |
| (1) |
| 8 |
| START TCDmin |
|  | 9 | L2 | L!Info_0 | I0 |
| 10 |
| ?TIMEOUT TCDmin |
|  | 11 |
| L!Info_n START TAC | I4_BASIC | (P) |
|  | 12 | L3 | ?TIMEOUT TAC |
| (F) | (4) |
| 13 |
| L?Info_0 | I0 |
| 14 |
| L!Info_n | I4_BASIC | (P) |
|  | 15 |
| GOTO L3 |
|  | 16 |
| L?Info_3 | I3_SFL |
| 17 |
| L!Info_n | I4_BASIC | (P) |
|  | 18 |
| GOTO L3 |
|  | 19 |
| L?Info_3 CANCEL TAC | I3_BASIC |
| 2012 |
| +CHK_F7_L2 |
|  | (2) |
| 2193 |
| L?Info_0 | I0 |
| 2214 |
| GOTO L2 |
|  | Detailed Comments: |

(1) Loss of frame alignment : IUT shall be in state F8.

(2) To check that the connection is still established.

(3) Not loss of frame alignment within TAC.

(4) IUT must send Info 3 within TAC

References to Requirements:

Subclause 9.4.2.5.