ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 121

Date:	2000-01-18

Subject:	Error in the layer 2 Test Case Selection Expression Definition in TBR 33

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 33 (Commission Decision 98/521/EC)

For the purposes of the above described applicability, this note specifically contains amendments to:

TBR 33, December 1997: Attachment requirements for packet mode terminal equipment to connect to an ISDN using ISDN basic access.

In consideration of the following:

-	The layer 2 Test Case Selection Expression Definitions in TBR 33 define "SAPI0" by an expression, which does not evaluate to a Boolean value, as required by ISO/IEC 9646-3.

ITAAB advises the following:

A Test Suite Parameter of Boolean type shall be defined to describe that SAPI = 0.

This parameter shall be used in the Test Case Selection Expression Definitions.

The corresponding amendments to be performed in TBR 33 are:

The Test Case Selection Expression Definitions shall be modified as follows:

| Test Case Selection Expression Definitions |
| --- |
| Expression Name | Selection Expression | Comments |
| AutomaticTei_PtMP_Stable_S1 | PC_AUTOMAT_TEI AND PC_PTMP_L2 AND PX_IUT_STA_S1 |

| AutomaticTei_PtMP | PC_AUTOMAT_TEI AND PC_PTMP_L2 |
| --- | --- |

| ManagementProcImplemented_StableState4 | PC_PTMP_L2 AND PX_IUT_STA_S4 |
| --- | --- |

| StableState4 | PX_IUT_STA_S4 |
| --- | --- |

| StableState4_TE_established_DL | PX_IUT_STA_S4 AND(DL_TE_DEMAND OR DL_SEMI_PERM_TE) |
| --- | --- |
|  | StableState4_NT_established_DL | PX_IUT_STA_S4 AND(DL_NT_DEMAND OR DL_SEMI_PERM_NT) |
|  | Disc_RX | DISC_RX |
|  | SAPI0 | PX_SAPI_0='000000'B | Only applicable to SAPI 0 data links |
| SAPI0orPTMP | PX_SAPI_0 OR PC_PTMP_L2 | Only applicable to SAPI 0 data links and to SAPI 16 data links in a point-to-multipoint environment |
| Detailed Comments: |

The Test Suite Parameter Declarations shall be modified as follows:

| Test Suite Parameter Declarations |
| --- |
| Parameter Name | Type | PICS/PIXIT Ref | Comments |
| PC_PTMP_L2 | BOOLEAN | A.18.1 | TRUE if the IUT does not use a single point to point data link. |
| PC_AUTOMAT_TEI | BOOLEAN | A.20.1 | TRUE if the IUT supports automatic TEI assignment. |
| PC_VER_TEI_C | BOOLEAN | A.20.9 | TRUE if the IUT supports the Identity verify procedure on error code C. |
| TAC_VAL | INTEGER | A.27.2, A.27.3 | If PC_PTMP_L2 is TRUE the value is 200ms. |
| INCOMING_CALL | BOOLEAN | A.1.3, A.1.7 | TRUE, if the IUT is able to operate with incoming calls |
| OUTGOING_CALL | BOOLEAN | A.1.4, A.1.8 | TRUE, if the IUT is able to operate with outgoing calls |
| DL_NT_DEMAND | BOOLEAN | A.21.4, A.22.4 | TRUE, if the IUT supports data link establishment on NT demand (1) |
| DL_TE_DEMAND | BOOLEAN | A.21.2, A.22.2 | TRUE, if the IUT supports data link establishment on TE demand (1) |
| DL_SEMI_PERM_NT | BOOLEAN | A.21.5, A.22.5 | TRUE, if the IUT supports a semi-permanent data link under NT responsability |
| DL_SEMI_PERM_TE | BOOLEAN | A.21.3, A.22.3 | TRUE, if the IUT supports a semi-permanent data link under TE responsability |
| DISC_RX | BOOLEAN | A.21.7, A.22.7 | True if the IUT is able to receive and take action on a DISC |
| PX_TEI_VALUE | INTEGER | E.5.1 | TEI value for non automatic assignment IUT. In case of automatic assignment IUT the initial value is 64. |
| PX_IUT_STA_S1 | BOOLEAN | E.5.6 | TRUE if the IUT is stable in state 1. |
| PX_IUT_STA_S4 | BOOLEAN | E.5.2 | TRUE if the IUT is stable in state 4 for at least 6 seconds. |
| PX_SAPI | SAPI_TYPE | E.5.3 | SAPI = 0 or SAPI = 16 |
| PX_SAPI_0 | BOOLEAN | E.5.3 | TRUE if PX_SAPI = '000000'B' |
| PX_L3_ACT_CMD | L3_INFO_TYPE | E.6.1 | Activate Message Command from the IUT (2) |
| PX_L3_DUM_MES | L3_INFO_TYPE | E.6.2 | Dummy message to IUT (3) |
| PX_L3_SOL_CMD | L3_INFO_TYPE | E.6.3 | Soliciting Message Command to the IUT (4) |
| PX_L3_SOL_RSP | L3_INFO_TYPE | E.6.4 | Soliciting Message Response from the IUT (5) |
| Detailed Comments: |

(1)   At least one must be TRUE.

(2)   Activate Message Command from the IUT. E.g.

SAPI=00 SETUP = '08010105'O  SAPI=16 CALL REQUEST

='10010B08435510210001000000'O

(3)   Dummy message send to the IUT, which cause no L3 response from the IUT. E.g.

SAPI=00  REL_COM = '0801815A08028290'O,  SAPI=16  Clear Confirm

='100117'O

(4)   Soliciting message send to the IUT. E.g.

SAPI=00  REL = '0801014D08028290'O,   SAPI=16  REST_IND

='1000FB0700'O

The IUT is expected  to response with the L3 message PX_L3_SOL_RSP.

(5)   Soliciting message response from the IUT. E.g.

SAPI=00 REL_COM = '0801815A'O, SAPI=16 REST_CON = '1000FF'O