ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 122

Date:	2000-01-18

Subject:	Errors in layer 3 PDU Constraint Declarations in TBR 33 and TBR 34

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 33 (Commission Decision 98/521/EC)

X	CTR 34 (Commission Decision 98/518/EC)

For the purposes of the above described applicability, this note specifically contains amendments to:

TBR 33, December 1997: Attachment requirements for packet mode terminal equipment to connect to an ISDN using ISDN basic access.

TBR 34, December 1997: Attachment requirements for packet mode terminal equipment to connect to an ISDN using ISDN primary rate access.

In consideration of the following:

-	The layer 3 PDU Constraint Declaration for "BASE_2_PAR" in TBR 33 and TBR 34 uses two parameters, but only the PAR2 is numbered;

-	The layer 3 PDU Constraint Declaration for "ANS" in TBR 33 and TBR 34 has two parameters, but uses the derivation path "BASE_NO_PAR", which does not carry any parameters.

ITAAB advises the following:

Both parameters in the PDU Constraint Declaration for "BASE_2_PAR" shall be numbered.

The derivation path in the PDU Constraint Declaration for "ANS" shall be "BASE_2_PAR".

The corresponding amendments to be performed in TBR 33 and TBR 34 are:

The PDU Constraint Declaration for "BASE_2_PAR" shall be modified as follows:

| PDU Constraint Declaration |
| --- |
| Constraint Name: | BASE_2_PAR(PAR1:BITSTRING; PAR2:CHI_T) |
| PDU Type: | B_PDU |
| Derivation Path: |
|  | Comments: |
|  | Field Name | Field Value | Comments |
| PD | '00001000'B |
|  | CR | - |
|  | MT | - |
|  | UE | - |
|  | IE_LIST | - |
|  | SCI | - |
|  | BCAP | - |
|  | CAU | - |
|  | EFAC | - |
|  | CID | - |
|  | CST | - |
|  | CHI | - |
|  | FAC | - |
|  | PI | - |
|  | NSF | - |
|  | NOID | - |
|  | DSP | - |
|  | DSP_1 | - |
|  | DSP_2 | - |
|  | KPF | - |
|  | CODN | - |
|  | CODS | - |
|  | CGPN | - |
|  | CGPS | - |
|  | CDPN | - |
|  | CDPS | - |
|  | TNS | - |
|  | RI | - |
|  | LLC | - |
|  | HLC | - |
|  | Detailed Comments: | The SCI information element could be received anywhere after the MT(Message Type) field. |

The PDU Constraint Declaration for "ANS" shall be modified as follows:

| PDU Constraint Declaration |
| --- |
| Constraint Name: | ANS(PAR1:BITSTRING; PAR2:CHI_T) |
| PDU Type: | B_PDU |
| Derivation Path: | BASE_2NO_PAR. |
| Comments: | Direction: LT <--- IUT |
| Field Name | Field Value | Comments |
| CR | CR1(PAR1) |
|  | MT | ('00000001'B, '00000010'B, '00000111'B) |
|  | EFAC | * |
|  | CHI | PAR2 |
|  | FAC | * |
|  | PI | * |
|  | NOID | * |
|  | Detailed Comments: |

PDU with "don't care" values and parametrized CHI;

This PDU is sent by the IUT as first answer to a SETUP PDU.