ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 124

Date:	2000-01-18

Subject:	Use of Circuit Mode layer 1 test results for CTR 33 and CTR 34 approval respectively

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 33 (Commission Decision 98/521/EC)

X	CTR 34 (Commission Decision 98/518/EC)

In consideration of the following:

-	SAPI 0 or SAPI 16 are layer 2 address field protocol elements;

-	The requirements for the priority mechanism are always fulfilled automatically by terminals using SAPI 0 (priority class 1) or SAPI 16 (priority class 2), because a SAPI 0 message has always higher priority than a SAPI 16 message due to the binary value of SAPI 16 compared with SAPI 0;

-	The detection of the mismatch between the D-channel bit and the Echo-bit by the terminal sending the SAPI 16 message will cause this terminal to stop transmitting. Therefore it is not considered necessary to have tests for SAPIs different from 0;

-	The modifications of TBR 3/A1 and TBR 4/A1 should be also used for TBR 33 and TBR 34 applications;

-	The layer 1 requirements of TBR 33 for On-demand layer 1 and Semi-permanent layer 1 access to the packet handler are a subset of the TBR 3 / TBR 3/A1 requirements;

-	The layer 1 requirements of TBR 34 for On-demand layer 1 access to the packet handler refers to TBR 4;

-	The layer 1 requirements of TBR 34 for Semi-permanent access to the packet handler refers to TBR 13.

ITAAB advises the following:

TBR 3 / TBR 3/A1 layer 1 test results (SAPI 0) can be used for CTR 33 approval of ISDN terminal equipment using On-demand layer 1 or Semi-permanent layer 1 access to the packet handler for transmission of packet data over the D-channel (SAPI 16) or the B-channel (SAPI 0).

TBR 4 / TBR 4/A1 layer 1 test results are applicable for CTR 34 approval of ISDN terminal equipment using On-demand layer 1 access to the packet handler.

TBR 13 layer 1 test results are applicable for CTR 34 approval of ISDN terminal equipment using Semi-permanent layer 1 access to the packet handler.