ITAAB ADVISORY NOTE

TRAC ISDN Type Approval Advisory Board

ITAAB Advisory Note Number: 125

Date:	2000-01-18

Subject:	Correction of test case references

APPLICABILITY

This note is specifically applicable for approval according to:

X	CTR 3 Amendment 1 (Commission Decision 98/515/EC)

X	CTR 33 (Commission Decision 98/521/EC)

X	CTR 34 (Commission Decision 98/518/EC)

For the purposes of the above described applicability, this note specifically contains amendments to:

TBR 3, Amendment A1, December 1997: Attachment requirements for terminal equipment to connect to an ISDN using ISDN basic access.

TBR 33, December 1997: Attachment requirements for packet mode terminal equipment to connect to an ISDN using ISDN basic access.

TBR 34, December 1997: Attachment requirements for packet mode terminal equipment to connect to an ISDN using ISDN primary rate access.

In consideration of the following:

-	Test case TC25013 is part of the TTCN code in TBR 33 but is not referenced in clause 10.

-	Test case TC25013 has been deleted in TBR 3/A1.

-	Test case TC24007 is referenced in subclauses 10.5.4.2 and 10.5.5.2 of TBR 3/A1, TBR 33 and TBR 34 but is not part of the TTCN code in TBR 3/A1, TBR 33 and TBR 34.

ITAAB advises the following:

-	Delete test case TC25013 in the TTCN code of TBR 33, layer 2.

-	Delete the references to test case TC24007 in subclauses 10.5.4.2 and 10.5.5.2 of TBR 3/A1, TBR 33 and TBR 34.